## Slide 1: 5G Broadcast –Technologies, Standards and Productization
September 15 - 18, 2023
IBC 2023
@qualcomm_tech
George Tsirtsis and Thomas Stockhammer
Qualcomm Technologies

## Slide 2
We are driving 5G broadcast adoption for digital media delivery and more…

## Slide 3: Taking a system approach to technology innovations
Making cellular broadcast a reality
Vision
Identifying a problem or need, and establishing system requirements
We envisioned a more efficient way to deliver mass media over cellular networks
Invention
Inventing new technologies and end-to-end system architecture
We pioneered key cellular broadcast technologies for 3G, 4G, and 5G
Proof-of-concept
Delivering end-to-end prototypes and impactful demonstrations
We showcased cellular broadcast technologies at various industry events
Standardization
Leading ecosystem towards new projects and driving new system designs
We led the mobile and broader industries to standardize cellular broadcast
System Trials
Collaborating on field trials that track standards development, preparing for commercialization
We worked with mobile operators, device manufacturer and content providers on trials
Commercialization
Engaging with global ecosystems to deploy new products and services
Successfully productize cellular broadcast in our products
1
3
2
4
5
6
Joint demo at MWC’23

## Slide 4: 5G Broadcast – Future TV+ for everyone
September 15, 2023
IBC 2023
@qualcomm_tech
Dr. Thomas Stockhammer
Senior Director Technical Standards
Qualcomm Technologies

## Slide 5
Presenter
Dr. Thomas Stockhammer
Senior Director, Technical Standards
Qualcomm Europe, Inc., IEEE Fellow
Leading and driving among others
DVB: 5G TF, DVB-I
MPEG: MPEG-I, CMAF and DASH
3GPP: XR over 5G, 5G Video, 5GMS
DASH-IF: Interop WG, Test
ETSI & 5G-MAG: 5G Broadcast and 5GMS
CTA WAVE: CMAF Device PB, Test
Metaverse Standards Forum: Chair, Board
Today’s agenda
# What is 5G Broadcast
# Standards
# Technologies and Trials
# Status of trials and deployments
# Opportunities and Selected Use Cases
# Next Steps

## Slide 6: What is 5G Broadcast? And what not?

## Slide 7: Challenges for Broadcasters: Devices, Formats, Users
Broadcasters
and Content Provider
Internet Cloud/Edge
Cellular WiFi
UHD/8K
Social
3D
Immersive
Personalized
Interactive
Gaming-like
Short & long
Live
On-Demand
User Generated
AI-supported
Location
Global
Secure
Time-shift
…
Quality
Cost
Scalability
UHF

## Slide 8: 5G defines two modes of broadcast communication
Addressing diverse ecosystem, deployment, and use case requirements
5G broadcast
Mixed-mode multicast
Single Frequency Network (SFN) for downlink broadcast only
Dynamic switching between broadcast and unicast, e.g., SC-PTM1
Focus of this presentation
Operator spectrum (IMT)
Integration with unicast network
Efficient delivery of multicast/broadcast traffic (vs unicast)
Reuse of cellular infrastructure (low power).
Broadcast spectrum (e.g. UHF)
No unicast. Downlink – only traffic.
Delivery of linear content (e.g. TV) or IP file delivery
Dedicated broadcast infrastructure (can be high power)

## Slide 9: General technology introduction
“5G broadcast” is a broadcasting standard defined by 3GPP (Release 16 - 2020)
  3GPP is the industry group responsible for defining global cellular tech standards (e.g. 4G / 5G)
  In the last few years 3GPP has expanded to new verticals (e.g. broadcast, automotive, satellite, etc.) hence it should not be regarded as a surprise that a broadcasting tech is coming out of 3GPP
Even though 5G Broadcast has been standardized by 3GPP, it is a broadcasting technology
  I.e. meant to be used by broadcasting operators, in broadcasting spectrum
  No need of supporting a unicast network. 5G Broadcast does not have anything to do with unicast
The main design target & “reason for being” of 5G broadcast is to enable operation of a broadcast network where the receivers are hardware-compatible with cellular modems
  “Hardware compatible” means lower barrier to adoption in mobile devices compared to other broadcasting technologies
    This is because several 5G Broadcast building blocks are already there in a 4G/5G modem, hence the additions are marginal.
    For other technologies, a separate piece of silicon / die area would be required
  To be clear, 5G Broadcast has nothing to do with “cellular operators trying to take over from broadcasters”
5G broadcast and 3GPP

## Slide 10: 5G Broadcast – Core Features for multiple use cases
SIM-less reception with simplified architecture
Receive-Only Mode (ROM) & Free-to-Air (FTA)
Different spectrum options (e.g. UHF, SDL), as well as SFN/MFN
Various deployment possibilities (e.g. MNOs, BNOs)
Using existing infrastructure (HPHT, MPMT and LPLT)
Highly flexible velocities (up to 250 KM/h Vs up to 300 µS)
Can be combined with existing 4G and 5G features (unicast, PWS)

## Slide 11
Significant interests towards 5G broadcast deployment worldwide
2020-22: 5G Media2Go Stuttgart/Heilbronn
2017-20: 5G Today in Bavaria
Germany
2020-22: VISTA Project with O2 Virgin Media
UK
2020: Distribution of free-to-air linear radio and TV using Rel-14 enTV with HPHT in Barcelona
2022 & 2023: MWC demos
Spain
2020-21: Delivery of TV and radio with Rel-14 broadcast trial deployment in Santiago de Tolú
Colombia
2020-23: TV 3.0 project calling for proposals
Brazil
2018-23: TV delivery with Rel-14/16 HPHT in Aosta and Turin
Italy
2020-23: Distribution of TV/Radio with 5G BC Rel-14/16 , with eMBB in Vienna
Austria
2020+: Growing interest in latest broadcast3 technologies
Late 2021: Distribution of live TV using Rel-16 enTV near Seoul
South Korea
1 National Radio and Television Administration 2 Academy of Broadcast and Science commercia potential 3 Prasar Bharti working jointly with IIT Kanpur on Next Generation Broadcast Technology
Malaysia
2020+: Growing interest in 5G BC in addition to ATSC3.0
2023: FCC Approves A Low Power TV Station To Broadcast Over 5G Networks
2023: First 5G Broadcast in the US and first 24/7 5G Broadcast station in the world on WWOO, Boston, MA!
US
Philippines
2019-22: Direct to mobile Live TV/Radio in Manilla
South Africa
2019-20: Live testing of Rel-14 in Johannsburg
2022+: 5G Broadcast under investigation as latest broadcast technology
Russia
2022: Interest towards 5G BC during Mediterranean Games
France
2018-2022: Live testing of 5G BC in Paris
Belgium
2022-24: 5G BC imec.icon project with 2 HPHT sites
Finland
2019-22: TV delivery with Rel-14/16 HPHT in 3 sites
CZ
2020-23: Distribution of TV/Radio in Prague
2019-24: AIB project based on 5G Broadcast under the administration of NRTA1 and ABS2
2023: 5G Broadcast Chengdu pilot project formally kicked off on July 20th
India
Denmark
Tour de France 22 powered by 5GB
Algeria
Greece
Croatia
2021-23: Live TV/Radio with 5G BC Rel-14/16 , with 3MHz in Athens
2022-24: Live 5G BC Rel-14/16
China
2023: Workshop on future of Broadcast
Europe
2023: European broadcasters ink 5G Broadcast MoU

## Slide 12: 5G Broadcast at IBC 2023
Rohde & Schwarz and Qualcomm to demonstrate 5G Broadcast ecosystem readiness at IBC2023
  At IBC2023 Rohde & Schwarz will demonstrate the latest innovative features, including seamless service continuity between broadcast and broadband, and low latency content distribution. Thanks to the software architecture of the TH1 transmitter family, all these and future enhancements can be readily added in the field on-demand.
https://www.nakolos.com/ibc2023/
  XGen Networks (Hall 1.D90)
  5G-MAG (5G MEDIA ACTION GROUP) @ EBU (Hall 10.D21)
  SYES - System Engineering Solutions (Hall 8.F46)
  Media Coding Industry Forum (Hall 8.B45)
  Plisch/RFMondial (Hall 8.C61)
5G-MAG Meetup
IBC Conference
To our best knowledge

## Slide 13: Standardization

## Slide 14
For more information on 5G broadcast standards…
ETSI TS 103 720: Profile of 3GPP specification containing the necessary parts to deploy 5G broadcast
TR 36.976: Overall description of enhanced TV (enTV) for 5G broadcast
Various specifications of 5G PHY supporting broadcast together with unicast in TS 36.211, 36.212, 36.213

## Slide 15: 5G Broadcast Standards Evolution
Rel-14
SCS1.25KHz/ CP=200µs Mobility up to 120 km/h
5G BC worldwide standard
TG6/1 and WP6A
Rel-16
Rooftop Mobility up to 250 km/h
5G BC is an EU standard (ETSI TS 103 720)
Rel-17 Enhanced BW= 6/7/8 MHz for UHF
Enhanced Version of ETSI TS 103 720
AI1.5 WRC23
Rel-18 Requirements for UHF and 6/7/8 MHz, URL Handling
Roadmap towards WRC23
3GPP
3GPP
ITU
ETSI
3GPP
ETSI 5G-MAG
ITU
3GPP
2017
2020
2019
2020
06/22
06/23
2023
09/23
Bug fixes and clarifications from trials & Rel-17
Adding bandwidth information, including 6/7/8 MHz
5G Media Streaming: integrated unicast & broadcast
Consistent codecs and formats
Support of Public Warning System & Emergency Alerts

## Slide 16: Latest Updates
5G Broadcast will evolve with 3GPP pace

## Slide 17: Technologies and Trials

## Slide 18: Proof of concept in 2022:
Objective: confirm feasibility and move ecosystem towards commercial deployments.
Summary of features:
  Reception from broadcast transmitter
  Reception in broadcast UHF spectrum
  Operation without SIM card
  Reuse of cellular hardware (smartphone)

## Slide 19
Spanish public
broadcaster
Streaming
solutions
Tower company
Network & transmitter
Smartphone / chipset

## Slide 20
Bearer Management
IP Multicast Allocation
Packet Routing/Forwarding
BM-SC
MBMS-GW
SGi-mb
SG-mb
M1
SNYC / FLUTE
Diameter
SYNC
Content Provider
Premium Content Synchronization
Multimedia Content Multiplexing
TMGI Allocation
RESTfull API
TSoIP
DASH
HLS
DTLS*
CMAF*
M2
M2AP
Dynamic Radio Resource Management for Broadcast/Multicast
MCE
Dynamic Resources Scheduling & MCS
R&S Internal Interface
Service Announcement
FEC
MPEG DASH
FLUTE
3GP DASH
ROUTE*
SFN
MFN
MBMS Service Area Management
Carrier Aggregation
Carrier Management
Multi-MCH
x-MB
BSCC2.0 – Internal architecture
Tx/eNB
* In development

## Slide 21: Qualcomm devices
QRDs based on Snapdragon 8 Gen 1 initially, now Gen 2 (8450 / 8550).
Modified (non-commercial) changes to enable a subset of 5G-broadcast features.
Meanwhile, Qualcomm supported enabling 5G Broadcast trials on Commercial devices by applying some firmware upgrades  Commercial Research Devices (CRDs)
Additional trial features are expected in next release of QRDs and CRDs.

## Slide 22: APIs – Test and commercial devices
Modem
Application Processor
Applications
Streaming App
File Download App
HLOS
MBMS Client
Streaming Service
File Download Service
Local DASH Server
Service Discovery
File Repair
Reception Reporting
Object Distribution Function
FLUTE
Multimedia System
DASH Client
DRM Agent
IP Stack (with multicast)
eMBMS Service
I-1
I-2
I-4
LTE Modem
I-3
Transparent Service
Group Communication
Packet Distribution Function
FEC
Transparent
IPTV app
Service Discovery
CMAS Client
SIB12 messages
messageIdentifier, serialNumber, dataCodingScheme geographical area coordinates
Depending on alert, action happens

## Slide 23: Android APIs
Download Session
  https://developer.android.com/reference/android/telephony/MbmsDownloadSession
Group Call Session:
  https://developer.android.com/reference/android/telephony/MbmsGroupCallSession
Streaming Session
  https://developer.android.com/reference/android/telephony/MbmsStreamingSession
MBMS API documentation
  https://developer.android.com/reference/android/telephony/mbms/package-summary

## Slide 24: QRD use in initial trials
Modem
Application Processor
Applications
Streaming App
File Download App
HLOS
MBMS Client
Streaming Service
File Download Service
Local DASH Server
Service Discovery
File Repair
Reception Reporting
Object Distribution Function
FLUTE
Multimedia System
DASH Client
DRM Agent
IP Stack (with multicast)
eMBMS Service
I-1
I-2
I-4
LTE Modem
I-3
Transparent Service
Group Communication
Packet Distribution Function
FEC
Transparent
IPTV app
Service Discovery
CMAS Client
SIB12 messages
messageIdentifier, serialNumber, dataCodingScheme geographical area coordinates
Depending on alert, action happens

## Slide 25: Eurovision Song contest
Link
5G Broadcast demoed live in multiple cities

## Slide 26: MWC 23
ORS booth

## Slide 27: Other demos / trials
TowerCast event in Paris
Stuttgart (test drive)
BES expo (Delhi)
CABSAT’22
IMC’22
Rio open ‘23 (BR)
MWC ‘23

## Slide 28: Technology Evolution

## Slide 29: MBMS/LTE eMBMS/5G broadcast History
Building upon a strong 3GPP technology foundation
eMBMS defined for LTE starting in Rel-8/Rel-9, improving coverage and efficiency
eMBMS enhancements in Rel-12 include MOOD and expansion to MCPTT
Enabling terrestrial broadcast and expanding to new services; Meeting 7/10 5G Broadcast requirements in Rel-14
LTE eMBMS/enTV
in 3GPP Rel-14
LTE
LTE-A
Further enhancements5
to fully satisfy 5G
broadcast requirements
5G
Target market focused on
Cellular operators
Target market expanded to
Broadcasters
3GPP Rel-14 (completed)
Enabling terrestrial broadcast and expanding to new services; Meeting all 5G Broadcast requirements in Rel-16
5G broadcast is a “broadcast standard” (same target as DVB or ATSC) based on 3GPP silicon and ecosystem.
3GPP could have taken a radical approach to define a clean slate radio system to meet the broadcasters’ requirements, instead a more pragmatic route was chosen. Experiences from the past with dedicated modems such as MediaFLO or DVB-H, and the need for easy integration into mainstream mobile devices, led to the decision to evolve eMBMS to LTE-based 5G Broadcast instead of any radical new designs.
3GPP Rel-16 (completed)

## Slide 30: 5G Broadcast: the technology
Main technology components
System layer enhancements
Radio access enhancements
Rel-14
enTV1
Rel-16
enTV
is 5G Broadcast
Broadcast
Broadcast
Unicast control
xMB
Content provider
    Receive only mode
    Delivery of free-to-air content to devices without SIM/service subscription
    Unified protocol stack
    CMAF packaging – compatible with unicast and broadcast stacks
    Standardized network APIs
    Content providers can deliver media over 5G Broadcast with a unified framework
    Shared broadcast
    Multiple operators can serve users on a common broadcast carrier
    Longer range & high mobility
    New numerology with 100/200/300us CP2 for up2 100km radius and 250km/h speed
    More broadcast capacity
    Supports dedicated broadcast network with 100% eMBMS carrier allocation
    More deployment flexibility
    Single network for mobile and fixed devices with enhanced support for rooftop reception
    Better efficiency
    New subframe design reduces overhead in dedicated broadcast transmissions

## Slide 31: RAN: MBMS  5G Broadcast Evolution
Mixed unicast/MBMS carrier
15 kHz numerology
Extended CP of 16.7us
Multi-cell transmission only (MBSFN)
Up to 60% of subframes for MBSFN transmission
Single-cell transmission (SC-PTM)
Transmission on PDSCH with new group identities
Non-synchronized transmitters
Longer cyclic prefixes for support of larger ISD
Up to 100% of subframes for MBSFN transmission on a dedicated carrier
Subframes fully dedicated to MBSFN transmission
Targeting rooftop and car-mounted antennas, handheld receivers
Release 9
Release 13
Release 14
> 15 km
“Operator controlled” MBMS
“Broadcaster controlled” MBMS
New numerologies to target rooftop reception with up to 125 km ISD
High mobility reception: fixed, portable and mobile receivers up to 250 km/h
Enhancements to CAS—increased PDCCH agg. Level, PBCH repetition, CFI in MIB
Release 16
6/7/8 MHz channel bandwidth to support common global channel bandwidth for broadcast systems
Introduction of UHF Band 108 to address RF transmitter and receiver requirements
Release 17/18

## Slide 32: Performance Comparison 5G Broadcast vs. an unconstrained system

## Slide 33: Summary of potentially identified differences
Channel Coding and modulation schemes
Time Interleaving
Frequency Interleaving
Antenna Configuration
Receiver requirements

## Slide 34: Simulations
Aligned with IEEE papers [1][2]
Parameter | Unconstrained System (i.e., ATSC 3.0) | 5G Broadcast
System Bandwidth (MHz) | 8 | 8
Useful BW (MHz) | 7.78 | 7.2
FFT length | 8192 | 12288
Subcarrier Spacing (kHz) | 1.125 | 1.25
Sampling rate (MHz) | 9.216 | 15.36
OFDM symbol duration (us) | 889 | 800
CP duration (us) | 222.2 | 200
Channel estimation | LMMSE over 48 consecutive pilots per RB bundle | 
Number of Rx antennas | 1 (unless specified otherwise) | 
Pilot pattern stagger | (Fd3, Td2) | (Fd3, Td2)
Time (T) and/or Frequency (F) interleaver | F interleaver: ON T interleaver: 400 ms extended CTI | None
Modulation | QPSK (Svc 1) NUC 16-QAM (Svc 2) | QPSK (Svc 1) 16-QAM (Svc 2)
Coding | 8/15 LDPC 64800 + BCH | 8/15 Turbo
TBS | 34368 | 5544 (Svc 1) 10296 (Svc 2)
Throughput | ~5 Mbps for Svc1 and ~10 Mbps for Svc 2 | 
Parameter | Unconstrained System (i.e., ATSC 3.0) | 5G Broadcast
System Bandwidth (MHz) | 8 | 8
Useful BW (MHz) | 7.78 | 7.2
FFT length | 8192 | 12288
Subcarrier Spacing (kHz) | 1.125 | 1.25
Sampling rate (MHz) | 9.216 | 15.36
OFDM symbol duration (us) | 889 | 800
CP duration (us) | 222.2 | 200
Channel estimation | LMMSE over 48 consecutive pilots per RB bundle | 
Number of Rx antennas | 1 (unless specified otherwise) | 
Pilot pattern stagger | (Fd3, Td2) | (Fd3, Td2)
Time (T) and/or Frequency (F) interleaver | F interleaver: ON T interleaver: 400 ms extended CTI | None
Modulation | QPSK (Svc 1) NUC 16-QAM (Svc 2) | QPSK (Svc 1) 16-QAM (Svc 2)
Coding | 8/15 LDPC 64800 + BCH | 
TBS | 34368 | 5544 (Svc 1) 10296 (Svc 2)
Throughput | ~5 Mbps for Svc1 and ~10 Mbps for Svc 2 | 
[1] S. -I. Park et al., "Performance Analysis of All Modulation and Code Combinations in ATSC 3.0 Physical Layer Protocol," in IEEE Trans. on Broadcasting, vol. 65, no. 2, pp. 197-210, June 2019, doi: 10.1109/TBC.2018.2871372
[2] S. -K. Ahn et al., "Evaluation of ATSC 3.0 and 3GPP Rel-17 5G Broadcasting Systems for Mobile Handheld Applications," in IEEE Trans. on Broadcasting, doi: 10.1109/TBC.2022.3222988.

## Slide 35: Achievable spectral efficiency&capacity (LTE, NR, ATSC)
1 Receive antenna, AWGN
All technologies close to Shannon limit (< 2dB), NR and LTE (5GB) offer similar performance
Gains of an unconstrained system are < 1dB, and get smaller with adding constraints (64k -> 16k)
Channel Code and BICM 0.5 – 1dB

## Slide 36: Frequency & Time Interleaver (1)
Analyzing the performance difference between ATSC 3.0 and 5G Broadcast over a Rician fading channel (RC20 channel from [1]) for static and 3 km/h
For static and 3 km/h, additional gain compared to AWGN (BICM and Code), is the Frequency Interleaver with around 0.5dB.
No gains for Time Interleaver with a reasonably powerful LoS component
Performance over multipath channels with line-of-sight (LoS) paths, single receive antenna
Frequency Interleaver 0.5 dB

## Slide 37: Frequency & Time Interleaver (2)
Analyzing the performance difference between ATSC 3.0 and 5G Broadcast over a NLoS RL20 channel from [1]
ATSC 3.0 offers additional performance benefits, with additional 0.5 dB (on top of the 1.4 dB gap)
Gain from using a frequency interleaver (in a static setting) remains relatively small.
Larger gain for ATSC 3.0 in Svc2 since at very high data rate, as the 5G Broadcast standard requires two codeblocks instead of one
Non-line-of-sight multipath channels, single receive antenna
Time Interleaver for static NLOS 0.5-1 dB

## Slide 38: Receive Antennas for NLoS
2 Rx antennas are a basic feature in cellular modems
Harness the spatial orders of diversity in a mobile environment, and result in a performance gap of 2 dB for 5G Broadcast, when compared against ATSC 3.0.
In low mobility, the time interleaver from ATSC provides additional gains of around 1dB
fading NLoS channel, for a pedestrian UE (with a mobility of 3 kmph) in an urban environment [2]
Time Interleaver for 3km/h NLOS 1 dB

## Slide 39: Some Fundamentals of Cellular Modems
3GPP technologies are primarily designed for exploiting frequent and rapid feedback on the current channel state at each receiver and then optimize the delivery exploiting time and frequency scheduling, adaptive coding and modulation, interference management, power allocation, spatial multiplexing using multiple antennas and other functionalities.
Hence, cellular modem hardware is built to process "one Transport Block in one slot", as a design principle to adapt and react to the above feedback.
Hybrid ARQ is designed to provide additional redundancy for one transport block within another single slot in order to react to non-decodable transport blocks
Any departure from the above design has significant impact on receiver implementation
  Cost of collecting LLRs for multiple transport blocks requires a large increase of on-chip memory
  A cellular modem only stores LLRs for a single transport block in the on-chip memory
  Huge change to the hardware implementation due to the scheduling of writing/reading to/from memory
  Area size is costly, moving data off and on chip is heavily impacting power consumption and and and  infeasible
For mobility and NLOS situations, the exploitation of time and frequency diversity is very essential

## Slide 40: Interleaving – Facts, Challenges and Opportunities
MBMS uses Application Layer FEC and Unicast Repair to address time diversity.
  Application Layer FEC works very well for the purpose of file casting with spreading over a long-time frame
    M. Luby, T. Gasiba, T. Stockhammer and M. Watson, "Reliable Multimedia Download Delivery in Cellular Broadcast Networks," in IEEE Transactions on Broadcasting, vol. 53, no. 1, pp. 235-246, March 2007, doi: 10.1109/TBC.2007.891703
  Application Layer FEC has its limits when it comes to below 1 second latencies (see 3GPP TR 26.881)
    It is recommended for that
      For low-delay applications, with latencies of at most 1 second, should be supported by well-dimensioned physical layer FEC
      for latencies in the range of a few seconds or more the technology in TS26.346 for AL-FEC is applicable as it has been chosen by 3GPP. The FEC framework was designed for latencies in the range of several seconds and therefore applies also to those cases.
  Application Layer FEC and Unicast Repair is obviously available in 5G Broadcast and can be exploited.
What about physical layer interleaving in 3GPP Systems?
  Harnessing time diversity for 5G Broadcast was first proposed in 3GPP by EBU/IRT/BBC (R1-1911355), where it was pointed out that physical-layer time interleaving provides performance benefits - especially for high-mobility use cases.
  However, the solution proposed in R1-1911355 would require anywhere between a x to x increase in the LLR buffer memory of the receiver.
  Due to the design principle "mixing multiple Transport Blocks into a single slot" it was considered infeasible
Can we create a modem-friendly time and frequency interleaving?
How to handle time and frequency diversity exploitation in case of the absence of a feedback channel

## Slide 41: Time Interleaving proposal: 3GPP modem-friendly designs
Objective: Design that provides time-diversity without increasing the LLR buffer memory at the receiver.
Basic Approach: Reuse of the 3GPP building block behind HARQ retransmissions and combining, which allows to spread the coded bits of a transport block (TB) across multiple non-consecutive slots/subframes.
Details:
  TB size is scaled by —the number of redundancy versions (RVs) used for each TB.
  The “HARQ memory” is used to store the LLRs corresponding to each RV and decode after all RVs for a TB have been received.
  Each RV spans a single slot/subframe, and each TB is transmitted over occasions, with separation of slots between each transmission.
Following two HARQ techniques at the receiver are re-used to build the time interleaver
  At a given (TTI), the modem is only required to process reception from a single TB. The ordering of coded bits within one TTI is the same as in current cellular systems.
  The already existing “HARQ-process handling” framework is re-used.
Interleaved transmission of “HARQ redundancy versions” of (scaled) transport blocks across slots/subframes.

## Slide 42: Time Interleaving proposals: modem-friendly designs
…
…
…
…
…
…
Parts of TBs spread across slots
Parts of TBs spread across slots
Original TBS
Scale original TBS by a factor of
Transmit “parts” (e.g., RVs) of the -scaled TB over “non-contiguous” slots
Example circular buffer (for a codeblock of a scaled TB) for incremental redundancy using “legacy” RV starting pointers
(Potentially) punctured systematic bits
Example circular buffer (for a codeblock of a scaled TB) for incremental redundancy using “modified” RV starting pointers
Updated design
Rate > 1 for "initial" transmission permitted
“modified” RVs ensure that the coded bits for start right after those for , and we are not restricted to 4 RVs
To spread out the systematic bits of each codeblock (carried by the lower-indexed RVs) within the TB as far apart in time as possible,
for , we use
for

## Slide 43: Frequency interleaving
With the scaled TB sizes, the number of codeblocks in a TB increases, thereby requiring frequency interleaving of the OFDM symbols.
The main principles behind the proposed frequency interleaver are:
      The tones corresponding to the codeblocks are written row-wise.
      Pseudo-random shifts are applied to the columns.
      Elements are read column-wise.
For a detailed standards’ focused description on these aspects, see R1-1912692

## Slide 44: Evolution of SNR requirements with interleaving
 | Baseline 5GB | 4 RV Time Intlv. only | 4 RV T/F Intlv. | 8 RV T/F Intlv.
SNR for 3 kmph | 17.7 dB | 17.5 dB (0.2 dB) | 16.3 dB (1.4 dB) | 15.6 dB (2.1 dB)
SNR for 40 kmph | 17.7 dB | 14.6 dB (3.1 dB) | 13.8 dB (3.9 dB) | 12.7 dB (5 dB)
SNR for 120 kmph | 18.3 dB | 14.7 dB (3.6 dB) | 14.2 dB (4.1 dB) | 12.9 dB (5.4 dB)
Performance comparison between
baseline 5G Broadcast
4 RV-based time interleaver with a depth of 128 ms: each TB samples the channel uniformly, every 32 ms.
4 RV-based time and Frequency interleaving with depth of 686 tones for maximal frequency spreading
8 RV-based time interleaver, with depth of 256 ms and frequency interleaving depth set to 383 tones.
Required SNRs for BLER, and gains (in parentheses) with interleavers
1 Receive Antennas, NLoS India-Urban channel [1]

## Slide 45: Impact of Modem-Friendly Time and Frequency Interleaving
2 Receive Antennas, NLoS India-Urban channel
SNR required for 0.1% BLER using 8RV-based intlv. + 2Rx
  2Rx + RV-based T/F intlv at 256ms time interleaving yields dB loss w.r.t. 2Rx-based ATSC 3.0 at 400ms time interleaving
Speed | ATSC 3.0 + 2Rx | Baseline 5G Broadcast + 2Rx | 5G Broadcast 8RV + 2Rx
3 km/h | 8.7 dB | 10.7 (-2 dB) | 8.9 dB (-0.2 dB)
40 km/h | 6.6 dB | 11 (-4.4 dB) | 7.1 dB (-0.5 dB)
120 km/h | 6.2 dB | 11.4 (-5.2 dB) | 7 dB (-0.8 dB)
0.8 dB
0.5 dB
0.2 dB

## Slide 46: Time-frequency interleaver status in 3GPP
Time-frequency interleaving for 5G Broadcast was discussed in Rel-16 and was shown to provide large gains in time-varying channels.
The following was captured in the RAN1#99
Chairman’s notes:
Figure (from R1-1913439) showing a 3+dB gain or a ~30% throughput gain from interleaving (at 0.1% BLER target)
R1-1913439 On time and frequency interleaving for terrestrial broadcast EBU, BBC, IRT, NHK, ABS, DISH, Eutelsat, Shanghai Jiao Tong University, Fraunhofer HHI, Fraunhofer IIS, Enensys, Qualcomm, Rohde&Schwarz, Nokia, Nokia Shanghai Bell, ATEME, Nomor Research, Sony
Time and frequency interleaving for terrestrial broadcast was discussed even though it was not explicitly in the scope of the WID. However, consensus was not reached. It can be considered for a later release.

## Slide 47: Summary and Conclusions
5G BROADCAST RECEIVERS: OPTIMIZING PERFORMANCE UNDER IMPLEMENTATION CONSTRAINTS
Broadcast networks and usage of configurations needs to be done for worst-case scenario.
For example, gains achieved in the 120 kmph scenario may not relevant, if such a planning would fail to serve a large number of receivers moving at lower speeds.
In this case, comparison between 5G broadcast and ATSC3.0 is provided for NLOS for different speeds and configurations
The main design target & “reason for being” of 5G broadcast is to enable operation of a broadcast network where the receivers are hardware-compatible with cellular modems
  “Hardware compatible” means lower barrier to adoption in mobile devices compared to other broadcasting technologies
    Several 5G Broadcast building blocks are already there in a 4G/5G modem, hence the additions are marginal.
    For other technologies, a separate piece of silicon / die area would be required
In comparison with unconstrained broadcast designs, 5G Broadcast Rel-18 is only marginally worse and there are expectations to address remaining gaps in Rel-19 without compromising the design goals
5G Broadcast is a transport and is successfully combined with unicast service layers – seamless unicast fallback has been successfully demonstrated
SNR for | ATSC 3.0 + 1Rx | ATSC 3.0 + 2Rx | 5G + 2Rx | 5G + 2Rx + TFI
3 kmph | 14.4 dB | 8.7 dB | 10.7 dB | 8.9 dB
40 kmph | 11.2 dB | 6.6 dB | 10.9 dB | 7.3 dB
120 kmph | 10.8 dB | 6.2 dB | 11.4 dB | 7 dB
Worst case | 14.4 dB | 8.7 dB | 11.4 dB | 8.9 dB

## Slide 48: Support the 5G Broadcast Community in 3GPP RAN Rel-19 Planning
For Rel-19, we propose to have a small work item on necessary enhancements for 5G Broadcast (5GB) that are essential for its deployment.
The scope of the proposed enhancements is limited to coexistence with other broadcast systems (mainly ATSC 3.0) due to regulatory constraints, and standardizing one mechanism already discussed in Rel-16 (time-frequency interleavers).
The main proposals are:
  Proposal 1: Standardize “CAS muting” for 5G Broadcast, i.e., the CAS can be dropped with some pattern that is known to the UE.
  Proposal 2: Standardize time-frequency interleavers for 5G Broadcast, taking as baseline the mechanism in R1-1913439.
Come to RAN#102 to Edinburgh and co-sign the initial proposal from Qualcomm and 5G-MAG input

## Slide 49: Opportunities and Selected Use Cases

## Slide 50: Selected use cases
Enhanced broadcast use cases with 5G broadcast
One-way communication directly to handsets
More cost efficient than unicast (RAN and CDN)
Live sports, special events, general programming
Key for massive events (e.g. World Cup)
Linear TV and Radio
Combine linear video with interactivity.
Linear content from broadcaster, unicast using mobile network.
Comments, ratings, e-commerce, advertising
Interactive media
Emergency notifications to smartphones from broadcast infrastructure.
Possibility of sending text-only notifications and multimedia content
Emergency messages
Software / firmware upgrades.
Download and storage of popular content:
  TV shows
  “Viral” videos in social media.
General file download

## Slide 51: Emergency alerts
5G broadcast inherits from 5G the public warning system capabilities.
The Cell Broadcast Service (CBS) does not require authentication with a PLMN. Hence, a ROM network is inherently compatible with CBS (see 3GPP TS 23 041).
CMAS (commercial mobile alert system) is available in current commercial devices.
  Devices monitor periodically a low-duty cycle paging channel (low power)
  CMAS over 5G broadcast has been demonstrated with R&S infrastructure
Additional capabilities of CMAS:
  Geofencing (send notification to users within a given area)
  Possibility of sending URL linking to emergency media

## Slide 52: Use cases for emergency notifications
Emergency Service Provider
Emergency Media Service
Emergency Alerts
Emergency Media Service
Emergency Alerts
Broadcast Service Provider
Broadcast Media Service
Broadcast Media Service
Possibility of sending an emergency message directly to handsets
UE is consuming 5G broadcast media service
cellular network is damaged due to disaster (see Germany 2021).
UE is out of cellular coverage
Device does not support an cellular reception
5G broadcast viewed as complementary “resiliency layer” in case of disaster.
URL
Emergency media can be accessed by means of a URL in the CMAS message (which supports text-only)
Details in ETSI TS 103 720

## Slide 53: Emergency message demo with ABS
Self-contained emergency system (text + multimedia) without need of unicast.

## Slide 54: How is the QRD MBMS Layer used?
Modem
Application Processor
Applications
Streaming App
File Download App
HLOS
MBMS Client
Streaming Service
File Download Service
Local DASH Server
Service Discovery
File Repair
Reception Reporting
Object Distribution Function
FLUTE
Multimedia System
DASH Client
DRM Agent
IP Stack (with multicast)
eMBMS Service
I-1
I-2
I-4
LTE Modem
I-3
Transparent Service
Group Communication
Packet Distribution Function
FEC
Transparent
IPTV app
Service Discovery
CMAS Client
SIB12 messages
messageIdentifier, serialNumber, dataCodingScheme geographical area coordinates
Depending on alert, action happens
WiFi Modem

## Slide 55: Coexistence of ATSC 3.0 & 5G Broadcast
5G Broadcast can be deployed by broadcasters in the exact same way as ATSC, and it greatly lowers the barrier to adoption in mobile devices since it is “only” an incremental feature to the 4G/5G modem
  Native broadcasting technologies like ATSC or DVB were never successfully incorporated in mobile devices at scale because their inclusion requires a separate piece of silicon (similar to, say, WiFi or GPS) and the ecosystem never took off
We could make use of the “reserved” frames of ATSC 3.0 to “superimpose” 5G Broadcast, thus achieving coexistence on the same channel
  An alternative would be for ATSC 3.0 and 5G Broadcast to coexist on two different frequencies, i.e. one MUX for each
The same broadcaster could thus deploy & operate both technologies at the same time
  ATSC 3.0 for fixed devices
  5G Broadcast for mobile devices
Documented in ATSC TG3-11
Rel-19 candidate work for 3GPP
ATSC 3.0 & 5G Broadcast can coexist: it does not have to be a either/or
Work Item in ATSC und 3GPP under preparation

## Slide 56: DVB-I via 5G Broadcast
Using MBMS/5G Broadcast Reference Points and APIs
Different options are considered
  Using file download services for carouselling metadata
  Using segment streaming for DVB-DASH
  Using transparent mode for DVB-I multicast distribution
Combinations with unicast, hybrid services also under development
See details in ETSI TR 103 972
Expected to be supported by reference tools
Joint DVB/5G-MAG task force

## Slide 57: Hybrid Unicast Broadcast
Content Provider may leverage 5G Unicast systems, 5G Broadcast systems, and 5G devices to build efficient and innovative applications
Supported by well defined network and client-side APIs
Examples:
  Hybrid Services
  Universal Coverage
  Broadcast on Demand
Integrated into 3GPP 5G specs, ETSI TS 103 720 and TR 103 972 (DVB over 5G)
Architectures, Collaboration Models and Use Cases
5G Broadcast Operator
Content Provider
5G MNO

## Slide 59: How is the QRD MBMS Layer used?
Modem
Application Processor
WiFi Modem
IP Unicast
HLOS
MBMS Client
IP Stack (with multicast)
eMBMS Service
LTE Modem
Group Communication
Group Communication

## Slide 60: 5G-MAG Reference Tools?
Current list of official contributors
Find information at developer.5g-mag.com
  Developer Space
  https://developer.5g-mag.com

## Slide 61
  Developer Space
  developer.5g-mag.com
www.youtube.com/
@5gmag
Discussions at the
5G-MAG Forum
github.com/5G-MAG/
Getting-Started/wiki
5G-MAG Reference Tools
Open-source Reference Tools for Multimedia Applications
developer.5g-mag.com
Need a full update on 5G-MAG REFERENCE TOOLS?
Visit: 5G-MAG Reference Tools XCHANGE + DEMOS
DEVELOPER XCHANGES: www.5g-mag.com/tutorials
https://www.youtube.com/watch?v=4RZ_cON5bfo

## Slide 62: 5G-MAG Reference Tools
Implementation in the 5G-MAG REFERENCE TOOLS
Find information about 5G-MAG Work Items at hub.5g-mag.com
DEV
Which Workgroups to join?
MORE SLIDES

## Slide 63: 5G-MAG Reference Tools
Implementation in the 5G-MAG REFERENCE TOOLS
Find information about 5G-MAG Work Items at hub.5g-mag.com
DEV
Which Workgroups to join?
MORE SLIDES

## Slide 64: Demos 2023
FOKUS Media Web Symposium
BBC’s 5G MEDIA Workshop
IEEE BMSB 2023

## Slide 65: Summary & Next Steps
Join the community of open standards, innovation and development
5G is a platform for Broadcasters and Content Providers with features including 5G broadcast, Public Warning and many others
3GPP Standards are global and address billions of devices – from smart phones to many more verticals (automotive, IOT, etc.)
Qualcomm contributes, supports and drives open systems through technologies, standards and reference tools

## Slide 67: Background – Coexistence with other broadcast systems
Due to FCC regulation, US broadcasters shall broadcast one free to air stream using ATSC 3.0 in their allocated spectrum (6 MHz carrier).
Outside of this mandatory stream, the rest of the radio resources can be used for any other purpose using any technology (“ancillary services”)
Therefore, to enable 5G Broadcast deployments in the US under current regulation, both technologies may need to coexist in the same 6 MHz carrier.
  The only feasible coexistence is by TDM
ATSC 3.0
5GB
ATSC 3.0
5GB
Transmitter
ATSC receiver
ATSC 3.0
Blank
ATSC 3.0
Blank
Blank
5GB
Blank
5GB
5GB receiver
6MHz carrier

## Slide 68: Background - Mechanisms for coexistence
Both ATSC and 5GB implement basic mechanisms for coexistence / forward compatibility:
5G Broadcast:
  In 5GB, the only signal that is “always on” is the CAS, with a periodicity of 40ms.
  The MBSFN subframes in between CAS can be signaled to belong to a given MBSFN area.
  For subframes not belonging to any MBSFN area (or not scheduled), the UE cannot assume presence of any signal.
  This mechanism was used in Rel-16 to introduce new numerologies, and in Rel-17 to introduce new PMCH bandwidth in a backward compatible way.
ATSC 3.0:
  In ATSC 3.0, forward compatibility is created by combining the “bootstrap” signal and limited frame length.
  The bootstrap can be seen as a sync signal (with a common structure) that can be used for future technologies
    A common bootstrap signal allows for the receiver to potentially search for two technologies with the same searcher hardware.
  The preamble after the bootstrap signal indicates the length of the frame. The bootstrap signals the minimum gap to the next bootstrap (min_time_to_next)
CAS |  | CAS |  | CAS |  | CAS | 
B | P | Subframes |  | B | P | Subframes | 
Variable
39ms
B: Bootstrap. P: Preamble

## Slide 69: Limitations to coexistence
Unfortunately, the approaches followed in both technologies are not compatible:
  In 5GB, the CAS (1ms) is periodic with a 40ms periodicity.
  In ATSC, there are no periodic signals, but every ATSC frame has a duration of at least 50ms.
CAS |  | CAS |  | CAS |  | CAS | 
1ms
39ms
5GB
ATSC frame
>=50ms
Cannot fit ATSC frame within the 39 “blank” milliseconds of 5GB
ATSC 3.0
  “Bootstrap”: 2 ms with configurable periodicity between 50 ms and 5 s
  “Preamble”: 1.2 ms (assuming a single preamble OFDM symbol with shortest numerology)
  “Data subframes”: 20 ms/subframe
  “Frame”: 50ms
ATSC 3.0 frame structure (from A/322)

## Slide 70: Proposal to enable clean coexistence
Proposal 1: Standardize “CAS muting”, i.e., the CAS can be dropped with some pattern that is known to the UE.
  The muting of other signals (e.g. MCCH) would follow “CAS” muting.
  MTCH will be scheduled during the ON periods.
ATSC frame
CAS | Data | CAS |  | CAS |  | CAS |  | CAS | Data
Muted CAS periods