## Slide 1: 5G Broadcast Receivers: Optimizing Performance under Implementation Constraints
September 15, 2023
IBC 2023
@qualcomm_tech
Dr. Thomas Stockhammer
Senior Director Technical Standards
Qualcomm Technologies

## Slide 3
Presenter
Dr. Thomas Stockhammer
Senior Director, Technical Standards
Qualcomm Europe, Inc., IEEE Fellow
Leading and driving among others
DVB: 5G TF, DVB-I
MPEG: MPEG-I, CMAF and DASH
3GPP: XR over 5G, 5G Video, 5GMS
DASH-IF: Interop WG, Test
ETSI & 5G-MAG: 5G Broadcast and 5GMS
CTA WAVE: CMAF Device PB, Test
Metaverse Standards Forum: Chair, Board
Today’s agenda
# What is 5G Broadcast
# Standards
# Technology Evolution
# Performance Comparison
# Conclusions
# Invitation to collaborate

## Slide 4: What is 5G Broadcast? And what not?

## Slide 5: Challenges for Broadcasters: Devices, Formats, Users
Broadcasters
and Content Provider
Internet Cloud/Edge
Cellular WiFi
UHD/8K
Social
3D
Immersive
Personalized
Interactive
Gaming-like
Short & long
Live
On-Demand
User Generated
AI-supported
Location
Global
Secure
Time-shift
…
Quality
Cost
Scalability
UHF

## Slide 6: 5G defines two modes of broadcast communication
Addressing diverse ecosystem, deployment, and use case requirements
5G broadcast
Mixed-mode multicast
Single Frequency Network (SFN) for downlink broadcast only
Dynamic switching between broadcast and unicast, e.g., SC-PTM1
Focus of this presentation
Operator spectrum (IMT)
Integration with unicast network
Efficient delivery of multicast/broadcast traffic (vs unicast)
Reuse of cellular infrastructure (low power).
Broadcast spectrum (e.g. UHF)
No unicast. Downlink – only traffic.
Delivery of linear content (e.g. TV) or IP file delivery
Dedicated broadcast infrastructure (can be high power)

## Slide 7: General technology introduction
“5G broadcast” is a broadcasting standard defined by 3GPP (Release 16 - 2020)
  3GPP is the industry group responsible for defining global cellular tech standards (e.g. 4G / 5G)
  In the last few years 3GPP has expanded to new verticals (e.g. broadcast, automotive, satellite, etc.) hence it should not be regarded as a surprise that a broadcasting tech is coming out of 3GPP
Even though 5G Broadcast has been standardized by 3GPP, it is a broadcasting technology
  I.e. meant to be used by broadcasting operators, in broadcasting spectrum
  No need of supporting a unicast network. 5G Broadcast does not have anything to do with unicast
The main design target & “reason for being” of 5G broadcast is to enable operation of a broadcast network where the receivers are hardware-compatible with cellular modems
  “Hardware compatible” means lower barrier to adoption in mobile devices compared to other broadcasting technologies
    This is because several 5G Broadcast building blocks are already there in a 4G/5G modem, hence the additions are marginal.
    For other technologies, a separate piece of silicon / die area would be required
  To be clear, 5G Broadcast has nothing to do with “cellular operators trying to take over from broadcasters”
5G broadcast and 3GPP

## Slide 8: 5G Broadcast – Core Features for multiple use cases
SIM-less reception with simplified architecture
Receive-Only Mode (ROM) & Free-to-Air (FTA)
Different spectrum options (e.g. UHF, SDL), as well as SFN/MFN
Various deployment possibilities (e.g. MNOs, BNOs)
Using existing infrastructure (HPHT, MPMT and LPLT)
Highly flexible velocities (up to 250 KM/h Vs up to 300 µS)
Can be combined with existing 4G and 5G features (unicast, PWS)

## Slide 9
Significant interests towards 5G broadcast deployment worldwide
2020-22: 5G Media2Go Stuttgart/Heilbronn
2017-20: 5G Today in Bavaria
Germany
2020-22: VISTA Project with O2 Virgin Media
UK
2020: Distribution of free-to-air linear radio and TV using Rel-14 enTV with HPHT in Barcelona
2022 & 2023: MWC demos
Spain
2020-21: Delivery of TV and radio with Rel-14 broadcast trial deployment in Santiago de Tolú
Colombia
2020-23: TV 3.0 project calling for proposals
Brazil
2018-23: TV delivery with Rel-14/16 HPHT in Aosta and Turin
Italy
2020-23: Distribution of TV/Radio with 5G BC Rel-14/16 , with eMBB in Vienna
Austria
2020+: Growing interest in latest broadcast3 technologies
Late 2021: Distribution of live TV using Rel-16 enTV near Seoul
South Korea
1 National Radio and Television Administration 2 Academy of Broadcast and Science commercia potential 3 Prasar Bharti working jointly with IIT Kanpur on Next Generation Broadcast Technology
Malaysia
2020+: Growing interest in 5G BC in addition to ATSC3.0
2023: FCC Approves A Low Power TV Station To Broadcast Over 5G Networks
2023: First 5G Broadcast in the US and first 24/7 5G Broadcast station in the world on WWOO, Boston, MA!
US
Philippines
2019-22: Direct to mobile Live TV/Radio in Manilla
South Africa
2019-20: Live testing of Rel-14 in Johannsburg
2022+: 5G Broadcast under investigation as latest broadcast technology
Russia
2022: Interest towards 5G BC during Mediterranean Games
France
2018-2022: Live testing of 5G BC in Paris
Belgium
2022-24: 5G BC imec.icon project with 2 HPHT sites
Finland
2019-22: TV delivery with Rel-14/16 HPHT in 3 sites
CZ
2020-23: Distribution of TV/Radio in Prague
2019-24: AIB project based on 5G Broadcast under the administration of NRTA1 and ABS2
2023: 5G Broadcast Chengdu pilot project formally kicked off on July 20th
India
Denmark
Tour de France 22 powered by 5GB
Algeria
Greece
Croatia
2021-23: Live TV/Radio with 5G BC Rel-14/16 , with 3MHz in Athens
2022-24: Live 5G BC Rel-14/16
China
2023: Workshop on future of Broadcast
Europe
2023: European broadcasters ink 5G Broadcast MoU

## Slide 10: 5G Broadcast at IBC 2023
Rohde & Schwarz and Qualcomm to demonstrate 5G Broadcast ecosystem readiness at IBC2023
  At IBC2023 Rohde & Schwarz will demonstrate the latest innovative features, including seamless service continuity between broadcast and broadband, and low latency content distribution. Thanks to the software architecture of the TH1 transmitter family, all these and future enhancements can be readily added in the field on-demand.
https://www.nakolos.com/ibc2023/
  XGen Networks (Hall 1.D90)
  5G-MAG (5G MEDIA ACTION GROUP) @ EBU (Hall 10.D21)
  SYES - System Engineering Solutions (Hall 8.F46)
  Media Coding Industry Forum (Hall 8.B45)
  Plisch/RFMondial (Hall 8.C61)
5G-MAG Meetup
IBC Conference
To our best knowledge

## Slide 11: Demos 2023 – QRDs and CRDs are real phones

## Slide 12: Standardization

## Slide 13
For more information on 5G broadcast standards…
ETSI TS 103 720: Profile of 3GPP specification containing the necessary parts to deploy 5G broadcast
TR 36.976: Overall description of enhanced TV (enTV) for 5G broadcast
Various specifications of 5G PHY supporting broadcast together with unicast in TS 36.211, 36.212, 36.213

## Slide 14: 5G Broadcast Standards Evolution
Rel-14
SCS1.25KHz/ CP=200µs Mobility up to 120 km/h
5G BC worldwide standard
TG6/1 and WP6A
Rel-16
Rooftop Mobility up to 250 km/h
5G BC is an EU standard (ETSI TS 103 720)
Rel-17 Enhanced BW= 6/7/8 MHz for UHF
Enhanced Version of ETSI TS 103 720
AI1.5 WRC23
Rel-18 Requirements for UHF band, URL Handling
Roadmap towards WRC23
3GPP
3GPP
ITU
ETSI
3GPP
ETSI 5G-MAG
ITU
3GPP
2017
2020
2019
2020
06/22
06/23
2023
09/23
Bug fixes and clarifications from trials & Rel-17
Adding bandwidth information, including 6/7/8 MHz
5G Media Streaming: integrated unicast & broadcast
Consistent codecs and formats
Support of Public Warning System & Emergency Alerts

## Slide 15: Latest Updates
5G Broadcast will evolve with 3GPP pace

## Slide 16: Technology Evolution

## Slide 17: MBMS/LTE eMBMS/5G broadcast History
Building upon a strong 3GPP technology foundation
eMBMS defined for LTE starting in Rel-8/Rel-9, improving coverage and efficiency
eMBMS enhancements in Rel-12 include MOOD and expansion to MCPTT
Enabling terrestrial broadcast and expanding to new services; Meeting 7/10 5G Broadcast requirements in Rel-14
LTE eMBMS/enTV
in 3GPP Rel-14
LTE
LTE-A
Further enhancements5
to fully satisfy 5G
broadcast requirements
5G
Target market focused on
Cellular operators
Target market expanded to
Broadcasters
3GPP Rel-14 (completed)
Enabling terrestrial broadcast and expanding to new services; Meeting all 5G Broadcast requirements in Rel-16
5G broadcast is a “broadcast standard” (same target as DVB or ATSC) based on 3GPP silicon and ecosystem.
3GPP could have taken a radical approach to define a clean slate radio system to meet the broadcasters’ requirements, instead a more pragmatic route was chosen. Experiences from the past with dedicated modems such as MediaFLO or DVB-H, and the need for easy integration into mainstream mobile devices, led to the decision to evolve eMBMS to LTE-based 5G Broadcast instead of any radical new designs.
3GPP Rel-16 (completed)

## Slide 18: 5G Broadcast: the technology
Main technology components
System layer enhancements
Radio access enhancements
Rel-14
enTV1
Rel-16
enTV
is 5G Broadcast
Broadcast
Broadcast
Unicast control
xMB
Content provider
    Receive only mode
    Delivery of free-to-air content to devices without SIM/service subscription
    Unified protocol stack
    CMAF packaging – compatible with unicast and broadcast stacks
    Standardized network APIs
    Content providers can deliver media over 5G Broadcast with a unified framework
    Shared broadcast
    Multiple operators can serve users on a common broadcast carrier
    Longer range & high mobility
    New numerology with 100/200/300us CP2 for up2 100km radius and 250km/h speed
    More broadcast capacity
    Supports dedicated broadcast network with 100% eMBMS carrier allocation
    More deployment flexibility
    Single network for mobile and fixed devices with enhanced support for rooftop reception
    Better efficiency
    New subframe design reduces overhead in dedicated broadcast transmissions

## Slide 19: RAN: MBMS  5G Broadcast Evolution
Mixed unicast/MBMS carrier
15 kHz numerology
Extended CP of 16.7us
Multi-cell transmission only (MBSFN)
Up to 60% of subframes for MBSFN transmission
Single-cell transmission (SC-PTM)
Transmission on PDSCH with new group identities
Non-synchronized transmitters
Longer cyclic prefixes for support of larger ISD
Up to 100% of subframes for MBSFN transmission on a dedicated carrier
Subframes fully dedicated to MBSFN transmission
Targeting rooftop and car-mounted antennas, handheld receivers
Release 9
Release 13
Release 14
> 15 km
“Operator controlled” MBMS
“Broadcaster controlled” MBMS
New numerologies to target rooftop reception with up to 125 km ISD
High mobility reception: fixed, portable and mobile receivers up to 250 km/h
Enhancements to CAS—increased PDCCH agg. Level, PBCH repetition, CFI in MIB
Release 16
6/7/8 MHz channel bandwidth to support common global channel bandwidth for broadcast systems
Introduction of UHF Band 108 to address RF transmitter and receiver requirements
Release 17/18

## Slide 20: Performance Comparison 5G Broadcast vs. an unconstrained system

## Slide 21: Summary of potentially identified differences
What are the impacts of features in different systems on the overall performance?
Channel Coding and modulation schemes
Time Interleaving
Frequency Interleaving
Antenna Configuration
Receiver requirements

## Slide 22: Simulations
Aligned with IEEE papers [1][2]
Parameter | Unconstrained System (i.e., ATSC 3.0) | 5G Broadcast
System Bandwidth (MHz) | 8 | 8
Useful BW (MHz) | 7.78 | 7.2
FFT length | 8192 | 12288
Subcarrier Spacing (kHz) | 1.125 | 1.25
Sampling rate (MHz) | 9.216 | 15.36
OFDM symbol duration (us) | 889 | 800
CP duration (us) | 222.2 | 200
Channel estimation | LMMSE over 48 consecutive pilots per RB bundle | 
Number of Rx antennas | 1 (unless specified otherwise) | 
Pilot pattern stagger | (Fd3, Td2) | (Fd3, Td2)
Time (T) and/or Frequency (F) interleaver | F interleaver: ON T interleaver: 400 ms extended CTI | None
Modulation | QPSK (Svc 1) NUC 16-QAM (Svc 2) | QPSK (Svc 1) 16-QAM (Svc 2)
Coding | 8/15 LDPC 64800 + BCH | 8/15 Turbo
TBS | 34368 | 5544 (Svc 1) 10296 (Svc 2)
Throughput | ~5 Mbps for Svc1 and ~10 Mbps for Svc 2 | 
Parameter | Unconstrained System (i.e., ATSC 3.0) | 5G Broadcast
System Bandwidth (MHz) | 8 | 8
Useful BW (MHz) | 7.78 | 7.2
FFT length | 8192 | 12288
Subcarrier Spacing (kHz) | 1.125 | 1.25
Sampling rate (MHz) | 9.216 | 15.36
OFDM symbol duration (us) | 889 | 800
CP duration (us) | 222.2 | 200
Channel estimation | LMMSE over 48 consecutive pilots per RB bundle | 
Number of Rx antennas | 1 (unless specified otherwise) | 
Pilot pattern stagger | (Fd3, Td2) | (Fd3, Td2)
Time (T) and/or Frequency (F) interleaver | F interleaver: ON T interleaver: 400 ms extended CTI | None
Modulation | QPSK (Svc 1) NUC 16-QAM (Svc 2) | QPSK (Svc 1) 16-QAM (Svc 2)
Coding | 8/15 LDPC 64800 + BCH | 
TBS | 34368 | 5544 (Svc 1) 10296 (Svc 2)
Throughput | ~5 Mbps for Svc1 and ~10 Mbps for Svc 2 | 
[1] S. -I. Park et al., "Performance Analysis of All Modulation and Code Combinations in ATSC 3.0 Physical Layer Protocol," in IEEE Trans. on Broadcasting, vol. 65, no. 2, pp. 197-210, June 2019, doi: 10.1109/TBC.2018.2871372
[2] S. -K. Ahn et al., "Evaluation of ATSC 3.0 and 3GPP Rel-17 5G Broadcasting Systems for Mobile Handheld Applications," in IEEE Trans. on Broadcasting, doi: 10.1109/TBC.2022.3222988.

## Slide 23: Achievable spectral efficiency&capacity (LTE, NR, ATSC)
1 Receive antenna, AWGN
All technologies close to Shannon limit (< 2dB), NR and LTE (5GB) offer similar performance
Gains of an unconstrained system are < 1dB, and get smaller with adding constraints (64k -> 16k)
Channel Code and BICM 0.5 – 1dB

## Slide 24: Frequency & Time Interleaver (1)
Analyzing the performance difference between ATSC 3.0 and 5G Broadcast over a Rician fading channel (RC20 channel from [1]) for static and 3 km/h
For static and 3 km/h, additional gain compared to AWGN (BICM and Code), is the Frequency Interleaver with around 0.5dB.
No gains for Time Interleaver with a reasonably powerful LoS component
Performance over multipath channels with line-of-sight (LoS) paths, single receive antenna
Frequency Interleaver 0.5 dB

## Slide 25: Frequency & Time Interleaver (2)
Analyzing the performance difference between ATSC 3.0 and 5G Broadcast over a NLoS RL20 channel from [1]
ATSC 3.0 offers additional performance benefits, with additional 0.5 dB (on top of the 1.4 dB gap)
Gain from using a frequency interleaver (in a static setting) remains relatively small.
Larger gain for ATSC 3.0 in Svc2 since at very high data rate, as the 5G Broadcast standard requires two codeblocks instead of one
Non-line-of-sight multipath channels, single receive antenna
Time Interleaver for static NLOS 0.5-1 dB

## Slide 26: Receive Antennas for NLoS
2 Rx antennas are a basic feature in cellular modems
Harness the spatial orders of diversity in a mobile environment, and result in a performance gap of 2 dB for 5G Broadcast, when compared against ATSC 3.0.
In low mobility, the time interleaver from ATSC provides additional gains of around 1dB
fading NLoS channel, for a pedestrian UE (with a mobility of 3 kmph) in an urban environment [2]
Time Interleaver for 3km/h NLOS 1 dB

## Slide 27: Some Fundamentals of Cellular Modems
3GPP technologies are primarily designed for exploiting frequent and rapid feedback on the current channel state at each receiver and then optimize the delivery exploiting time and frequency scheduling, adaptive coding and modulation, interference management, power allocation, spatial multiplexing using multiple antennas and other functionalities.
Hence, cellular modem hardware is built to process "one Transport Block in one slot", as a design principle to adapt and react to the above feedback.
Hybrid ARQ is designed to provide additional redundancy for one transport block within another single slot in order to react to non-decodable transport blocks
Any departure from the above design has significant impact on receiver implementation
  Cost of collecting LLRs for multiple transport blocks requires a large increase of on-chip memory
  A cellular modem only stores LLRs for a single transport block in the on-chip memory
  Huge change to the hardware implementation due to the scheduling of writing/reading to/from memory
  Area size is costly, moving data off and on chip is heavily impacting power consumption and and and  infeasible
For mobility and NLOS situations, the exploitation of time and frequency diversity is very essential

## Slide 28: Interleaving – Facts, Challenges and Opportunities
MBMS uses Application Layer FEC and Unicast Repair to address time diversity.
  Application Layer FEC works very well for the purpose of file casting with spreading over a long-time frame
    M. Luby, T. Gasiba, T. Stockhammer and M. Watson, "Reliable Multimedia Download Delivery in Cellular Broadcast Networks," in IEEE Transactions on Broadcasting, vol. 53, no. 1, pp. 235-246, March 2007, doi: 10.1109/TBC.2007.891703
  Application Layer FEC has its limits when it comes to below 1 second latencies (see 3GPP TR 26.881)
    It is recommended for that
      For low-delay applications, with latencies of at most 1 second, should be supported by well-dimensioned physical layer FEC
      for latencies in the range of a few seconds or more the technology in TS26.346 for AL-FEC is applicable as it has been chosen by 3GPP. The FEC framework was designed for latencies in the range of several seconds and therefore applies also to those cases.
  Application Layer FEC and Unicast Repair is obviously available in 5G Broadcast and can be exploited.
What about physical layer interleaving in 3GPP Systems?
  Harnessing time diversity for 5G Broadcast was first proposed in 3GPP by EBU/IRT/BBC (R1-1911355), where it was pointed out that physical-layer time interleaving provides performance benefits - especially for high-mobility use cases.
  However, the solution proposed in R1-1911355 would require anywhere between a x to x increase in the LLR buffer memory of the receiver.
  Due to the design principle "mixing multiple Transport Blocks into a single slot" it was considered infeasible
Can we create a modem-friendly time and frequency interleaving?
How to handle time and frequency diversity exploitation in case of the absence of a feedback channel

## Slide 29: Time Interleaving proposal: 3GPP modem-friendly designs
Objective: Design that provides time-diversity without increasing the LLR buffer memory at the receiver.
Basic Approach: Reuse of the 3GPP building block behind HARQ retransmissions and combining, which allows to spread the coded bits of a transport block (TB) across multiple non-consecutive slots/subframes.
Details:
  TB size is scaled by —the number of redundancy versions (RVs) used for each TB.
  The “HARQ memory” is used to store the LLRs corresponding to each RV and decode after all RVs for a TB have been received.
  Each RV spans a single slot/subframe, and each TB is transmitted over occasions, with separation of slots between each transmission.
Following two HARQ techniques at the receiver are re-used to build the time interleaver
  At a given (TTI), the modem is only required to process reception from a single TB. The ordering of coded bits within one TTI is the same as in current cellular systems.
  The already existing “HARQ-process handling” framework is re-used.
Interleaved transmission of “HARQ redundancy versions” of (scaled) transport blocks across slots/subframes.

## Slide 30: Time Interleaving proposals: modem-friendly designs
…
…
…
…
…
…
Parts of TBs spread across slots
Parts of TBs spread across slots
Original TBS
Scale original TBS by a factor of
Transmit “parts” (e.g., RVs) of the -scaled TB over “non-contiguous” slots
Example circular buffer (for a codeblock of a scaled TB) for incremental redundancy using “legacy” RV starting pointers
(Potentially) punctured systematic bits
Example circular buffer (for a codeblock of a scaled TB) for incremental redundancy using “modified” RV starting pointers
Updated design
Rate > 1 for "initial" transmission permitted
“modified” RVs ensure that the coded bits for start right after those for , and we are not restricted to 4 RVs
To spread out the systematic bits of each codeblock (carried by the lower-indexed RVs) within the TB as far apart in time as possible,
for , we use
for

## Slide 31: Frequency interleaving
With the scaled TB sizes, the number of codeblocks in a TB increases, thereby requiring frequency interleaving of the OFDM symbols.
The main principles behind the proposed frequency interleaver are:
      The tones corresponding to the codeblocks are written row-wise.
      Pseudo-random shifts are applied to the columns.
      Elements are read column-wise.
For a detailed standards’ focused description on these aspects, see R1-1912692

## Slide 32: Evolution of SNR requirements with interleaving
 | Baseline 5GB | 4 RV Time Intlv. only | 4 RV T/F Intlv. | 8 RV T/F Intlv.
SNR for 3 kmph | 17.7 dB | 17.5 dB (0.2 dB) | 16.3 dB (1.4 dB) | 15.6 dB (2.1 dB)
SNR for 40 kmph | 17.7 dB | 14.6 dB (3.1 dB) | 13.8 dB (3.9 dB) | 12.7 dB (5 dB)
SNR for 120 kmph | 18.3 dB | 14.7 dB (3.6 dB) | 14.2 dB (4.1 dB) | 12.9 dB (5.4 dB)
Performance comparison between
baseline 5G Broadcast
4 RV-based time interleaver with a depth of 128 ms: each TB samples the channel uniformly, every 32 ms.
4 RV-based time and Frequency interleaving with depth of 686 tones for maximal frequency spreading
8 RV-based time interleaver, with depth of 256 ms and frequency interleaving depth set to 383 tones.
Required SNRs for BLER, and gains (in parentheses) with interleavers
1 Receive Antennas, NLoS India-Urban channel [1]

## Slide 33: Impact of Modem-Friendly Time and Frequency Interleaving
2 Receive Antennas, NLoS India-Urban channel
SNR required for 0.1% BLER using 8RV-based intlv. + 2Rx
  2Rx + RV-based T/F intlv at 256ms time interleaving yields dB loss w.r.t. 2Rx-based ATSC 3.0 at 400ms time interleaving
Speed | ATSC 3.0 + 2Rx | Baseline 5G Broadcast + 2Rx | 5G Broadcast 8RV + 2Rx
3 km/h | 8.7 dB | 10.7 (-2 dB) | 8.9 dB (-0.2 dB)
40 km/h | 6.6 dB | 11 (-4.4 dB) | 7.1 dB (-0.5 dB)
120 km/h | 6.2 dB | 11.4 (-5.2 dB) | 7 dB (-0.8 dB)
0.8 dB
0.5 dB
0.2 dB

## Slide 34: Time-frequency interleaver status in 3GPP
Time-frequency interleaving for 5G Broadcast was discussed in Rel-16 and was shown to provide large gains in time-varying channels.
The following was captured in the RAN1#99
Chairman’s notes:
Figure (from R1-1913439) showing a 3+dB gain or a ~30% throughput gain from interleaving (at 0.1% BLER target)
R1-1913439 On time and frequency interleaving for terrestrial broadcast EBU, BBC, IRT, NHK, ABS, DISH, Eutelsat, Shanghai Jiao Tong University, Fraunhofer HHI, Fraunhofer IIS, Enensys, Qualcomm, Rohde&Schwarz, Nokia, Nokia Shanghai Bell, ATEME, Nomor Research, Sony
Time and frequency interleaving for terrestrial broadcast was discussed even though it was not explicitly in the scope of the WID. However, consensus was not reached. It can be considered for a later release.

## Slide 35: Summary and Conclusions
5G BROADCAST RECEIVERS: OPTIMIZING PERFORMANCE UNDER IMPLEMENTATION CONSTRAINTS
Broadcast networks and usage of configurations needs to be done for worst-case scenario.
For example, gains achieved in the 120 kmph scenario may not relevant, if such a planning would fail to serve a large number of receivers moving at lower speeds.
In this case, comparison between 5G broadcast and ATSC3.0 is provided for NLOS for different speeds and configurations
The main design target & “reason for being” of 5G broadcast is to enable operation of a broadcast network where the receivers are hardware-compatible with cellular modems
  “Hardware compatible” means lower barrier to adoption in mobile devices compared to other broadcasting technologies
    Several 5G Broadcast building blocks are already there in a 4G/5G modem, hence the additions are marginal.
    For other technologies, a separate piece of silicon / die area would be required
In comparison with unconstrained broadcast designs, 5G Broadcast Rel-18 is only marginally worse and there are expectations to address remaining gaps in Rel-19 without compromising the design goals
5G Broadcast is a transport and is successfully combined with unicast service layers – seamless unicast fallback has been successfully demonstrated
SNR for | ATSC 3.0 + 1Rx | ATSC 3.0 + 2Rx | 5G + 2Rx | 5G + 2Rx + TFI
3 kmph | 14.4 dB | 8.7 dB | 10.7 dB | 8.9 dB
40 kmph | 11.2 dB | 6.6 dB | 10.9 dB | 7.3 dB
120 kmph | 10.8 dB | 6.2 dB | 11.4 dB | 7 dB
Worst case | 14.4 dB | 8.7 dB | 11.4 dB | 8.9 dB

## Slide 36: Support the 5G Broadcast Community in 3GPP RAN Rel-19 Planning
For Rel-19, we propose to have a small work item on necessary enhancements for 5G Broadcast (5GB) that are essential for its deployment.
The scope of the proposed enhancements is limited to coexistence with other broadcast systems (mainly ATSC 3.0) due to regulatory constraints, and standardizing one mechanism already discussed in Rel-16 (time-frequency interleavers).
The main proposals are:
  Proposal 1: Standardize “CAS muting” for 5G Broadcast, i.e., the CAS can be dropped with some pattern that is known to the UE.
  Proposal 2: Standardize time-frequency interleavers for 5G Broadcast, taking as baseline the mechanism in R1-1913439.
Come to RAN#102 to Edinburgh and co-sign the initial proposal from Qualcomm and 5G-MAG input