## Slide 1: 5G Broadcast - Standards, Technologies and Market Updates
April 19, 2024
ITU-D Question 2/1 Focus session on Evolution of Broadcasting systems
@qualcomm_tech
Dr. Thomas Stockhammer
Senior Director Technical Standards
Qualcomm Technologies

## Slide 2
Presenter
Dr. Thomas Stockhammer
Senior Director, Technical Standards
Qualcomm Europe, Inc., IEEE Fellow
Leading and driving among others
DVB: 5G TF, DVB-I
MPEG: MPEG-I, CMAF and DASH
3GPP: XR over 5G, 5G Video, 5GMS
DASH-IF: Interop WG, Test
ETSI & 5G-MAG: 5G Broadcast and 5GMS
CTA WAVE: CMAF Device PB, Test
Metaverse Standards Forum: Chair, Board
Today’s agenda
# What is 5G Broadcast
# Standards
# Technologies
# Trials and deployments
# Opportunities and Selected Use Cases
# Next Steps

## Slide 3: Challenges for Broadcasters: Devices, Formats, Users
Broadcasters
and Content Provider
Internet Cloud/Edge
Cellular WiFi
UHD/8K
Social
3D
Immersive
Personalized
Interactive
Gaming-like
Short & long
Live
On-Demand
User Generated
AI-supported
Location
Global
Secure
Time-shift
…
Quality
Cost
Scalability
UHF

## Slide 4: 5G defines two modes of broadcast communication
Addressing diverse ecosystem, deployment, and use case requirements
5G broadcast
Mixed-mode multicast
Single Frequency Network (SFN) for downlink broadcast only
Dynamic switching between broadcast and unicast, e.g., SC-PTM1
Focus of this presentation
Operator spectrum (IMT)
Integration with unicast network
Efficient delivery of multicast/broadcast traffic (vs unicast)
Reuse of cellular infrastructure (low power).
Broadcast spectrum (e.g. UHF)
No unicast. Downlink – only traffic.
Delivery of linear content (e.g. TV) or IP file delivery
Dedicated broadcast infrastructure (can be high power)

## Slide 5: General technology introduction
“5G broadcast” is a broadcasting standard defined by 3GPP (Release 16 - 2020)
  3GPP is the industry group responsible for defining global cellular tech standards (e.g. 4G / 5G)
  In the last few years 3GPP has expanded to new verticals (e.g. broadcast, automotive, satellite, etc.) hence it should not be regarded as a surprise that a broadcasting tech is coming out of 3GPP
Even though 5G Broadcast has been standardized by 3GPP, it is a broadcasting technology
  I.e. meant to be used by broadcasting operators, in broadcasting spectrum
  No need of supporting a unicast network. 5G Broadcast does not have anything to do with unicast
The main design target & “reason for being” of 5G broadcast is to enable operation of a broadcast network where the receivers are hardware-compatible with cellular modems
  “Hardware compatible” means lower barrier to adoption in mobile devices compared to other broadcasting technologies
    This is because several 5G Broadcast building blocks are already there in a 4G/5G modem, hence the additions are marginal.
    For other technologies, a separate piece of silicon / die area would be required
  To be clear, 5G Broadcast has nothing to do with “cellular operators trying to take over from broadcasters”
5G broadcast and 3GPP

## Slide 6: 5G Broadcast – Core Features for multiple use cases
SIM-less reception with simplified architecture
Receive-Only Mode (ROM) & Free-to-Air (FTA)
Different spectrum options (e.g. UHF, SDL), as well as SFN/MFN
Various deployment possibilities (e.g. MNOs, BNOs)
Using existing infrastructure (HPHT, MPMT and LPLT)
Highly flexible velocities (up to 250 KM/h Vs up to 300 µS)
Can be combined with existing 4G and 5G features (unicast, PWS)

## Slide 7
Significant interests towards 5G broadcast deployment worldwide
2024: European Championship
2020-22: 5G Media2Go Stuttgart/Heilbronn
2017-20: 5G Today in Bavaria
Germany
2020-22: VISTA Project with O2 Virgin Media
UK
2020: Distribution of free-to-air linear radio and TV using Rel-14 enTV with HPHT in Barcelona
2022 & 2023: MWC demos
Spain
2020-21: Delivery of TV and radio with Rel-14 broadcast trial deployment in Santiago de Tolú
Colombia
2020-23: TV 3.0 project calling for proposals
Brazil
2018-23: TV delivery with Rel-14/16 HPHT in Aosta and Turin
Italy
2020-23: Distribution of TV/Radio with 5G BC Rel-14/16 , with eMBB in Vienna
Austria
2020+: Growing interest in latest broadcast3 technologies
2023: Discussion on DTM strategy based on market feedback
Late 2021: Distribution of live TV using Rel-16 enTV near Seoul
South Korea
1 National Radio and Television Administration 2 Academy of Broadcast and Science commercia potential 3 Prasar Bharti working jointly with IIT Kanpur on Next Generation Broadcast Technology
Malaysia
2020+: Growing interest in 5G BC in addition to ATSC3.0
2023: FCC Approves A Low Power TV Station To Broadcast Over 5G Networks
2023: First 5G Broadcast in the US and first 24/7 5G Broadcast globally
2024: Foundation of 5G Broadcast Collective
US
Philippines
2019-22: Direct to mobile Live TV/Radio in Manilla
South Africa
2019-20: Live testing of Rel-14 in Johannsburg
2022+: 5G Broadcast under investigation as latest broadcast technology
Russia
2022: Interest towards 5G BC during Mediterranean Games
France
2018-2022: Live testing of 5G BC in Paris
2024: Olympics
Belgium
2022-24: 5G BC imec.icon project with 2 HPHT sites
Finland
2019-22: TV delivery with Rel-14/16 HPHT in 3 sites
CZ
2020-23: Distribution of TV/Radio in Prague
2019-24: AIB project based on 5G Broadcast under the administration of NRTA1 and ABS2
2023: 5G Broadcast Chengdu pilot project formally kicked off on July 20th
GATIS' Global 5G Broadcast Summit
India
Denmark
Tour de France 22 powered by 5GB
Algeria
Greece
Croatia
2021-23: Live TV/Radio with 5G BC Rel-14/16 , with 3MHz in Athens
2022-24: Live 5G BC Rel-14/16
China
2024: Report close to completion – next steps are trials
Europe
2023: European broadcasters ink 5G Broadcast MoU

## Slide 8: First 5G Broadcast in US
July 14th 2023 - FCC granted experimental license for 5G broadcast
Sep 13th 2023 – Station went on air and started 24/7 re-broadcast of FranceTV
Full leverage of existing infrastructure with no change in freq, antenna, power output
Successful indoor –stationary and outdoor – stationary and mobile reception with 8650 QRD units
Next steps: presentation to FCC, additional licenses for another 5-10 stations
Also emergency notification, first responder live trial, datacasting use cases
NAB 2024: Foundation of 5G Broadcast collective https://5gbc.tv/

## Slide 9: China Status
Chinese and international experts and scholars from Beihang University, Communication University of China (CUC), 5G-MAG, EBU, ORS, TDF, XGN, Rohde & Schwarz (R&S), Qualcomm, Xiaomi, vivo, Chengdu Kaiteng Sifang and Beijing BBEF Science & Technology
Sichuan has initiated the first trials and deployment of 5G Broadcast.
Regional broadcasters show great interests to duplicate the demo to verify & demo the 5GB services in their own network. Guangdong already asked, Guangxi is in the line, Shanxi also asked during the meeting, more requests are on the way.
ABS supports them together with domestic infra vendors and OEMs to launch pre-commercial trials
https://www.5g-mag.com/post/27-10-23-5g-mag-participates-at-gatis-summit

## Slide 11: 5G Broadcast at IBC 2023
Rohde & Schwarz and Qualcomm to demonstrate 5G Broadcast ecosystem readiness at IBC2023
  At IBC2023 Rohde & Schwarz will demonstrate the latest innovative features, including seamless service continuity between broadcast and broadband, and low latency content distribution. Thanks to the software architecture of the TH1 transmitter family, all these and future enhancements can be readily added in the field on-demand.
https://www.nakolos.com/ibc2023/
  XGen Networks (Hall 1.D90)
  5G-MAG (5G MEDIA ACTION GROUP) @ EBU (Hall 10.D21)
  SYES - System Engineering Solutions (Hall 8.F46)
  Media Coding Industry Forum (Hall 8.B45)
  Plisch/RFMondial (Hall 8.C61)
5G-MAG Meetup
IBC Conference
To our best knowledge

## Slide 12: Demos 2023 – QRDs and CRDs are real phones

## Slide 13: Standardization

## Slide 14
For more information on 5G broadcast standards…
ETSI TS 103 720: Profile of 3GPP specification containing the necessary parts to deploy 5G broadcast
TR 36.976: Overall description of enhanced TV (enTV) for 5G broadcast
Various specifications of 5G PHY supporting broadcast together with unicast in TS 36.211, 36.212, 36.213

## Slide 15: 5G Broadcast Standards Evolution
Rel-14
SCS1.25KHz/ CP=200µs Mobility up to 120 km/h
5G BC worldwide standard
TG6/1 and WP6A
Rel-16
Rooftop Mobility up to 250 km/h
5G BC is an EU standard (ETSI TS 103 720)
Rel-17 Enhanced BW= 6/7/8 MHz for UHF
Enhanced Version of ETSI TS 103 720v.1.2.1
Enhanced Version of ETSI TS 103 720v.1.3.1
Rel-18 Requirements for UHF band, URL Handling
Rel-19 work in planning (TFI, Co-existence, Low-Latency)
Roadmap towards WRC23
3GPP
3GPP
ITU
ETSI
3GPP
ETSI 5G-MAG
3GPP
2017
2020
2019
2020
06/22
06/23
06/25
12/23
ETSI 5G-MAG
3GPP
12/24

## Slide 16: Technology Evolution

## Slide 17: MBMS/LTE eMBMS/5G broadcast History
Building upon a strong 3GPP technology foundation
eMBMS defined for LTE starting in Rel-8/Rel-9, improving coverage and efficiency
eMBMS enhancements in Rel-12 include MOOD and expansion to MCPTT
Enabling terrestrial broadcast and expanding to new services; Meeting 7/10 5G Broadcast requirements in Rel-14
LTE eMBMS/enTV
in 3GPP Rel-14
LTE
LTE-A
Further enhancements5
to fully satisfy 5G
broadcast requirements
5G
Target market focused on
Cellular operators
Target market expanded to
Broadcasters
3GPP Rel-14 (completed)
Enabling terrestrial broadcast and expanding to new services; Meeting all 5G Broadcast requirements in Rel-16
5G broadcast is a “broadcast standard” (same target as DVB or ATSC) based on 3GPP silicon and ecosystem.
3GPP could have taken a radical approach to define a clean slate radio system to meet the broadcasters’ requirements, instead a more pragmatic route was chosen. Experiences from the past with dedicated modems such as MediaFLO or DVB-H, and the need for easy integration into mainstream mobile devices, led to the decision to evolve eMBMS to LTE-based 5G Broadcast instead of any radical new designs.
3GPP Rel-16 (completed)

## Slide 18: RAN: MBMS  5G Broadcast Evolution
Mixed unicast/MBMS carrier
15 kHz numerology
Extended CP of 16.7us
Multi-cell transmission only (MBSFN)
Up to 60% of subframes for MBSFN transmission
Single-cell transmission (SC-PTM)
Transmission on PDSCH with new group identities
Non-synchronized transmitters
Longer cyclic prefixes for support of larger ISD
Up to 100% of subframes for MBSFN transmission on a dedicated carrier
Subframes fully dedicated to MBSFN transmission
Targeting rooftop and car-mounted antennas, handheld receivers
Release 9
Release 13
Release 14
> 15 km
“Operator controlled” MBMS
“Broadcaster controlled” MBMS
New numerologies to target rooftop reception with up to 125 km ISD
High mobility reception: fixed, portable and mobile receivers up to 250 km/h
Enhancements to CAS—increased PDCCH agg. Level, PBCH repetition, CFI in MIB
Release 16
6/7/8 MHz channel bandwidth to support common global channel bandwidth for broadcast systems
Introduction of UHF Band 108 to address RF transmitter and receiver requirements
Release 17/18

## Slide 19
Details of the paper
Session and Recording

## Slide 20: Summary and Conclusions
5G BROADCAST RECEIVERS: OPTIMIZING PERFORMANCE UNDER IMPLEMENTATION CONSTRAINTS
Broadcast networks and usage of configurations needs to be done for worst-case scenario.
For example, gains achieved in the 120 kmph scenario may not relevant, if such a planning would fail to serve a large number of receivers moving at lower speeds.
In this case, comparison between 5G broadcast and ATSC3.0 is provided for NLOS for different speeds and configurations
The main design target & “reason for being” of 5G broadcast is to enable operation of a broadcast network where the receivers are hardware-compatible with cellular modems
  “Hardware compatible” means lower barrier to adoption in mobile devices compared to other broadcasting technologies
    Several 5G Broadcast building blocks are already there in a 4G/5G modem, hence the additions are marginal.
    For other technologies, a separate piece of silicon / die area would be required
In comparison with unconstrained broadcast designs, 5G Broadcast Rel-18 is only marginally worse and there are expectations to address remaining gaps in Rel-19 without compromising the design goals
5G Broadcast is a transport system and has been successfully combined with unicast service layers – seamless unicast fallback successfully demonstrated
SNR for | ATSC 3.0 + 1Rx | ATSC 3.0 + 2Rx | 5G + 2Rx | 5G + 2Rx + TFI
3 kmph | 14.4 dB | 8.7 dB | 10.7 dB | 8.9 dB
40 kmph | 11.2 dB | 6.6 dB | 10.9 dB | 7.3 dB
120 kmph | 10.8 dB | 6.2 dB | 11.4 dB | 7 dB
Worst case | 14.4 dB | 8.7 dB | 11.4 dB | 8.9 dB

## Slide 21: Technologies and Trials

## Slide 22: Taking a system approach to technology innovations
Making cellular broadcast a reality
Vision
Identifying a problem or need, and establishing system requirements
We envisioned a more efficient way to deliver mass media over cellular networks
Invention
Inventing new technologies and end-to-end system architecture
We pioneered key cellular broadcast technologies for 3G, 4G, and 5G
Proof-of-concept
Delivering end-to-end prototypes and impactful demonstrations
We showcased cellular broadcast technologies at various industry events
Standardization
Leading ecosystem towards new projects and driving new system designs
We led the mobile and broader industries to standardize cellular broadcast
System Trials
Collaborating on field trials that track standards development, preparing for commercialization
We worked with mobile operators, device manufacturer and content providers on trials
Commercialization
Engaging with global ecosystems to deploy new products and services
Successfully productize cellular broadcast in our products
1
3
2
4
5
6
Joint demo at MWC’23

## Slide 23: Proof of concept in 2022:
Objective: confirm feasibility and move ecosystem towards commercial deployments.
Summary of features:
  Reception from broadcast transmitter
  Reception in broadcast UHF spectrum
  Operation without SIM card
  Reuse of cellular hardware (smartphone)

## Slide 24
Spanish public
broadcaster
Streaming
solutions
Tower company
Network & transmitter
Smartphone / chipset

## Slide 25
Bearer Management
IP Multicast Allocation
Packet Routing/Forwarding
BM-SC
MBMS-GW
SGi-mb
SG-mb
M1
SNYC / FLUTE
Diameter
SYNC
Content Provider
Premium Content Synchronization
Multimedia Content Multiplexing
TMGI Allocation
RESTfull API
TSoIP
DASH
HLS
DTLS*
CMAF*
M2
M2AP
Dynamic Radio Resource Management for Broadcast/Multicast
MCE
Dynamic Resources Scheduling & MCS
R&S Internal Interface
Service Announcement
FEC
MPEG DASH
FLUTE
3GP DASH
ROUTE*
SFN
MFN
MBMS Service Area Management
Carrier Aggregation
Carrier Management
Multi-MCH
x-MB
BSCC2.0 – Internal architecture
Tx/eNB
* In development

## Slide 26: Qualcomm devices
QRDs based on Snapdragon 8 Gen 1 initially, now Gen 2 (8450 / 8550).
Modified (non-commercial) changes to enable a subset of 5G-broadcast features.
Meanwhile, Qualcomm supported enabling 5G Broadcast trials on Commercial devices by applying some firmware upgrades  Commercial Research Devices (CRDs)
Additional trial features are expected in next release of QRDs and CRDs.

## Slide 27: Eurovision Song contest
Link
5G Broadcast demoed live in multiple cities

## Slide 28: Other demos / trials
TowerCast event in Paris
Stuttgart (test drive)
BES expo (Delhi)
CABSAT’22
IMC’22
Rio open ‘23 (BR)
MWC ‘23

## Slide 29: Selected use cases
Enhanced broadcast use cases with 5G broadcast
One-way communication directly to handsets
More cost efficient than unicast (RAN and CDN)
Live sports, special events, general programming
Key for massive events (e.g. World Cup)
Linear TV and Radio
Combine linear video with interactivity.
Linear content from broadcaster, unicast using mobile network.
Comments, ratings, e-commerce, advertising
Interactive media
Emergency notifications to smartphones from broadcast infrastructure.
Possibility of sending text-only notifications and multimedia content
Emergency messages
Software / firmware upgrades.
Download and storage of popular content:
  TV shows
  “Viral” videos in social media.
General file download

## Slide 30: Emergency alerts
5G broadcast inherits from 5G the public warning system capabilities.
The Cell Broadcast Service (CBS) does not require authentication with a PLMN. Hence, a ROM network is inherently compatible with CBS (see 3GPP TS 23 041).
CMAS (commercial mobile alert system) is available in current commercial devices.
  Devices monitor periodically a low-duty cycle paging channel (low power)
  CMAS over 5G broadcast has been demonstrated with R&S infrastructure
Additional capabilities of CMAS:
  Geofencing (send notification to users within a given area)
  Possibility of sending URL linking to emergency media

## Slide 31: Emergency message demo with ABS
Self-contained emergency system (text + multimedia) without need of unicast.

## Slide 32: Coexistence of ATSC 3.0 & 5G Broadcast
5G Broadcast can be deployed by broadcasters in the exact same way as ATSC, and it greatly lowers the barrier to adoption in mobile devices since it is “only” an incremental feature to the 4G/5G modem
  Native broadcasting technologies like ATSC or DVB were never successfully incorporated in mobile devices at scale because their inclusion requires a separate piece of silicon (similar to, say, WiFi or GPS) and the ecosystem never took off
We could make use of the “reserved” frames of ATSC 3.0 to “superimpose” 5G Broadcast, thus achieving coexistence on the same channel
  An alternative would be for ATSC 3.0 and 5G Broadcast to coexist on two different frequencies, i.e. one MUX for each
The same broadcaster could thus deploy & operate both technologies at the same time
  ATSC 3.0 for fixed devices
  5G Broadcast for mobile devices
Documented in ATSC TG3-11
Rel-19 candidate work for 3GPP
ATSC 3.0 & 5G Broadcast can coexist: it does not have to be a either/or
Work Item in ATSC approved and 3GPP under preparation

## Slide 33: DVB-I via 5G Broadcast
Using MBMS/5G Broadcast Reference Points and APIs
Different options are considered
  Using file download services for carouselling metadata
  Using segment streaming for DVB-DASH
  Using transparent mode for DVB-I multicast distribution
Combinations with unicast, hybrid services also under development
See details in ETSI TR 103 972
Expected to be supported by reference tools
Joint DVB/5G-MAG task force

## Slide 34: Hybrid Unicast Broadcast
Content Provider may leverage 5G Unicast systems, 5G Broadcast systems, and 5G devices to build efficient and innovative applications
Supported by well defined network and client-side APIs
Examples:
  Hybrid Services
  Universal Coverage
  Broadcast on Demand
Integrated into 3GPP 5G specs, ETSI TS 103 720 and TR 103 972 (DVB over 5G)
Architectures, Collaboration Models and Use Cases
5G Broadcast Operator
Content Provider
5G MNO

## Slide 35: DVB-I over 5G – combining the best of two worlds
DVB Commercial Requirements in Bluebook C100 (07/21)
ETSI TS 103 720 (06/23): LTE-based 5G Broadcast
ETSI TR 103 972 (07/23): Deployment Guidelines for DVB-I services over 5G Systems
ETSI TS 103 770 DVB-I Service Discovery (11/20)
  Latest version used in trials is A177r4 (09/22)
  Latest published version is the bluebook A177r6 (02/24)
ETSI TS 103 285 DVB-DASH (Dynamic Adaptive Streaming over HTTP)
3GPP TS 26.501 (12/23), TS 26.510 (06/24) TS 26.512 (06/24)
DVB Service layer with 5G Broadcast distribution – specification work

## Slide 36
Qualcomm and Rohde & Schwarz show the world’s first standards-conforming demo of 5G Broadcast integrated into the DVB-I service framework on a commercial smartphone. 5G Broadcast transmissions from the Ismaning/Munich broadcast tower are added as service instance to a DVB-I service list and the DVB-I client is updated to select services included in the 5G Broadcast signals. The 5G Broadcast signals are integrated in the service list of the German DVB-I Pilot, whereby the instances for 5G Broadcast get highest priority and will hence be selected by the 5G Broadcast capable receivers, but ignored by regular TV sets or smartphones.
Joint demo of Rohde & Schwarz, Qualcomm and the colleagues from ZDF and ARD

## Slide 37: 5G-MAG Reference Tools?
Current list of official contributors
  Developer Space
  https://developer.5g-mag.com

## Slide 38: Summary & Next Steps
Join the community of open standards, innovation and development
5G is a platform for Broadcasters and Content Providers with features including 5G broadcast, Public Warning and many others
3GPP Standards are global and address billions of devices – from smart phones to many more verticals (automotive, IOT, etc.)
Qualcomm contributes, supports and drives open systems through technologies, standards and reference tools