## Slide 1: 5G Broadcast – Latest on Standards, Technologies and Devices
Based on IBC 2024 Info
October 2024
@qualcomm_tech
Dr. Thomas Stockhammer
Senior Director Technical Standards
Qualcomm Technologies

## Slide 2: 5G defines two modes of broadcast communication
Addressing diverse ecosystem, deployment, and use case requirements
5G broadcast
Mixed-mode multicast
Single Frequency Network (SFN) for downlink broadcast only
Dynamic switching between broadcast and unicast, e.g., SC-PTM1
Focus of this presentation
Operator spectrum (IMT)
Integration with unicast network
Efficient delivery of multicast/broadcast traffic (vs unicast)
Reuse of cellular infrastructure (low power).
Broadcast spectrum (e.g. UHF)
No unicast. Downlink – only traffic.
Delivery of linear content (e.g. TV) or IP file delivery
Dedicated broadcast infrastructure (can be high power)

## Slide 3: General technology introduction
“5G broadcast” is a broadcasting standard defined by 3GPP (Release 16 - 2020)
  3GPP is the industry group responsible for defining global cellular tech standards (e.g. 4G / 5G)
  In the last few years 3GPP has expanded to new verticals (e.g. broadcast, automotive, satellite, etc.) hence it should not be regarded as a surprise that a broadcasting tech is coming out of 3GPP
Even though 5G Broadcast has been standardized by 3GPP, it is a broadcasting technology
  I.e. meant to be used by broadcasting operators, in broadcasting spectrum
  No need of supporting a unicast network. 5G Broadcast does not have anything to do with unicast
The main design target & “reason for being” of 5G broadcast is to enable operation of a broadcast network where the receivers are hardware-compatible with cellular modems
  “Hardware compatible” means lower barrier to adoption in mobile devices compared to other broadcasting technologies
    This is because several 5G Broadcast building blocks are already there in a 4G/5G modem, hence the additions are marginal.
    For other technologies, a separate piece of silicon / die area would be required
  To be clear, 5G Broadcast has nothing to do with “cellular operators trying to take over from broadcasters”
5G broadcast and 3GPP

## Slide 4: 5G Broadcast – Core Features for multiple use cases
SIM-less reception with simplified architecture
Receive-Only Mode (ROM) & Free-to-Air (FTA)
Different spectrum options (e.g. UHF, SDL), as well as SFN/MFN
Various deployment possibilities (e.g. MNOs, BNOs)
Using existing infrastructure (HPHT, MPMT and LPLT)
Highly flexible velocities (up to 250 KM/h Vs up to 300 µS)
Can be combined with existing 4G and 5G features (unicast, PWS)

## Slide 5: Business use cases, trial experiences, new requirements

## Slide 6
Significant interests towards 5G broadcast deployment worldwide
2024: European Championship
2020-22: 5G Media2Go Stuttgart/Heilbronn
2017-20: 5G Today in Bavaria
Germany
2020-22: VISTA Project with O2 Virgin Media
UK
2020: Distribution of free-to-air linear radio and TV using Rel-14 enTV with HPHT in Barcelona
2022 & 2023: MWC demos
Spain
2020-21: Delivery of TV and radio with Rel-14 broadcast trial deployment in Santiago de Tolú
Colombia
2020-23: TV 3.0 project calling for proposals
Brazil
2018-23: TV delivery with Rel-14/16 HPHT in Aosta and Turin
Italy
2020-23: Distribution of TV/Radio with 5G BC Rel-14/16 , with eMBB in Vienna
Austria
2020+: Growing interest in latest broadcast3 technologies
2023: Discussion on DTM strategy based on market feedback
Late 2021: Distribution of live TV using Rel-16 enTV near Seoul
South Korea
1 National Radio and Television Administration 2 Academy of Broadcast and Science commercia potential 3 Prasar Bharti working jointly with IIT Kanpur on Next Generation Broadcast Technology
Malaysia
2020+: Growing interest in 5G BC in addition to ATSC 3.0
2023: FCC Approves A Low Power TV Station To Broadcast Over 5G Networks
2023: First 5G Broadcast in the US and first 24/7 5G Broadcast globally
2024: Foundation of 5G Broadcast Collective
US
Philippines
2019-22: Direct to mobile Live TV/Radio in Manilla
South Africa
2019-20: Live testing of Rel-14 in Johannsburg
2022+: 5G Broadcast under investigation as latest broadcast technology
Russia
2022: Interest towards 5G BC during Mediterranean Games
France
2018-2022: Live testing of 5G BC in Paris
2024: Olympics
Belgium
2022-24: 5G BC imec.icon project with 2 HPHT sites
Finland
2019-22: TV delivery with Rel-14/16 HPHT in 3 sites
CZ
2020-23: Distribution of TV/Radio in Prague
2019-24: AIB project based on 5G Broadcast under the administration of NRTA1 and ABS2
2023: 5G Broadcast Chengdu pilot project formally kicked off on July 20th
GATIS' Global 5G Broadcast Summit
India
Denmark
Tour de France 22 powered by 5GB
Algeria
Greece
Croatia
2021-23: Live TV/Radio with 5G BC Rel-14/16 , with 3MHz in Athens
2022-24: Live 5G BC Rel-14/16
China
2024: Report completed – next steps are trials
Europe
2023: European broadcasters ink 5G Broadcast MoU
2024: European profile for 5G Broadcast receivers

## Slide 7: First 5G Broadcast in US
July 14th 2023 - FCC granted experimental license for 5G broadcast
Sep 13th 2023 – Station went on air and started 24/7 re-broadcast of FranceTV
Full leverage of existing infrastructure with no change in freq, antenna, power output
Successful indoor –stationary and outdoor – stationary and mobile reception with 8650 QRD units
Next steps: presentation to FCC, additional licenses for another 5-10 stations
Also emergency notification, first responder live trial, datacasting use cases
NAB 2024: Foundation of 5G Broadcast collective https://5gbc.tv/

## Slide 8
XGen Network LLC
Emergency Alerts/First Responder Solutions
Ancillary data delivery to road signs, particularly in emergencies
United States 5G Broadcast Proof of Concept 2
Priorities
Visit us at Booth 14.B18

## Slide 9: China Status
Chinese and international experts and scholars from Beihang University, Communication University of China (CUC), 5G-MAG, EBU, ORS, TDF, XGN, Rohde & Schwarz (R&S), Qualcomm, Xiaomi, vivo, Chengdu Kaiteng Sifang and Beijing BBEF Science & Technology
Sichuan has initiated the first trials and deployment of 5G Broadcast.
Regional broadcasters show great interests to duplicate the demo to verify & demo the 5GB services in their own network. Guangdong already asked, Guangxi is in the line, Shanxi also asked during the meeting, more requests are on the way.
ABS supports them together with domestic infra vendors and OEMs to launch pre-commercial trials
https://www.5g-mag.com/post/27-10-23-5g-mag-participates-at-gatis-summit

## Slide 10
What we have done for 5G Broadcasting
Successful Reception: 96%
(MCS9, 1 bit/s/Hz)
Location: setup at the top of Wutong Mountain
Power: 260W (four directions, about 65W for each one)
Field Test in Shenzhen
West Pearl Tower
Sichuan Radio and Television
Sichuan Radio and Television Bureau 702
Trial Network in Chengdu
NERC-DTV is working with some chip companies for the development of Individual receiver chip
显示处理
Receiver Chip
Individual receiver chip
NRTA has approved to set a trial network in Chengdu City, Sichuan Province

## Slide 11
5G Cellular
Network
5G Broadcast
Network
Internet
Linear TV
Radio
5G Phone
5G Phone
UHF band support
5G Cellular and
5G Broadcast
Converged Network
Linear TV
Radio
5G Phone
UHF band support
Internet
ATSC Broadcast
Network
Linear TV
Radio
ATSC TV
5G Cellular and
ATSC Broadcast
Converged Network
Linear TV
Radio
5G Phone
UHF band support
Internet
ATSC receiver
Supports:
Free-To-Air
No SIM operation
Rel-19 Work on non-3GPP Broadcast interworking
India
Samsung, Qualcomm, And Other Tech Giants Raise Concerns Over India’s Plan For Live TV On Smartphones
News

## Slide 12
2
FUTURE BROADCASTING STUDY WORKPLAN
Establishment of the study group for the Future Broadcasting Study
To publish a comprehensive report on the Future Broadcasting Study
To publish report on the outcomes of the Test-bed facility
To conduct a Test-bed facility to validate the use-cases
JAN - DEC 2023
JAN - DEC 2024
1
Collaboration Partner :
STAGE 1:
TERM OF REFERENCE (TOR)
STAGE 2:
ESTABLISHED STUDY GROUP
STAGE 3:
PUBLISH INDUSTRY
STUDY REPORT
STAGE 4:
ENGAGEMENT WITH INDUSTRY
STAGE 5:
TEST-BED SESSION
STAGE 6:
5G BROADCAST DAY SHOWCASE
STAGE 7:
ESTABLISH FINAL REPORT
2023
2024
Mar 2025
PHASE 1
PHASE 2
Malaysia

## Slide 13
WAY FORWARD OF 5G BROADCAST ACTIVITY
SITES
CENTRAL REGION
NOTE: Proposal only, subject to change
TO CONDUCT POC FOR 5G BROADCAST BUT SUBJECT TO THE SUCCESSFUL OUCTOMES OF TEST-BED SESSION
2025 -2026

## Slide 15
A France premiere… and a world premiere too !
Friendly users
2
Pop up store
0
20
devices
150
devices
Return in
Sept./Oct.
Street
demo
1
A running Live Test during Olympics with several objectives :
  A large coverage: Paris, Bordeaux, Nantes
  An end-to-end architecture
  ~150 Xiaomi smartphones distributed to the ecosystem
  The brand insTNT

## Slide 16
EXPERIMENTAL
MULTIPLEX
1 PAY TV
MULTIPLEX
5 Free TV
MULTIPLEX
SWITCH MUX
Free TV
channels
UHD T2/HEVC
2023
2025
2026
2027
2028
2029
2030
2024
SWITCH MUX
Free TV channels
5G Broadcast
Pay TV channels
SD/HD
Free TV channels
HD
SWITCH MUX
5G Broadcast roll out from 2028 in Exp. MUX then in another MUX to scale up with market adoption
UHD roll out in 2024 with adoption driven by Olympics Games
Free TV channels
HD+ / UHD
Free TV channels
5G Broadcast
TDF roadmap for France

## Slide 17: Promotion and other activities
IBC September 2024
  Demos
    Demos to showcase 5G Broadcast use cases (using current SW/HW in Qualcomm devices and rooted Xiaomi/OnePlus devices)
    DVB-I over 5G Broadcast demo at DVB booth (youtube.com)
    Significant interest from multiple companies for future technology demps: ATEME, XGeN Network, ORS, Sofia Digital Ltd., TDF, R&S, castLabs, Alicloud
  IBC Conference - Qualcomm involvement with 2 paper presentations and member of paper/program committee:
    Smart Introduction Of 5G Broadcast In Co-existence With Legacy Broadcast Systems (Javier Rodriguez Fernandez, Ayan Sengupta, Alberto Rico Alverino (Qualcomm Technologies Inc., San Diego, USA), Thomas Stockhammer (Qualcomm CDMA Technologies Gmbh, Munich, Germany))
    DVB-I Extensions and 3GPP Service URLs - Modernising Service Announcement and Discovery (Thomas Stockhammer (Qualcomm, Munich, Germany), Frederic Gabin (Dolby, Paris, France), Richard Bradbury (British Broadcasting Corporation, UK), Marc Hoffrichter (ZDF, Mainz, Germany), Daniel Silhavy (Fraunhofer FOKUS, Berlin, Germany))
  IEEE BTS "Mobile TV – Finally?" with focus on 5G Broadcast
    Program and presentations are available: https://bts.ieee.org/conferences-events/bts-international.html
    In Part 1, presentations from ATSC, DVB, TDF, 5G-MAG, Media Broadcast, Telecom Italia, et al.
    Part 2 round table discussion with implementers, regulators, BNOs, OEMs.
    Qualcomm involvement: Thomas organizer and panel moderator, Aytac part of panel
  FOBTV Meeting: update from around the world on broadcast
  Rohde &Schwarz partner event
  5G-MAG Insights with a dedicated session on 5G-Broadcast
SET Expo August 2024 Rio de Janeiro: Demo, Paper, Presentation, Panel
Further promotion expected in 2025 for MWC, NAB, IBC
detailed review tomorrow

## Slide 18: Summary Latest 5GBC Market & Ecosystem status
 | Recent developments
Europe | Summer Olympics trial by TDF 5G Broadcast receiver profile for EU released Media Broadcast 5GB signal on air in 5 German cities Communication with Xiaomi and Samsung PdM
China | China receiver profile from ABS Neuron 5GB SOC announcement RnS Broadcast core running on Alibaba cloud
India | Sinclair & Saankya announced development of devices with ATSC 3.0 for trials Engaged with TRAI, TEC for 5GB promotion Aligning with MNOs and mobile OEMs on the technology choice Newly formed group with MIB, DOT to deliberate and finalize D2M policy
Brazil | Briefed Ministry of Communication staff with 5GB 5GB demo, presentation/paper and panel at Set Expo Clear message that ATSC3.0 is not for mobile
USA | Handheld Nautiz X21 (QCM6490) will be enabled on B71 for XGN trials
Other regions | Trials in Mexico, Puerto Rico (Q1/25), Malaysia and Indonesia (H1/25)
OEM engagements | Enabled Xiaomi Mi13, Moto Edge, Moto Razor for demos New interest from Samsung Germany Enable Samsung S24 for demo at MWC25 Drive interest to Samsung HQ through local offices in France, Italy, Brazil and India
Infra engagements | Good number of broadcast core vendors claiming to be ready for commercial deployment: Syes, Tredess, Nakolos Engagement with Enensys and Digicap for ATSC 3.0 & 5GB harmonization

## Slide 19: Standardization – Where do we stand

## Slide 20
For more information on 5G broadcast standards…
ETSI TS 103 720: Profile of 3GPP specification containing the necessary parts to deploy 5G broadcast
TR 36.976: Overall description of enhanced TV (enTV) for 5G broadcast
Various specifications of 5G PHY supporting broadcast together with unicast in TS 36.211, 36.212, 36.213

## Slide 21: 5G Broadcast Standards Evolution
Rel-14
SCS1.25KHz/ CP=200µs Mobility up to 120 km/h
5G BC worldwide standard
TG6/1 and WP6A
Rel-16
Rooftop Mobility up to 250 km/h
5G BC is an EU standard (ETSI TS 103 720)
Rel-17 Enhanced BW= 6/7/8 MHz for UHF
Enhanced Version of ETSI TS 103 720v.1.2.1
Enhanced Version of ETSI TS 103 720v.1.3.1
Rel-18 Requirements for UHF band, URL Handling
Rel-19 work in planning (TFI, Co-existence, Low-Latency)
Where do we stand?
3GPP
3GPP
ITU
ETSI
3GPP
ETSI 5G-MAG
3GPP
2017
2020
2019
2020
06/22
06/23
06/25
12/23
ETSI 5G-MAG
3GPP
12/24

## Slide 22: RAN: MBMS  5G Broadcast Evolution
Mixed unicast/MBMS carrier
15 kHz numerology
Extended CP of 16.7us
Multi-cell transmission only (MBSFN)
Up to 60% of subframes for MBSFN transmission
Single-cell transmission (SC-PTM)
Transmission on PDSCH with new group identities
Non-synchronized transmitters
Longer cyclic prefixes for support of larger ISD
Up to 100% of subframes for MBSFN transmission on a dedicated carrier
Subframes fully dedicated to MBSFN transmission
Targeting rooftop and car-mounted antennas, handheld receivers
Release 9
Release 13
Release 14
> 15 km
“Operator controlled” MBMS
“Broadcaster controlled” MBMS
New numerologies to target rooftop reception with up to 125 km ISD
High mobility reception: fixed, portable and mobile receivers up to 250 km/h
Enhancements to CAS—increased PDCCH agg. Level, PBCH repetition, CFI in MIB
Release 16
6/7/8 MHz channel bandwidth to support common global channel bandwidth for broadcast systems
Introduction of UHF Band 108 to address RF transmitter and receiver requirements
Release 17/18

## Slide 23
B107 is not sufficient, I need the entire UHF band defined in 3GPP
ATSC3.0 the only reasonable course as the underlying nature of D2M
I am building a DVB-I large scale trial. How can we add 5G Broadcast?
5G Broadcast and unicast combined is a MUST including low latency
What features will be included in the first set of commercial chipsets?
How can we launch 5G Broadcast emergency services?
I may have a regulator requirement to distribute some ATSC signal on my broadcast carrier
I want to re-use my existing app/player

## Slide 24: Target Organizations
Qualcomm is engaged in global standardization ecosystem

## Slide 25
Details of the paper
Session and Recording

## Slide 26: Recap IBC 2023: 5G Broadcast, 3GPP and cellular modems
Broadcasting technologies traditionally use time & frequency interleavers to harness diversity
  3GPP cellular technologies “don’t need to” rely on interleavers due to additional diversity sources (e.g. HARQ feedback/retransmissions, spatial diversity, etc.)
Last year, we focused on
  1- How we could create “3GPP-modem-friendly” time and frequency interleavers
  2- How interleavers improve 5G Broadcast performance in different mobility scenarios
The big picture
3GPP Modem
UHF band support
CP
CB
CB 2
CB 1
…
CB 3
CP
Block
Block 2
Block 1
…
Block 2
rows
columns
input tones
Write row-wise
Read
col-wise
interleaved OFDM tones
Time interleaver
Frequency interleaver
Not specified for Rel. 19, may be standardized in the future in 3GPP or somewhere else

## Slide 27: Summary and Conclusions of Paper
5G BROADCAST RECEIVERS: OPTIMIZING PERFORMANCE UNDER IMPLEMENTATION CONSTRAINTS
Broadcast networks and usage of configurations needs to be done for worst-case scenario.
For example, gains achieved in the 120 kmph scenario may not relevant, if such a planning would fail to serve a large number of receivers moving at lower speeds.
In this case, comparison between 5G broadcast and ATSC3.0 is provided for NLOS for different speeds and configurations
The main design target & “reason for being” of 5G broadcast is to enable operation of a broadcast network where the receivers are hardware-compatible with cellular modems
  “Hardware compatible” means lower barrier to adoption in mobile devices compared to other broadcasting technologies
    Several 5G Broadcast building blocks are already there in a 4G/5G modem, hence the additions are marginal.
    For other technologies, a separate piece of silicon / die area would be required
In comparison with unconstrained broadcast designs, 5G Broadcast Rel-18 is only marginally worse
Address remaining gaps in Rel-19 without compromising the design goals implementing a Time-Frequency Interleaver re-using HARQ procedures
SNR for | ATSC 3.0 + 1Rx | ATSC 3.0 + 2Rx | 5G + 2Rx | 5G + 2Rx + TFI
3 kmph | 14.4 dB | 8.7 dB | 10.7 dB | 8.9 dB
40 kmph | 11.2 dB | 6.6 dB | 10.9 dB | 7.3 dB
120 kmph | 10.8 dB | 6.2 dB | 11.4 dB | 7 dB
Worst case | 14.4 dB | 8.7 dB | 11.4 dB | 8.9 dB

## Slide 28: Broadcast – 3GPP
Previously planned scope for Rel-19:
  Time-frequency interleaving
  “CAS muting”
Rel-19 work item rejected in September plenary due to objections of mainly Huawei and Samsung.
Current plan:
  Get more vocal supporters (XGN, BNE)
  Do pre-standard work in 5G-MAG (draft specs internally virtually completed - here) + LS to 3GPP
  Offline discussion with Samsung and Huawei
  Resubmit to December plenary for Rel-19
On the technical side, we also get infra vendors already implementing the feature in their products

## Slide 29
SET EXPO Paper August 2024

## Slide 30: 5G Broadcast and other radio technologies
5G Broadcast is generally not expected to be deployed as greenfield or as standalone technology
Cellular and
5G Broadcast
Converged – Apps and Devices
Linear TV
Radio
Cellular Modem
UHF band support
Internet
Technical aspects and opportunities of co-existence presented in the following
Notes: Motivation
  However, when introducing a new broadcast technology, the co-existence with and the migration from existing broadcast technologies is one of the most challenging efforts – also taking into account spectrum scarcity, the need to support legacy receivers, and regulatory constraints.
  Secondly, in the modern world of apps and software-based service layers, there exists a huge opportunity to share service layers across transport technologies including stationary and cellular unicast delivery, providing a unified and enhanced user experience. As 5G broadcast is decoupled from a specific service layer, unique and exciting co-existence scenarios exist.
  A third aspect is the deployment of 5G Broadcast jointly with unicast, including initial discussions on spectrum and technology requirements.

## Slide 31: #1: Sharing UHF Resources with legacy broadcast systems
Frequency Division Multiplex (FDM) on different carriers (see paper) or Time Division Multiplex (TDM) on the same carrier
CAS
PMCH
# 0
PMCH
# 1
…
…
CAS
CAS
PMCH
# 0
CAS-muted region
CAS-muted region
SIB-indication
5GB
Bootstrap | Preamble | ATSC Frame |  | Bootstrap | Preamble | ATSC Frame | 
min_time_to_next = [50ms; 5300ms]
P1
P2
# 0
Data
# 1
Data
# 3
P1
FEF Data
FEF frame starting with P1 symbol
1st DVB-T2 frame
1st FEF frame
(up to 250 ms T2-Base / 1s T2-Lite)
Data
# 0
P1
P2
# 0
Data
# 1
Data
# 3
Data
# 0
FEF Data
2nd DVB-T2 frame
P1
ATSC3.0 supports blanking
DVB-T2 support Future Extension Frames
5G Broadcast Rel-19 expected to support CAS muting

## Slide 32: ATSC 3.0 and 5G Broadcast in-band coexistence (NPP in ATSC)
Addresses regulatory constraints, i.e. the need to distribute a subset of services with ATSC
Flexible allocation of carrier bandwidth over different time spans across ATSC/5GB, for example:
  Over deployment maturity: gradually increasing the share for the new technology when new receivers get available
  Over time of the day. During commute morning and afternoon hours more mobile 5GB, evenings stationary TV users.
  based on consumption/metrics reporting: the share mobile vs stationary reception can dynamically be adjusted.
Coordinated transmission needed, proof-of-concepts and standards work ongoing
A novel opportunity to leverage the best of both technologies – with lots of deployment flexibility
B | P | ATSC Frame |  | B | P | ATSC Frame | 
Blanked for ATSC 3.0
min_time_to_next
CAS
PMCH
# 0
PMCH
# 1
…
…
CAS
CAS
PMCH
# 0
CAS-muted region
CAS-muted region
Blanked for ATSC 3.0
ATSC 3.0
5GB
SIB-indication
ATSC3.0
5G Broadcast
ATSC3.0
5G Broadcast
Note: TV supports ATSC, mobile 5GB

## Slide 33
5G Technology – convergence with broadcast
Sunday 15th 16:00-17:00 @ Conference Room 2

## Slide 34: #2: Unified Service Layer
5G Broadcast as transport-only technology can be integrated into existing service layers and apps => DVB-I + 5G Broadcast
Vision: DVB Service Layer (Codecs, Packaging, DRM, Service Announcement and Discovery, IP-based protocols) runs on top of any transport network, in particular 5G Unicast and 5G Broadcast
ETSI TR 103 972 (07/23): Deployment Guidelines for DVB-I services over 5G Systems  mostly plug and play leveraging DVB-I and 5G Broadcast APIs and reference points (see figure on the right-hand side)
specs completed in 3GPP, DVB, 5G-MAG, ETSI
Successful over-the-air demonstrations in 2024:
  DVB World (03/24): standalone DVB-I list over 5G Broadcast
  Media Web symposium (06/24): integrated into German DVB-I Pilot list as one service instance, fallback to unicast if out of coverage
  IBC 2024 – see DVB booth
Similar efforts started for ATSC3.0 integration

## Slide 35: DVB-I via 5G Broadcast
Using MBMS/5G Broadcast Reference Points and APIs
Different options are considered
  Using file download services for carouselling metadata
  Using segment streaming for DVB-DASH
  Using transparent mode for DVB-I multicast distribution
Combinations with unicast, hybrid services also under development
See details in ETSI TR 103 972
Expected to be supported by reference tools
Joint DVB/5G-MAG task force

## Slide 36
Qualcomm and Rohde & Schwarz show the world’s first standards-conforming demo of 5G Broadcast integrated into the DVB-I service framework on a commercial smartphone. 5G Broadcast transmissions from the Ismaning/Munich broadcast tower are added as service instance to a DVB-I service list and the DVB-I client is updated to select services included in the 5G Broadcast signals. The 5G Broadcast signals are integrated in the service list of the German DVB-I Pilot, whereby the instances for 5G Broadcast get highest priority and will hence be selected by the 5G Broadcast capable receivers, but ignored by regular TV sets or smartphones.
Joint demo of Rohde & Schwarz, Qualcomm and the colleagues from ZDF and ARD

## Slide 37
5G Technology – convergence with broadcast
Sunday 15th 16:00-17:00 @ Conference Room 2

## Slide 38: #3: 5G Broadcast combined with cellular unicast
Technical Enablers
  5G Broadcast (as a fully defined 3GPP technology) allows the coordination of frequency bands in uplink and downlink, and the concurrent processing of broadcast and unicast spectrum in same modem.
  Current commercial 3GPP modems already support simultaneous operation in multiple bands (dual-SIM and dual connectivity)
    Concurrent operation of 5G Broadcast and unicast is realized by leveraging the same mechanisms
    difference that one of the bands is a receive-only broadcast band (UHF is 3GPP Band 108).
Selected Opportunities
  Seamless coverage extension with unicast fallback (indoor, rural, etc.)
  Broadcast-on-demand: consumption and QoE metrics reporting allow a user-centric allocation of radio resources to specific programs
  User-targeted features: interactivity, DRM-protected content, targeted ads, personalization, accessibility, advanced media capabilities (HDR, VR, etc.)
  Re-use of existing apps – 5G Broadcast is a transport-only technology and supports improved quality, cost efficiency, and reliability.
  More rapid development and deployments (upgrades, app systems, etc.)
5G Broadcast is expected to be available as a new feature in mainstream mobile devices w/o comprising existing features
Broadcast
Cellular Modem
Internet
TV Application/Service Provider
Cellular unicast
High Power
High Tower
5G broadcast
TV/Media Application

## Slide 39: Selected use cases
Enhanced broadcast use cases with 5G broadcast
One-way communication directly to handsets
More cost efficient than unicast (RAN and CDN)
Live sports, special events, general programming
Key for massive events (e.g. World Cup)
Linear TV and Radio
Combine linear video with interactivity.
Linear content from broadcaster, unicast using mobile network.
Comments, ratings, e-commerce, advertising
Interactive media
Emergency notifications to smartphones from broadcast infrastructure.
Possibility of sending text-only notifications and multimedia content
Emergency messages
Software / firmware upgrades.
Download and storage of popular content:
  TV shows
  “Viral” videos in social media.
General file download
IBC 2024, Amsterdam, The Netherlands

## Slide 40: Emergency alerts
5G broadcast inherits from 5G the public warning system capabilities.
The Cell Broadcast Service (CBS) does not require authentication with a PLMN. Hence, a ROM network is inherently compatible with CBS (see 3GPP TS 23 041).
CMAS (commercial mobile alert system) is available in current commercial devices.
  Devices monitor periodically a low-duty cycle paging channel (low power)
  CMAS over 5G broadcast has been demonstrated with R&S infrastructure
Additional capabilities of CMAS:
  Geofencing (send notification to users within a given area)
  Possibility of sending URL linking to emergency media

## Slide 41: Emergency message demo with ABS
Self-contained emergency system (text + multimedia) without need of unicast.

## Slide 42: New version of ETSI TS 103 720
Qualcomm is rapporteur of work
Identified Work Topics by 5G-MAG
    DVB-I over 5G - add details to TS 103 720
    Band support for receivers including Band 108
    5G Broadcast as PWS Improvement
    Concurrent support of 5G Broadcast and 5G Unicast
    ETSI TS 103 720 V1.2.1 - Delivery of Warning Messages from MME to eNodeB
    Support of time-frequency interleaving (for improved performance in time/frequency selective channels)
    Support of coexistence with other broadcast technology in the same radio channel by TDM (for “soft refarming” and regulatory requirements)
    Clarification on features on handsets in Europe (Receiver profile)
    distributed vs. centralized MCE architecture
    Clarification on use of protocols and transparent mode
    URL handling for bootstrap of services
Other Potential topics:
  Service layer: low-latency, DRM, codecs, MBS Service layer, unicast repair
  Implementations: device APIs and interfaces, player optimizations, app integration
  Radio layer: RAN-only profile (transparent/group communication), Statistical multiplexing & power savings
Some of the work above relies on Rel-19 3GPP work in RAN and SA4
ETSI milestone | Target date
TB adoption of WI | 2024/10/10
Early Draft | 2024/12/31
Stable Draft | 2025/03/31
Draft for approval | 2025/04/15
TB approval | 2025/06/30
To be published as version: | V2.1.1 or v1.3.1
5G-MAG milestone | Target date
Initial ETSI Draft work item with at least 4 supporters | 2024/06/30
Agreed initial feature set for next release of ETSI spec | 2024/07/31
Agreed ETSI Draft work item with at least 4 supporters | 2024/08/31
Initial draft change requests for TS 103 720 | 2024/11/30
Stable draft change requests for TS 103 720 | 2024/12/20
Integrated version of change requests | 2024/12/31