## Slide 1: Enabling 5G Broadcast on Devices: Standards, Chipset and Global Adoption Path
5G Broadcast Conference
September 25, 2025
@qualcomm_tech
Dr. Thomas Stockhammer
Senior Director Technical Standards
Qualcomm Technologies

## Slide 2
5G Broadcast for Qualcomm
Standards
Technologies
Adoption Path

## Slide 3: 5G defines two modes of broadcast communication
Addressing diverse ecosystem, deployment, and use case requirements
5G broadcast
Mixed-mode multicast
Single Frequency Network (SFN) for downlink broadcast only
Dynamic switching between broadcast and unicast, e.g., SC-PTM1
Focus of this presentation
Operator spectrum (IMT)
Integration with unicast network
Efficient delivery of multicast/broadcast traffic (vs unicast)
Reuse of cellular infrastructure (low power).
Broadcast spectrum (e.g. UHF)
No unicast. Downlink – only traffic.
Delivery of linear content (e.g. TV) or IP file delivery
Dedicated broadcast infrastructure (can be high power)

## Slide 4: 5G Broadcast – Core Features for multiple use cases
SIM-less reception, Receive-Only Mode (ROM) & Free-to-Air (FTA)
Different spectrum options (e.g. UHF, SDL), as well as SFN/MFN
Various deployment possibilities (e.g. MNOs, BNOs)
Using existing infrastructure (HPHT, MPMT and LPLT)
Highly flexible velocities (up to 250 KM/h Vs up to 300 µS)
Can be combined with existing 4G and 5G features (unicast, PWS)
Performance en par and Co-existence with legacy broadcast

## Slide 5
Why 5G Broadcast for mobile?
Building block | Hardware (HW) / Software (SW) / Firmware (FW) | 5G Broadcast | Legacy Broadcast (DVB, ATSC, etc.)
RF | HW | Requires new components depending on supported band | 
OFDM IFFT | HW | Can reuse 4G/5G HW | May reuse 4G/5G HW
Searcher | HW / FW | Same as 4G/5G | Different
Tone/LLR mapping | HW | Same as 4G/5G | Different
Modulation de-mapper | HW | Same as 4G/5G | Different
Coding / packet segmentation | HW | Same as 4G/5G | Different
Scrambling | HW | Same as 4G/5G | Different
RAN protocol stack | SW | Same as 4G/5G | Different
5G Broadcast reuses several building blocks of 4G/5G cellular modem  it is a modem feature
5G Broadcast in a mobile device doesn’t require separate demodulator chip as is the case with other broadcast standards
A testament is the ability we can demonstrate 5G Broadcast in limited functionality with off the shelf phones
OnePlus 10 Pro
OnePlus 10T
Xiaomi Mi 13
Motorola Razr
Motorola Edge
More to be announced later in 2025 !

## Slide 6: Standardization and Technology updates

## Slide 7
For more information on 5G broadcast standards…
ETSI TS 103 720: Profile of 3GPP specification containing the necessary parts to deploy 5G broadcast
TR 36.976: Overall description of enhanced TV (enTV) for 5G broadcast
Various specifications of 5G PHY supporting broadcast together with unicast in TS 36.211, 36.212, 36.213

## Slide 8: 5G Broadcast Standards Evolution
Rel-14
SCS1.25KHz/ CP=200µs Mobility up to 120 km/h
5G BC worldwide standard
TG6/1 and WP6A
Rel-16
Rooftop Mobility up to 250 km/h
5G BC is an EU standard (ETSI TS 103 720)
Rel-17 Enhanced BW= 6/7/8 MHz for UHF
Enhanced Version of ETSI TS 103 720v.1.2.1
Enhanced Version of ETSI TS 103 720v.1.3.1
Rel-18 Requirements for UHF band, URL Handling
Rel-19 work (TFI, Co-existence, New bands)
Where do we stand?
3GPP
3GPP
ITU
ETSI
3GPP
ETSI 5G-MAG
3GPP
2017
2020
2019
2020
06/22
06/23
12/25
12/23
ETSI 5G-MAG
3GPP
06/25

## Slide 9: RAN: MBMS  5G Broadcast Evolution
Mixed unicast/MBMS carrier
15 kHz numerology
Extended CP of 16.7us
Multi-cell transmission only (MBSFN)
Up to 60% of subframes for MBSFN transmission
Single-cell transmission (SC-PTM)
Transmission on PDSCH with new group identities
Non-synchronized transmitters
Longer cyclic prefixes for support of larger ISD
Up to 100% of subframes for MBSFN transmission on a dedicated carrier
Subframes fully dedicated to MBSFN transmission
Targeting rooftop and car-mounted antennas, handheld receivers
Release 9
Release 13
Release 14
> 15 km
“Operator controlled” MBMS
“Broadcaster controlled” MBMS  5G Broadcast
New numerologies to target rooftop reception with up to 125 km ISD
High mobility reception: fixed, portable and mobile receivers up to 250 km/h
Enhancements to CAS—increased PDCCH agg. Level, PBCH repetition, CFI in MIB
Release 16
6/7/8 MHz channel bandwidth to support common global channel bandwidth for broadcast systems
Introduction of UHF Band 108 to address RF transmitter and receiver requirements
Release 18
CAS Muting for co-existence with legacy broadcast
Time-Frequency Interleaving coverage enhancements
Introduction of UHF Band 112 and 113 to support early deployments
Release 19

## Slide 10: 3GPP RAN Defined new Features For 5G Broadcast for Rel-19 in 2025
3
2

## Slide 11: Services: Re-use of existing apps and players
Application Processor
HLOS
MBMS Client
Re-usable components, device-internal interfaces and APIs, combination with advanced unicast technologies
Streaming App
File Download App
Streaming Service
File Download Service
Local HTTP Server
Service Discovery
File Repair
Reception Reporting
Object Distribution Function
FLUTE
Multimedia System
DASH Client
HTTP/TCP
IP Stack (with multicast)
eMBMS Service
I-1
I-2
I-4
5G Broadcast Feature
I-3
Transparent Service
Packet Distribution Function
FEC
Transparent
IPTV app
Service Discovery
NR/LTE/WiFi modems
IP Stack (unicast)
MBMS-APIs
Supported Features
Broadcast only playback
DASH and HLS Support
Seamless BC/UC switching
In-session repair
HTTPS support
DRM Support
Metrics/CMCD reporting
Ad Insertion
Lower Latency
Immersive Content
A/B Watermarking
And and and

## Slide 12: Supporting Organizations for Profiles and Services
Qualcomm is engaged in global standardization ecosystem

## Slide 13: Status of standards and multi-vendor interop
Modem
Service Layer
Feature complete with Rel-19
Profiling
Launch Profile stabilizing
Middleware and APIs specified
Testing and Interop
Network Interop (BNE) initiated
Device Interop (5G-MAG) in planning
Re-use of existing service layers and apps

## Slide 14: Adoption Path

## Slide 15
#FMT
5G Broadcast - Ready for launch?
Where: Main IBC Conference Center Room E102
When: Saturday, September 13, 12:15 - 13:00

## Slide 16
Infra vendor
SOC vendor
BNO
Broadcaster Content Owner
Consumer
Device vendor
Multi-vendor Interoperability
Johann Mika
CINO @ Big Blue Marble/ORS

## Slide 17
Infra vendor
SOC vendor
BNO
Broadcaster Content Owner
Consumer
Device vendor
Multi-Player Business Model
Markus Schneider
5G BC Business TF Media Broadcast
Aytac Biber
Qualcomm Product Management

## Slide 18: POPULATION COVERAGE PLANNING EU MARKETS COMBINED
Chart: 5GB Pop Deployment Timeline
| Q4 2026 | Q1 2027 | Q2 2027 | Q3 2027 | Q4 2027 | Q1 2028 | Q2 2028 | Q3 2028 | Q4 2028 | Q1 2029 | Q2 2029 | Q3 2029 | Q4 2029
Germany | 0.75 | 15.11 | 24.97 | 33.52 | 47.5 | 47.5 | 47.5 | 47.5 | 47.5 | 47.5 | 47.5 | 47.5 | 47.5
France | 0.25 | 0.25 | 0.25 | 0.25 | 0.25 | 19.23 | 30.28 | 38.27 | 42.96 | 42.96 | 42.96 | 42.96 | 42.96
Czechia | 0.15 | 0.15 | 0.15 | 2.21 | 4.19 | 4.19 | 4.19 | 4.19 | 4.19 | 4.19 | 4.19 | 4.19 | 4.19
Poland | 0.4 | 0.4 | 0.4 | 0.4 | 2.5 | 2.5 | 2.5 | 2.5 | 8.93 | 8.93 | 8.93 | 8.93 | 11.43
Belgium | 0 | 0 | 0 | 1 | 2 | 3 | 4 | 4.5 | 5 | 5 | 5 | 5 | 5
Italy | 0 | 0 | 0 | 0 | 0 | 3 | 7 | 10 | 13 | 16 | 16 | 16 | 16
Content Provider’s customers
OEM Devices
5G BC Pop Coverage
125M*
78%
39,2M**
*
All numbers are assumptions of major BNOs in their countries, based on the precondition of market readiness.
* Numbers for Italy refer to the pre-commercial transmissions started in 2024. No concrete plans yet in Italy.
** Current reports indicate that 40% of all streaming is performed on mobile devices

## Slide 19
Test platforms
Commercial Reference Design
CRD
n71 (617-698 MHz)
Qualcomm Reference Design
QRD
550Mhz and higher
Band 108 (470-698Mhz)
Band 107 (612-652Mhz)
Band 112 (470-608Mhz)
Band 113 (606-698Mhz)
3GPP defined receive-only broadcast bands
Notes: In Sept 2023 3GPP defined receive only Band 108 and 107 as broadcast bands which encompass all broadcast UHF channels utilized in Europe and elsewhere
And recently 3GPP defined additional sub bands with the thought that these subbands could help OEMs target certain regions, in the process expediting implementation of such subband in a mobile device.
NEXT
It is likely you came across and even worked on some of these test platforms.
First we have Qualcomm reference designs which are called QRD
We have both mobile and CPE form factors with these devices. These are our standard development platforms where we have more control on HW and SW aspects.
Since we have control on the RF front end we were able to modify the design to add support for higher 500Mhz band on these devices.
NEXT
As the number of partners interested in trialing 5G Broadcast grew we needed to find an alternative to get more devices that could be used for development. For that reason we looked at unlocked onePlus devices that had band71 support which overlaps with Band 107. We received permission from OnePlus and authorize two partners ORS and Rohde Schwarz to enable and distribute OnePlus devices to broadcast partners who could use Band71 for trials. Thanks to this program we were able to get development devices to many partners which we couldn’t help otherwise.
in summary we have QCOM official reference designs which we build in very small quantities with custom parts.
We use these devices to develop and demonstrate a brand new such as unicast+broadcast concurrency which would be missing on CRD devices or OEM devices.
Because of the scarcity of QRD devices we prefer using these devices when CRD devices are not viable to use for the targeted frequency band.
Anywhere else we could use band71 we prefer using CRD devices or OEM models I showed in previous slide as it provides better logistics.

## Slide 20
The core idea about handhelds for 5G Broadcast is the full integration of the modem with commercially large scale SOCs, such as those available in flagship devices from large OEMs. This makes 5G Broadcast a modem feature.
3GPP defines many features in each Release and a modem can only support a small subset, so features (and their detailed parameters) are selected by commercial needs and implementation complexity, area costs, etc.
5G Broadcast is defined such that the latter (implementation costs) are minimized by making the technology hardware-compatible with existing SoCs.
Acknowledging solidified plans from BNOs to start services in 2027, 5GB is a seriously considered feature (a "contender") for upcoming modems and scoping of the feature has started (identifying exact implementation requirements and costs).
Start of scoping is a result from consolidating business opportunities around the world. Moving forward, the process will continue by consolidating implementation requirements and business opportunities - in particular for OEMs to support the feature on their devices.
Anticipating leading Android OEMs to be in market with H1/2028 models, Qualcomm plans to support OEMs to meet their commercialization goals.
Typically, a major feature like 5GB arrives to flagship devices and waterfalls to lower tiers gradually. Anticipating SOCs for other form factors such as CPE, compute, automotive to follow in a waterfall fashion
The features to be added beyond what is already in the modem are primarily "receive-only", new frequency bands, new carrier bandwidths, concurrency with unicast, otherwise re-use.
We are on track on making 5G Broadcast a reality and attractive to Service Providers and OEMs. Standards/Engineering focus now on implementation support of scoped features: test transmitters, test cases, etc.

## Slide 22: General technology introduction
“5G broadcast” is a broadcasting standard defined by 3GPP (Release 16 - 2020)
  3GPP is the industry group responsible for defining global cellular tech standards (e.g. 4G / 5G)
  In the last few years 3GPP has expanded to new verticals (e.g. broadcast, automotive, satellite, etc.) hence it should not be regarded as a surprise that a broadcasting tech is coming out of 3GPP
Even though 5G Broadcast has been standardized by 3GPP, it is a broadcasting technology
  I.e. meant to be used by broadcasting operators, in broadcasting spectrum
  No need of supporting a unicast network. 5G Broadcast does not have anything to do with unicast
The main design target & “reason for being” of 5G broadcast is to enable operation of a broadcast network where the receivers are hardware-compatible with cellular modems
  “Hardware compatible” means lower barrier to adoption in mobile devices compared to other broadcasting technologies
    This is because several 5G Broadcast building blocks are already there in a 4G/5G modem, hence the additions are marginal.
    For other technologies, a separate piece of silicon / die area would be required
  To be clear, 5G Broadcast has nothing to do with “cellular operators trying to take over from broadcasters”
5G broadcast and 3GPP

## Slide 23: 5G Broadcast and other radio technologies
5G Broadcast is generally not expected to be deployed as greenfield or as standalone technology
Cellular and
5G Broadcast
Converged – Apps and Devices
Linear TV
Radio
Cellular Modem
UHF band support
Internet
Technical aspects and opportunities of co-existence presented in the following
Notes: Motivation
  However, when introducing a new broadcast technology, the co-existence with and the migration from existing broadcast technologies is one of the most challenging efforts – also taking into account spectrum scarcity, the need to support legacy receivers, and regulatory constraints.
  Secondly, in the modern world of apps and software-based service layers, there exists a huge opportunity to share service layers across transport technologies including stationary and cellular unicast delivery, providing a unified and enhanced user experience. As 5G broadcast is decoupled from a specific service layer, unique and exciting co-existence scenarios exist.
  A third aspect is the deployment of 5G Broadcast jointly with unicast, including initial discussions on spectrum and technology requirements.

## Slide 24: #1 Sharing UHF Resources with legacy broadcast systems
Frequency Division Multiplex (FDM) on different carriers or Time Division Multiplex (TDM) on the same carrier
CAS
PMCH
# 0
PMCH
# 1
…
…
CAS
CAS
PMCH
# 0
CAS-muted region
CAS-muted region
SIB-indication
5GB
Bootstrap | Preamble | ATSC Frame |  | Bootstrap | Preamble | ATSC Frame | 
min_time_to_next = [50ms; 5300ms]
P1
P2
# 0
Data
# 1
Data
# 3
P1
FEF Data
FEF frame starting with P1 symbol
1st DVB-T2 frame
1st FEF frame
(up to 250 ms T2-Base / 1s T2-Lite)
Data
# 0
P1
P2
# 0
Data
# 1
Data
# 3
Data
# 0
FEF Data
2nd DVB-T2 frame
P1
ATSC3.0 supports blanking
DVB-T2 support Future Extension Frames
Rel-19 now supports CAS muting

## Slide 25: #2: Unified Service Layer
5G Broadcast as transport-only technology can be integrated into existing service layers and apps => DVB-I + 5G Broadcast
Vision: DVB Service Layer (Codecs, Packaging, DRM, Service Announcement and Discovery, IP-based protocols) runs on top of any transport network, in particular 5G Unicast and 5G Broadcast
ETSI TR 103 972 (07/23): Deployment Guidelines for DVB-I services over 5G Systems  mostly plug and play leveraging DVB-I and 5G Broadcast APIs and reference points (see figure on the right-hand side)
specs completed in 3GPP, DVB, 5G-MAG, ETSI
Successful over-the-air demonstrations in 2024:
  DVB World (03/24): standalone DVB-I list over 5G Broadcast
  Media Web symposium (06/24): integrated into German DVB-I Pilot list as one service instance, fallback to unicast if out of coverage
  IBC 2024 at DVB booth and also shown at MWS
Similar efforts started for ATSC3.0 integration

## Slide 26: #3: 5G Broadcast combined with cellular unicast
Technical Enablers
  5G Broadcast (as a fully defined 3GPP technology) allows the coordination of frequency bands in uplink and downlink, and the concurrent processing of broadcast and unicast spectrum in same modem.
  Current commercial 3GPP modems already support simultaneous operation in multiple bands (dual-SIM and dual connectivity)
    Concurrent operation of 5G Broadcast and unicast is realized by leveraging the same mechanisms
    difference that one of the bands is a receive-only broadcast band (UHF is 3GPP Band 108).
Selected Opportunities
  Seamless coverage extension with unicast fallback (indoor, rural, etc.)
  Broadcast-on-demand: consumption and QoE metrics reporting allow a user-centric allocation of radio resources to specific programs
  User-targeted features: interactivity, DRM-protected content, targeted ads, personalization, accessibility, advanced media capabilities (HDR, VR, etc.)
  Re-use of existing apps – 5G Broadcast is a transport-only technology and supports improved quality, cost efficiency, and reliability.
  More rapid development and deployments (upgrades, app systems, etc.)
5G Broadcast is expected to be available as a new feature in mainstream mobile devices w/o comprising existing features
Broadcast
Cellular Modem
Internet
TV Application/Service Provider
Cellular unicast
High Power
High Tower
5G broadcast
TV/Media Application

## Slide 27: Trial Updates

## Slide 28
Trials and demonstrations - Europe
France
Germany
Italy
Czech Republic
UK
Austria
Spain
Greece
Estonia
2023: EU broadcasters signed MoU for 5G Broadcast for collaboration
2024: European 5G Broadcast Handset Taskforce released 5G Broadcast receiver profile for Europe
2018: First field trial in Aosta during Europe championship
2022: Demo on phones during Eurovision contest
2023: Test bed and field trials
2024-2025: Pre-commercial phase with live signal in 5 major cities
2024: large scale trial by TDF during Olympics using Xiaomi phones
2025: Additional tests for hybrid tests, interactivity, signal optimizations
2022: 5G VISTA project to study how 5G Broadcast could enable multi-angle HD streams with interactivity in stadiums
2028: TDF considering rolling out 5G Broadcast
2024: Live signal in 5 cities for advanced tests using Xiaomi phones and Qualcomm reference designs
2027: MediaBroadcast is planning to start commercial service
2022-2023: 5G Broadcast demonstrations at ISA and MWC shows with Cellnex Telecom
2025: 5G Broadcast trial in Valencia
2022: CRA ran 5G Broadcast tests in Prague
2024: CRA running new tests with SFN in two sites
2023: ORS used 5G Broadcast during MotoGP race
2022: Europe wide 5G broadcast trial delivering Eurovision in Italy, France, Germany, Austria
2023: Tested 5G Broadcast at Crevex 2023
2025: Further tests for alert functionality with integration to cell broadcast for news and critical updates
2021-2023: Live TV/Radio with 5G BC Rel-14/16 , with 3MHz in Athens

## Slide 29
Trials and demonstrations - Asia
China
India
Malaysia
Indonesia
2022-2024: Tech demonstrations at IMC and BES events
2025: Proposal to run trial on national broadcast network
2024 : Initial meeting led by Ministry of Communications and Information (MCI) to define next steps towards trial in 2025
2024: Malaysian Technical Standards Forum released future broadcasting study report setting the stage for 5G Broadcast
2024: Malaysian Communication and Multimedia Commission (MCMC) organized 5G Broadcast test-bed facility session with BNOs, MNOs, device manufacturers in preparation of large scale trial in 2025
2025: upcoming 5G Broadcast Conference in Malaysia, where we will be showcasing various potential use cases of 5G Broadcast technology and initiate large scale trial
2023: Chengdu pilot project with live TV and public warning messages
2023: Global 5G Broadcast Summit Forum hosted by GATIS
2024: First 5G Broadcast over Astrum, L-Band GEO satellite
2025: Extending to phase 2 with additional sites and additional states
Driving test @ 60Km/h
Emergency notifications

## Slide 30
Trials and demonstrations - Americas
USA
Mexico
Colombia
Brazil
2023: First experimental 5G Broadcast in Boston by XGN using existing infrastructure with no change in frequency, antenna, power output
2024-2025: XGN moved to Phase 2 and added three additional stations with experimental license to test SFN, emergency notifications, road sign update for emergency, first responder communication and channel bonding
2024: First demo with Moto Edge phones in Mexico City
2025: Larger trial covering center area of Mexico City
2020-2021: Delivery of TV and Radio with Rel-14 5G broadcast trial deployment in Santiago de Tolu
2024: First demonstration of 5G Broadcast combined with ISDB-T combined waveform
2023: Multi-angle 5G Broadcast demo during Rio Open
2024: Demo at Set Expo in collaboration between Claro, Globo, Motorola, Rohde & Schwarz and Qualcomm

## Slide 31: Selected use cases
Enhanced broadcast use cases with 5G broadcast
One-way communication directly to handsets
More cost efficient than unicast (RAN and CDN)
Live sports, special events, general programming
Key for massive events (e.g. World Cup)
Linear TV and Radio
Combine linear video with interactivity.
Linear content from broadcaster, unicast using mobile network.
Comments, ratings, e-commerce, advertising
Interactive media
Emergency notifications to smartphones from broadcast infrastructure.
Possibility of sending text-only notifications and multimedia content
Emergency messages
Software / firmware upgrades.
Download and storage of popular content:
  TV shows
  “Viral” videos in social media.
General file download
IBC 2024, Amsterdam, The Netherlands

## Slide 32
B107 is not sufficient, I need the entire UHF band defined in 3GPP
ATSC3.0 the only reasonable course as the underlying nature of D2M
I am building a DVB-I large scale trial. How can we add 5G Broadcast?
5G Broadcast and unicast combined is a MUST including low latency
What features will be included in the first set of commercial chipsets?
How can we launch 5G Broadcast emergency services?
I may have a regulator requirement to distribute some ATSC signal on my broadcast carrier
I want to re-use my existing app/player

## Slide 33: Re-use of existing apps and players & frequency switching
Re-usable components, device-internal interfaces and APIs, combination with advanced unicast technologies
Application Processor
Applications
Streaming App
File Download App
HLOS
MBMS Client
Streaming Service
File Download Service
Local DASH Server
Service Discovery
File Repair
Reception Reporting
Object Distribution Function
FLUTE
Multimedia System
DASH Client
HTTP/TCP
IP Stack (with multicast)
eMBMS Service
I-1
I-2
I-4
LTE Modem
I-3
Transparent Service
Group Communication
Packet Distribution Function
FEC
Transparent
IPTV app
Service Discovery
NR/LTE/WiFi
IP Stack (unicast)
Work in Progress
Broadcast only playback
DASH and HLS Support
Broadcast-unicast seamless switching
In-session repair
HTTPS support on local interface
DRM Support
Metrics/CMCD reporting
Ad Insertion
Lower Latency
Immersive Content
A/B Watermarking

## Slide 34: DVB-I via 5G Broadcast
Using MBMS/5G Broadcast Reference Points and APIs
Different options are considered
  Using file download services for carouselling metadata
  Using segment streaming for DVB-DASH
  Using transparent mode for DVB-I multicast distribution
Combinations with unicast, hybrid services also under development
See details in ETSI TR 103 972
Expected to be supported by reference tools
Joint DVB/5G-MAG task force

## Slide 35
3GPP SA4 Advanced Media Delivery
Common Client Metadata.
Common Server-and Network-Assisted Streaming.
Multi-Access Media Delivery.
Media Delivery from multiple service endpoints/location.
Modem Usage Optimized Media Streaming.
DASH/HLS Interoperability.
Further harmonization of RTC and Streaming for Advanced Media Delivery.
Improved QoS support for Media Streaming services.
QUIC-based segmented media delivery.
In-band signalling of QoS for 5G Media Streaming.
Dynamic content generation from multiple sources.
In-session Unicast Repair for MBS Object Distribution.
MBS User Service and Delivery Protocols for eMBMS.
Selected MBMS Functionalities not supported in MBS.
FS_AMD
Study completed in Dec ‘25 (stage 2) and Mar ‘25
Identified normative work
AMD-ARCH-MED
Stage-2 work for Streaming and MBS
Completed also in Mar 25
AMD_PRO-MED
Stage-3 Protocol work ongoing
Completion expected by Sep 25, open API Dec 25
More study topics for future Releases

## Slide 36: Unicast Broadcast Combinations
Application Providers
The selective requests may combine information in
  http headers, query strings, or based on a pattern in the request URL
  With information provided in the configuration information, for example a filter when to issue unicast requests
  Unicast requests may also be issued based on certain randomization
The selective requests may be forwarded as is, or may be modified by the MC/BC client
The configuration needs to take into account the ability to scale the unicast traffic
The MC/BC client issues selective requests for unicast based on information from the player and the configuration
Multicast Broadcast Client
Media Server SL1
Application
DASH or HLS Client (including multiple service locations)
MBMS-API
Potentially Request Data
Network Media Server (SL2)
Multicast Broadcast Network functions
Push resources
MC/BC Distribution
Policy Function
Configuration
Configuration
Unicast requests
Request Application Service Document
Service Location Steering Policy

## Slide 37: CMCD Adaptation to Multicast/Broadcast
In the case above case the general architecture and call flow is adapted to configure the DASH/HLS for CMCD data collection (e.g. in the manifest). The client requests data with CMCD configuration. The MC/BC client is configured accordingly to collects the data.
The MC/BC client provides the aggregated information to the network function, for example NWDAF – note that this would then align with unicast.
Application Providers
Multicast Broadcast Client
Media Server
Application
DASH or HLS Client
MBMS-API
Request Data including CMCD
MPD URL M3U8
Network Media Server
Multicast Broadcast Network functions
Push resources
MC/BC Distribution
Request and response function collecting CMCD data
Configuration (incl. CMCD data)
Configuration
Provided aggregated CMCD data to network, for example NWDAF
Manifest (incl. CMCD data collection configuration)

## Slide 38: In-session Repair Adaptation to Multicast/Broadcast
In the case above case the general architecture and call flow is adapted. The client requests data from unicast in case broadcast is failing/partial.
The MC/BC client uses the information to reconstruct the objects accordingly.
Application Providers
Multicast Broadcast Client
Media Server
Application
DASH or HLS Client
MBMS-API
Request Data
MPD URL M3U8
Network Media Server
Multicast Broadcast Network functions
Push resources
MC/BC Distribution
Request and response function
Configuration (incl. unicast config)
Configuration
Request data, potentially partially from unicast
Manifest

## Slide 39: Update for ETSI spec TS 103 720 v1.3.1 – Work Item in 5G-MAG and ETSI
39
IBC 2024
Aim:
Have an agreed work item for IBC 2024
Have a stable draft by May 2025
Have a stable version by September 2025 for IBC 2025
Milestone name | Target date
TB adoption of WI | 2024/08/31
Early Draft | 2025/04/30
Stable Draft | 2025/06/30
Draft for approval | 2025/08/15
TB approval | 2025/09/15
To be published as | V2.1.1 or v1.3.1

## Slide 40
Details of the paper
Session and Recording

## Slide 41: Recap IBC 2023: 5G Broadcast, 3GPP and cellular modems
Broadcasting technologies traditionally use time & frequency interleavers to harness diversity
  3GPP cellular technologies “don’t need to” rely on interleavers due to additional diversity sources (e.g. HARQ feedback/retransmissions, spatial diversity, etc.)
Last year, we focused on
  1- How we could create “3GPP-modem-friendly” time and frequency interleavers
  2- How interleavers improve 5G Broadcast performance in different mobility scenarios
The big picture
3GPP Modem
UHF band support
CP
CB
CB 2
CB 1
…
CB 3
CP
Block
Block 2
Block 1
…
Block 2
rows
columns
input tones
Write row-wise
Read
col-wise
interleaved OFDM tones
Time interleaver
Frequency interleaver
Now specified in Rel-19

## Slide 42: Summary and Conclusions of Paper
5G BROADCAST RECEIVERS: OPTIMIZING PERFORMANCE UNDER IMPLEMENTATION CONSTRAINTS
Broadcast networks and usage of configurations needs to be done for worst-case scenario.
For example, gains achieved in the 120 kmph scenario may not relevant, if such a planning would fail to serve a large number of receivers moving at lower speeds.
In this case, comparison between 5G broadcast and ATSC3.0 is provided for NLOS for different speeds and configurations
The main design target & “reason for being” of 5G broadcast is to enable operation of a broadcast network where the receivers are hardware-compatible with cellular modems
  “Hardware compatible” means lower barrier to adoption in mobile devices compared to other broadcasting technologies
    Several 5G Broadcast building blocks are already there in a 4G/5G modem, hence the additions are marginal.
    For other technologies, a separate piece of silicon / die area would be required
In comparison with unconstrained broadcast designs, 5G Broadcast Rel-18 is only marginally worse
Address remaining gaps in Rel-19 without compromising the design goals implementing a Time-Frequency Interleaver re-using HARQ procedures
SNR for | ATSC 3.0 + 1Rx | ATSC 3.0 + 2Rx | 5G + 2Rx | 5G + 2Rx + TFI
3 kmph | 14.4 dB | 8.7 dB | 10.7 dB | 8.9 dB
40 kmph | 11.2 dB | 6.6 dB | 10.9 dB | 7.3 dB
120 kmph | 10.8 dB | 6.2 dB | 11.4 dB | 7 dB
Worst case | 14.4 dB | 8.7 dB | 11.4 dB | 8.9 dB

## Slide 43
SET EXPO Paper August 2024
Also presented more details during IBC 2024 and NAB 2025