## Slide 1: DVB & 5G Broadcast: A dynamic duo
Moderator: Thomas Stockhammer (Qualcomm)
Presenters:
Johann Mika (Big Blue Marble/ORS)
Javier Rodriguez Fernandes (Qualcomm)

## Slide 2: Overview
Intro: 5G Broadcast at IBC#2025
5G Broadcast: Challenges from an operator POV (Johann)
DVB-T2 and 5G Broadcast on the same carrier (Javier)
Latest performance updates including TFI (Javier)
Demo (Johann and colleagues)

## Slide 3
#FMT
5G Broadcast - Ready for launch?
Where: Main IBC Conference Center Room E102
When: Saturday, September 13, 12:15 - 13:00

## Slide 4
Infra vendor
SOC vendor
BNO
Broadcaster Content Owner
Consumer
Device vendor
Multi-vendor Interoperability
Johann Mika
CINO @ Big Blue Marble/ORS

## Slide 5
Infra vendor
SOC vendor
BNO
Broadcaster Content Owner
Consumer
Device vendor
Multi-Player Business Model
Markus Schneider
5G BC Business TF Media Broadcast
Aytac Biber
Qualcomm Product Management

## Slide 6: POPULATION COVERAGE PLANNING EU MARKETS COMBINED
Chart: 5GB Pop Deployment Timeline
| Q4 2026 | Q1 2027 | Q2 2027 | Q3 2027 | Q4 2027 | Q1 2028 | Q2 2028 | Q3 2028 | Q4 2028 | Q1 2029 | Q2 2029 | Q3 2029 | Q4 2029
Germany | 0.75 | 15.11 | 24.97 | 33.52 | 47.5 | 47.5 | 47.5 | 47.5 | 47.5 | 47.5 | 47.5 | 47.5 | 47.5
France | 0.25 | 0.25 | 0.25 | 0.25 | 0.25 | 19.23 | 30.28 | 38.27 | 42.96 | 42.96 | 42.96 | 42.96 | 42.96
Czechia | 0.15 | 0.15 | 0.15 | 2.21 | 4.19 | 4.19 | 4.19 | 4.19 | 4.19 | 4.19 | 4.19 | 4.19 | 4.19
Poland | 0.4 | 0.4 | 0.4 | 0.4 | 2.5 | 2.5 | 2.5 | 2.5 | 8.93 | 8.93 | 8.93 | 8.93 | 11.43
Belgium | 0 | 0 | 0 | 1 | 2 | 3 | 4 | 4.5 | 5 | 5 | 5 | 5 | 5
Italy | 0 | 0 | 0 | 0 | 0 | 3 | 7 | 10 | 13 | 16 | 16 | 16 | 16
Content Provider’s customers
OEM Devices
5G BC Pop Coverage
125M*
78%
39,2M**
*
All numbers are assumptions of major BNOs in their countries, based on the precondition of market readiness.
* Numbers for Italy refer to the pre-commercial transmissions started in 2024. No concrete plans yet in Italy.
** Current reports indicate that 40% of all streaming is performed on mobile devices

## Slide 7
Outlook for Silicon and Commercial Device
5G Broadcast is considered a new feature for 3GPP cellular modem
No plan for broadcast-only silicon, feature is added to cellular modem
Major development to add bands, new numerology, concurrency etc.
Forward looking, feature only available with new released devices
Initial targets are Mobile and FWA devices with integrated and standalone modems
Feature scoping is underway
Business Case Development
Secure alignment with mobile OEMs on commercial feature set and availability
Launch timeline (Contingent on OEM alignment)
On track to support first wave of mobile devices in Q1/28
Test devices will be available to OEMs in Q3/27
Flagship phone models in first year
Waterfall to mid and low tier phone SOCs following years
Also, waterfalling to verticals like automotive
based on receiver profile established by 5G-MAG

## Slide 8
Frederico Siqueira (Minister of Communications of Brazil)
Wilson Wellisch (Secretário Nacional de Comunicação Social Eletrônica do Ministério das Comunicações)

## Slide 9
5G Broadcast Tests

## Slide 12: 5G defines two modes of broadcast communication
Addressing diverse ecosystem, deployment, and use case requirements
5G broadcast
Mixed-mode multicast
Single Frequency Network (SFN) for downlink broadcast only
Dynamic switching between broadcast and unicast, e.g., SC-PTM1
Focus of this presentation
Operator spectrum (IMT)
Integration with unicast network
Efficient delivery of multicast/broadcast traffic (vs unicast)
Reuse of cellular infrastructure (low power).
Broadcast spectrum (e.g. UHF)
No unicast. Downlink – only traffic.
Delivery of linear content (e.g. TV) or IP file delivery
Dedicated broadcast infrastructure (can be high power)

## Slide 13: 5G Broadcast – what is it?
Building upon a strong 3GPP technology foundation
eMBMS defined for LTE starting in Rel-8/Rel-9, improving coverage and efficiency
eMBMS enhancements in Rel-12 include MOOD and expansion to MCPTT
Enabling terrestrial broadcast and expanding to new services; Meeting 7/10 5G Broadcast requirements in Rel-14
LTE eMBMS/enTV
in 3GPP Rel-14
LTE
LTE-A
Further enhancements5
to fully satisfy 5G
broadcast requirements
5G
Target market focused on
Cellular operators
Target market expanded to
Broadcasters
3GPP Rel-14 (completed)
Enabling terrestrial broadcast and expanding to new services; Meeting all 5G Broadcast requirements in Rel-16
5G broadcast is a “broadcast standard” (same target as DVB or ATSC) based on 3GPP silicon and ecosystem.
3GPP could have taken a radical approach to define a clean slate radio system to meet the broadcasters’ requirements, instead a more pragmatic route was chosen. Experiences from the past with dedicated modems such as MediaFLO or DVB-H, and the need for easy integration into mainstream mobile devices, led to the decision to evolve eMBMS to LTE-based 5G Broadcast instead of any radical new designs.
3GPP Rel-16 (completed)
3GPP could have taken a radical approach to define a clean slate radio system to meet the broadcasters’ requirements, instead a more pragmatic route was chosen. Experiences from the past with dedicated modems such as MediaFLO or DVB-H, and the need for easy integration into mainstream mobile devices, led to the decision to evolve eMBMS to LTE-based 5G Broadcast instead of any radical new designs.

## Slide 14: RAN: MBMS  5G Broadcast Evolution
Mixed unicast/MBMS carrier
15 kHz numerology
Extended CP of 16.7us
Multi-cell transmission only (MBSFN)
Up to 60% of subframes for MBSFN transmission
Single-cell transmission (SC-PTM)
Transmission on PDSCH with new group identities
Non-synchronized transmitters
Longer cyclic prefixes for support of larger ISD
Up to 100% of subframes for MBSFN transmission on a dedicated carrier
Subframes fully dedicated to MBSFN transmission
Targeting rooftop and car-mounted antennas, handheld receivers
Release 9
Release 13
Release 14
> 15 km
“Operator controlled” MBMS
“Broadcaster controlled” MBMS
Release 16
6/7/8 MHz channel bandwidth to support common global channel bandwidth for broadcast systems
Introduction of UHF Band 108 to address RF transmitter and receiver requirements
Release 17/18
New numerologies to target rooftop reception with up to 125 km ISD
High mobility reception: fixed, portable and mobile receivers up to 250 km/h
Enhancements to CAS—increased PDCCH agg. Level, PBCH repetition, CFI in MIB
T/F interleaving for 1.25, 2.5, 7.5 and 15 kHz numerologies
CAS muting
Introduction of two new UHF subbands within Band 108
Release 19

## Slide 15: 5G Broadcast – Core Features for multiple use cases
SIM-less reception with simplified architecture
Receive-Only Mode (ROM) & Free-to-Air (FTA)
Different spectrum options (e.g. UHF, SDL), as well as SFN/MFN
Various deployment possibilities (e.g. MNOs, BNOs)
Using existing infrastructure (HPHT, MPMT and LPLT)
Highly flexible velocities (up to 250 km/h Vs up to 300 µs)
Can be combined with existing 4G and 5G features (e.g. unicast)
Flexible time interleaving depths and multiplexing patterns

## Slide 16: DVB & 5G Broadcast: A dynamic duo
Johann Mika, CINO

## Slide 17: 5G Broadcast: Challenges from an operator POV
Financial risk of deployment
Interoperability of infrastructure
Lack of customers (and devices)

## Slide 18: 5G Broadcast: Challenges from an operator POV
Goal: Reduce the investments at the beginning as much as possible
  Use of existing infrastructure: Co-existence of DVB and 5G Broadcast
  Increase the robustness of the signal: lower tower density and improved coverage  „Time-Frequency-Interleaving“
Financial risk of deployment
2024: Broadcast Networks Europe (BNE) joined efforts with EBU to engange in 3GPP for Release 19

## Slide 19: DVB & 5G Broadcast: Why Co-Existence Matters
The Challenges:
Spectrum scarcity: no new UHF bands available
Audiences split:
  Millions still rely on DVB-T2 TV sets
  Growing demand for mobile-first consumption (smartphones, cars, tablets)
Broadcasters need to innovate without disruption
Our Opportunity:
Use existing DVB-T2 capacity to introduce 5G Broadcast
Deliver TV + Mobile services in parallel on one RF channel

## Slide 20: 5G Broadcast: Why TFI matters
Robust Reception, Everywhere
Enhances coverage in challenging environments (urban canyons, indoor, high-speed mobility)
Consistent Quality of Service
Reduces risk of service degradation → fewer complaints from viewers
Efficient Deployment
Maximizes spectrum use by improving robustness without needing more transmit power or sites

## Slide 21: Bridging the broadcast and cellular worlds: CAS Muting and Time/Frequency Interleaving in Release 19 5G Broadcast
September 14th, 2025
IBC 2025
Javier Rodriguez-Fernandez, Senior Standards Engineer
Qualcomm Technologies, Inc.

## Slide 22: Convergence of broadcast and cellular

## Slide 23: Cellular unicast: mapping data (bits) to a subframe
Systematic bits (extremely important for decoding)
Parity bits (“less” important, used to correct errors)
1 subframe with 6 OFDM symbols
TB generation and subframe mapping in 3GPP
Input Transport Block (TB) with size TBS = 25456 bits
Segmentation, CRC, etc
Physical layer mapping (akin to DVB-T2, ATSC 3.0, etc.)
Taken from 3GPP TS 36.213
Modulation (e.g. 16-QAM), channel coding
Pilot (DMRS) pattern
HARQ buffer
Cellular unicast in 3GPP

## Slide 24: Time interleaving in 3GPP Release 19: continuous RVs
Time interleaving in Release 19
Baseline TBS = 25456 bits, TBs, RVs
Baseline TBS = 25456 bits, 𝑀 TBs, 𝑁 RVs
Scaling by a factor of and rounding => TBS = 101840 bits
Scaling by a factor of 𝑁=4 and rounding => TBS = 101840 bits
Transmit parts (RVs) of TBs over 16 subframes
Transmit parts (RVs) of 𝑀=4 TBs over 16 subframes
Systematic bits
Parity bits
5G Broadcast Rel. 19
RV#0 of 4 TBs
RV#1 of 4 TBs
RV#2 of 4 TBs
RV#3 of 4 TBs
Cellular unicast RVs
Firmware configuration
HW
HARQ Buffer
Input config
Start pointer
# bits
Output
011010101…0 ( bits)
Punctured bits
Time interleaving depth of
4 TBs x 4 RVs x 1 ms = 16 ms

## Slide 25: Performance analysis methodology

## Slide 26: OFDM allocation within 8 MHz channel BW
ATSC 3.0
2.8% Total guarband
.
.
6913 payload + pilot tones (7.78 MHz)
…
Different useful BW in 5GB and ATSC 3.0, and LLS operate on an average SNR per tone
  ATSC 3.0 power for the same system (i.e. SNR) quality
Measure performance over useful BW for each system => ATSC 3.0 still has an advantage due to e.g. more frequency diversity and extra coding rate
5G Broadcast
5760 PMCH + DMRS tones (7.2 MHz)
10% Total guarband
.
.
…

## Slide 27: Spectral efficiency computation
time interleaved (scaled) TBs
Each TB of size bits
Such TBs are collectively mapped to subframes
  Single OFDM symbol per subframe with 200/800 numerology (1.25 kHz SCS)
  Each OFDM symbol has PMCH + DMRS tones
(bps/Hz)
Spectral efficiency measured at 0.1% BLER
Same CP overhead and pilot pattern ratios
5G Broadcast
ATSC 3.0
Single PLP comprising multiple baseband packets after input formatting
  Such baseband packets collectively transport information bits
  The information bits are computed within the TI depth for each QAM size and code rate
Such baseband packets are time interleaved using CTI interleaving mode across several OFDM symbols
  Every OFDM symbol has 222.2/889 numerology (1.125 kHz SCS)
  Each OFDM symbol has payload plus pilot tones
(bps/Hz)
Spectral efficiency metric measures effective number of information bits that each standard can carry per time and frequency unit
Numerical simulations conducted for each MCS (i.e. QAM size, code rate, and corresponding TB / baseband packet size for 5G Broadcast and ATSC 3.0)

## Slide 28: Numerical performance

## Slide 29: Spectral efficiency results
Key takeaways at low speed (3 km/h)
  Performance improvement of 2-3 dB with respect to pre-Rel. 19 5GB
  Time-interleaved 5GB shows net performance gain of 0.5-1.2 dB over ATSC 3.0
  Extra time diversity outmatches NUC shaping and BICM gains
Key takeaways at higher speed (60 km/h)
  Performance improvement of 4-7 dB with respect to pre-Rel. 19 5GB
  Time-interleaved 5GB shows small gap of 0.5-1.5 dB versus ATSC 3.0
  Combination of continuous time interleaving + NUC shaping gain and BICM

## Slide 30: Convergence of broadcast standards: CAS muting

## Slide 31: CAS muting as a feature enabling co-existence
CAS
PMCH
# 0
PMCH
# 1
…
…
CAS
CAS
PMCH
# 0
CAS-muted region
SIB-indication of muting pattern
CAS muting
Enhancement
Now adopted as part of Release 19 features for 5G Broadcast
CAS
PMCH
# 0
PMCH
# 1
…
CAS
CAS
Rel. 18 5G Broadcast
PMCH
# 0
PMCH
# 1
…
“Always on” signal sync./scheduling
1ms
39ms
MBSFN subframes belonging to an MBSFN Area or empty
Main issue: Limited flexibility to transmit legacy standards in the “gap” (39 ms)
Example: ATSC’s recommended frame duration is 250 ms
…
PMCH
# 0
Multiples of ~40 ms

## Slide 32: DVB-T2 mechanisms for in-band coexistence
Super Frame
#
…
Super Frame
#
Super Frame
#
T2-frame
# 0
T2-frame
# A-1
FEF frame
# 0
…
FEF frame
# 1
T2-frame
# A
T2-frame
# A+B-1
…
FEF frame
# 2
T2-frame
# A+B
T2-frame
# A+B+C-1
…
FEF interval
FEF length
FEF interval
FEF length
FEF interval
FEF length
A
B
C
A + B + C = frames
A = B = C = FEF interval
DVB-T2 introduces FEF frames to enable coexistence with other broadcasting technologies
  L1-signaled FEF interval and FEF length would control the duty-cycle of DVB-T2 and 5G Broadcast
  Lots of flexibility to attain different time shares for DVB-T2 and 5G Broadcast
If T2-Lite is also deployed, both the Lite profile and 5G Broadcast can coexist with different time shares
FEF type (4 bits): reserved for future use
FEF interval (8 bits): up to 255 T2-frames
FEF length (22 bits): up to 250 ms / 1s
DVB-T2 supports Future Extension Frames (FEF)

## Slide 33: DVB-T2 and 5G Broadcast in-band coexistence
Efficient integration of 5G Broadcast within DVB-T2 superframes
T2-frame
P1
FEF Data containing
5G Broadcast traffic
FEF frame starting with P1 symbol
1st DVB-T2 frame
1st FEF frame
(up to 250 ms T2-Base / 1s T2-Lite)
5G Broadcast 40-ms-length frames
T2-frame
FEF Data containing
5G Broadcast traffic
2nd DVB-T2 frame
2nd FEF frame
(up to 250 ms T2-Base / 1s T2-Lite)
P1
CAS
PMCH
# 0
PMCH
# 1
…
…
CAS
CAS
PMCH
# 0
CAS-muted region
DVB-T2
5G Broadcast
DVB-T2
5G Broadcast
SIB-indication
DVB-T2 receivers expected to detect FEF frames and ignore the content of FEF data
  FEF frame starts with P1 symbol, which should be contained within the 5G Broadcast CAS-muted region
DVB-T2 receivers to keep AGC gain constant during FEF parts to avoid interference
DVB-T2 and 5G Broadcast transmitters need to coordinate for dynamic allocation of resources
DVB-T2
5GB
CAS-muted region

## Slide 34: Broadcaster and BNO Benefits
Service Continuity
Protect investments, no disruption to households with DVB-T2
Expanded Reach
Direct-to-mobile delivery: smartphones, vehicles, portable devices
Risk Mitigation
No need for full new multiplex rollout → lower upfront investment
 Allows smooth integration and lower pre-investment deployment scenarios for Broadcast Network Operators (and faster deployment of Public Warning Services)

## Slide 35: Worlds First: 5G Broadcast embedded in DVB-T2
Benefits for broadcasters and broadcast network operators:
• Service continuity
• Expanded reach
• Risk mitigation for early deployments
• New use cases
• Flexible multiplex transition strategies
Notes: • Service continuity: broadcasters can evolve their infrastructure without disrupting services to households still relying on DVB-T2.
• Expanded reach: 5G Broadcast enables direct-to-mobile content delivery (television, radio, streaming, ...), expanding the potential audience to include smartphones, tablets, and connected vehicles.
• Risk mitigation for early deployments: by using existing DVB-T2 infrastructure Example of co-existence of DVB-T2 and 5G Broadcast in which 5G Broadcast data is transmitted within FEF frames (as adapted from J. Rodriguez Fernandez, A. Sengupta, A. Rico Alvarino, T. Stockhammer, “Smart Introduction of 5G Broadcast in Co-existence with Legacy Broadcast Systems,” IBC Conference, Sep. 2024. instead of a complete roll-out of a new 5G Broadcast multiplex from day one, upfront investments can be reduced while mitigating business failure and other risks.
• New use cases: from live sports to emergency alerts and software updates, 5G Broadcast supports a range of new, f lexible services that are not supported in legacy systems.
• Flexible multiplex transition strategies: broadcasters can use free capacity in existing DVB-T2 carriers and gradually shift it from DVB-T2 to 5G Broadcast as device penetration increases and audience behaviour evolves.

## Slide 36: Worlds First: 5G Broadcast embedded in DVB-T2

## Slide 37: Worlds First: 5G Broadcast embedded in DVB-T2
Benefits for broadcasters and broadcast network operators:
• Service continuity
• Expanded reach
• Risk mitigation for early deployments
• New use cases
• Flexible multiplex transition strategies
Result: Ready-for-deployment coexistence model that proves DVB-T2 and 5G Broadcast can share the same carrier – ensuring compatibility today while unlocking innovation for tomorrow.
Notes: • Service continuity: broadcasters can evolve their infrastructure without disrupting services to households still relying on DVB-T2.
• Expanded reach: 5G Broadcast enables direct-to-mobile content delivery (television, radio, streaming, ...), expanding the potential audience to include smartphones, tablets, and connected vehicles.
• Risk mitigation for early deployments: by using existing DVB-T2 infrastructure Example of co-existence of DVB-T2 and 5G Broadcast in which 5G Broadcast data is transmitted within FEF frames (as adapted from J. Rodriguez Fernandez, A. Sengupta, A. Rico Alvarino, T. Stockhammer, “Smart Introduction of 5G Broadcast in Co-existence with Legacy Broadcast Systems,” IBC Conference, Sep. 2024. instead of a complete roll-out of a new 5G Broadcast multiplex from day one, upfront investments can be reduced while mitigating business failure and other risks.
• New use cases: from live sports to emergency alerts and software updates, 5G Broadcast supports a range of new, f lexible services that are not supported in legacy systems.
• Flexible multiplex transition strategies: broadcasters can use free capacity in existing DVB-T2 carriers and gradually shift it from DVB-T2 to 5G Broadcast as device penetration increases and audience behaviour evolves.

## Slide 38: Appendix: Simulation parameters

## Slide 39: Simulation parameters
Rx ant. related
[3] M. Fuentes, D. Mi, H. Chen, E. Garro, J. L. Carcel, D. Vargas,B. Mouhouche, and D. Gomez-Barquero, “Physical Layer PerformanceEvaluation of LTE-Advanced Pro Broadcast and ATSC 3.0 Systems,”IEEE Transactions on Broadcasting, vol. 65, no. 3, pp. 477–488, 2019.
[10] 3GPP, “3rd Generation Partnership Project; Technical SpecificationGroup Radio Access Network; Evolved Universal Terrestrial RadioAccess (E-UTRA); Physical layer procedures (Release 19),” 3GPP,Tech. Rep., Jun. 2025.
[16] 3GPP, “3rd Generation Partnership Project; Technical SpecificationGroup Radio Access Network; Evolved Universal Terrestrial Radio Ac-cess (E-UTRA); User Equipment (UE) radio transmission and reception(Release 18),” 3GPP, Tech. Rep., Jun. 2024.
BICM related
Time Intlv. related

## Slide 40: Appendix: Network planning

## Slide 41: Implications of different link budgets of 5G Broadcast and ATSC 3.0
ATSC 3.0
5GB
Network planning is usually carried out for the worst-case link-quality scenario
Worst-case link budget differences can be compensated by
  Introducing gap-fillers operating at another band
  Adjusting the MCS, transmit power
  Adjusting the video stream quality
Improving the corresponding standard to reduce link margin differences
Gap filler
Network planning targets worst-case scenario