## Slide 1: 5G Media: towards a universal Media Distribution Platform
November 28, 2023
ATSC PT-4
@qualcomm_tech
Dr. Thomas Stockhammer
Senior Director Technical Standards
Qualcomm Technologies

## Slide 2
About this talk
Presenter
Dr. Thomas Stockhammer
Senior Director, Technical Standards
Qualcomm Europe, Inc., IEEE Fellow
Leading and driving among others
DVB: 5G TF, DVB-I
MPEG: MPEG-I, CMAF and DASH
3GPP: XR over 5G, 5G Video, 5GMS
DASH-IF: Interop WG, Test
ETSI & 5G-MAG: 5G Broadcast and 5GMS
CTA WAVE: CMAF Device PB, Test
Metaverse Standards Forum: Chair, Board
# 3GPP and the Gs
# 5G Media Delivery
# Video Codecs in 3GPP
# XR and the Metaverse
# Beyond Rel-18
# Summary

## Slide 3: Mobile has made a leap every ~10 years
Mobile broadband and emerging expansion
2010s
Mobile broadband
LTE, LTE Advanced, Gigabit LTE
Focus shifts to mobile data
2000s
Wireless Internet
CDMA2000/EV-DO WCDMA/HSPA+,
Efficient voice to reach billions
1990s
Digital voice
D-AMPS, GSM, IS-95 (CDMA)
Mobile voice communication
1980s
Analog voice
AMPS, NMT, TACS
A unified connectivity platform
2020s
Connected intelligent edge
5G New Radio (NR)
The next innovation platform
2030s
Next-gen wireless
AI-native, new spectrum, RF sensing, and many more…
Notes: Key points:
Today you will hear how Qualcomm is going to deliver on the 5G vision, but first let's go back in history
Mobile has made a leap every approximately 10 years. 5G builds in these previous generation combined with continuous research and innovation
Detailed speaker notes
Qualcomm wants to take you to this new and amazing digitized world. A place where everyone and everything is intelligently connected.
But I want to show how Qualcomm is going to deliver on that vision by going back in history, as the origin of 5G started a long time ago.

## Slide 4: The telecom industry is based on technology standards
Standards are essential for commercializing new technologies
Inventions from early R&D need to be first standardized, e.g., 5G NR in 3GPP, before productization
Ensuring inter-vendor system interoperability
Vendors design and manufacture products adhering to standards, so products from one vendor can work seamlessly with ones from another — a cornerstone of global roaming
Spurring transparent and fair industry competition
Standards are available to anyone who wishes to access them; in many cases, they are free to download on the Internet (e.g., cellular standards
at www.3gpp.org)
Technology standardization is key
for an openly competitive ecosystem

## Slide 5
Foundation to “G” leadership is technology leadership
Early R&D and technology inventions essential to leading ecosystem forward
Proof-of-concept
Deliver end-to-end prototypes and impactful demonstrations
Vision
Identify a problem or need; establish requirements
Standardization
Drive e2e design with ecosystem and through standards process
Commercialization
Engage with global network operators to deploy new features with standards-compliant infrastructure and devices
Trials
Collaborate on OTA field trials that track 3GPP standardization and drive ecosystem towards rapid commercialization
Invention
Invent new technologies and e2e system architecture
New Wireless Generation
Confidential – Qualcomm Technologies, Inc. and/or its affiliated companies – May Contain Trade Secrets
~10 years

## Slide 6: 5G Media Delivery
Streaming, Broadcast and Real-time Communication

## Slide 7: Trends & News
Collected from Sandvine report, Bitmovin Developer report and Will Law from Akamai
Traffic
Mobile
Sports
Codecs
Monetization

## Slide 8: Multimedia Systems Technology and 3GPP SA4
Influencers and customers
SA4
SA1/2/RAN
?

## Slide 9: Rel-16 5G Media Streaming – The Idea
Approach:
  Framework aligned with today‘s OTTmedia distribution practices
  Supplementing MNO and third-party media services to easily access 5GS and 5GMS features
  Concrete instantiation for one or a small subset of recommended technologies (e.g. codecs, formats, etc.)

## Slide 10
Notes: 5G-MAG was instrumental to deliver an open-source platform for 5G Broadcast.
For target 2023, we in Qualcomm support the next steps in 5G-MAG Reference Tools to integrate 5G Broadcast with 5G Media Streaming.
As our first contribution to this exiting new project, we implemented basic 5G Media Streaming UE functions, the Media Session Handler and the Media Player, and connected to BBC‘s 5GMS network.
I hand over to my colleagues Weiyu and Shiling in China to explain more details..

## Slide 11
5G Content Provider UK
5G UE in China
5GMS-aware Application
Media Session Handler
Media Player
5GMS AS
5GMS AF
Select BBC
Access: http://5gms.bbc.uk/3gpp-m5/v2/service-access-information/d54a1fcc-d411-4e32-807b-2c60dbaeaf5f
JSON Response
{
"provisioningSessionId": "d54a1fcc-d411-4e32-807b-2c60dbaeaf5f",
"provisioningSessionType": "DOWNLINK",
"streamingAccess": {
"mediaPlayerEntry": "http://5gms.bbc.uk/m4d/provisioning-session-d54a1fcc-d411-4e32-807b-
2c60dbaeaf5f/Christmas-Greetings-to-5G-MAG.mpd"
}
}
Play BBC
GET X-MAS MPD
MPD Response
Notes: Hello, my name is Weiyu from Qualcomm China. I explain you the first handshake we did just a few days ago with the BBC 5GMS Network components you saw earlier.
We implemented initial functions of Media Session Handler and Media Player.
Here is our test app. Let us check the BBC Christmas Greetings.
[Click]
We send a 5GMS RESTful API call to the AF and get a 5G conforming JSON response.
The Media Session Handler instructs the media player to play the video and the Media Player gets the MPD from the AS.
[Click]

## Slide 12
5G Content Provider UK
5G UE in China
5GMS-aware Application
Media Session Handler
Media Player
5GMS AS
5GMS AF
MPD Response
<?xml version="1.0" ?>
<!-- MPD file BBC Christmas Greetings -->
<MPD xmlns="urn:mpeg:dash:schema:mpd:2011" minBufferTime="PT2S" type="static" mediaPresentationDuration="PT0H0M30S" maxSegmentDuration="PT0H0M2S" profiles="urn:mpeg:dash:profile:isoff-live:2011 ">
<Period duration="PT0H0M30.000S">
<AdaptationSet segmentAlignment="true" maxWidth="1920" maxHeight="1080" maxFrameRate="25" par="16:9" lang="und" startWithSAP="1" contentType="video" containerProfiles="'cmf2', 'cfhd'">
<SegmentTemplate media="1/$Time$.m4s" initialization="1/init.mp4" timescale="12800">
<SegmentTimeline>
<S t="0" d="25600" r="14"/>
</SegmentTimeline>
</SegmentTemplate>
<Representation id="1" mimeType="video/mp4" codecs="avc1.640028" width="1920" height="1080" frameRate="25" sar="1:1" bandwidth="5100000">
</Representation>
</AdaptationSet>
</Period>
</MPD>
GET X-MAS Segments
Segment Response
Monitor and Support
Notes: So let‘s unpack our Christmas present.
[Click]
We got a voucher for some Segments and we request those while 5GMS Control functions monitor the session.
[wait until the end of Richard‘s message]
Thank you Richard
[END]

## Slide 13: 5G Media Streaming Features for Rel-16
Only downlink features
Content Hosting
Network Assistance
Dynamic Policies
Consumption Reporting
Metrics Reporting

## Slide 14: 3GPP Specifications for Edge Enablers
SA6:
TS 23.558: Architecture for enabling Edge Applications
SA2:
TS 23.501: Policy and charging control framework for the 5G System (5GS); Stage 2
TS 23.548: 5G System Enhancements for Edge Computing; Stage 2
SA4:
TS 26.501: 5G Media Streaming (5GMS): General description and architecture
TS 26.512: 5G Media Streaming (5GMS): Protocols
CT1:
TS 24.558: Enabling Edge Applications: Protocol specification
CT3:
TS 29.558: Enabling Edge Applications; Application Programming Interface (API) specification; Stage 3

## Slide 15: Rel-17 5GMS and Edge
Building on EDGEAPP and other 3GPP work on edge
Application Provider Provisioning
  Define application needs for edge resource and QoS requirement templates
Network Assistance
  5GMS AF works with the MSH (in UE) to translate templates into actual allocations for a media session
  UE discovers Edge Server that meets the requirements and can server the application
Core Application: XR Split Rendering
Enabling MM services with stringent requirements
FS_EMSA
5GMS_EDGE
5GMS_EDGE_3
3GPP Release 17
EDGE_ENH?
3GPP Release 18+

## Slide 16: Rel-17 EVEX – Event Exposure
UEs can log and report a variety of useful information (e.g. QoE metrics, usage measurements, dynamic QoS/Charging policy invocations) to a Data Collection AF, for subsequent offering via Event Exposure services to external entities for device, network and service performance monitoring and data analytics
5G Core
NR/
gNB
Data Collection
Application Function
Application
Service
Provider
Media/Service
Content
Network &
Data Analytics
Function
UE Data Measurement / Reporting
Event Exposure
Service
Data Collection & Reporting Configuration
Provisioning Info
Media/Service
Content
Notes: So how does all this work in reality?
The edge cloud will augment on-device processing for boundless photorealistic XR
Looking at the animation [CLICK]
When the XR user moves his head, the on-device processing will determine the 6-DoF head pose and send it to the edge cloud through a low latency and high quality of service 5G link.
The edge cloud will use the head pose to partially render the next frame. The edge cloud capabilities will vary based on investment, but it should have racks of compute/CPU/GPUs to do photorealistic rendering. After quickly rendering the frame, the edge cloud will send the encoded data back to the XR headset.
The XR headset will decode the data, and based on the latest 6-DoF pose, which is being generated at a high frequency, the on-device processing will do any further rendering and adjustment to minimize motion-to-photon latency.
As you can imagine, making the XR experience truly immersive will require a system solution that guarantees low latency and high reliability. 5G is crucial for this. Depending on the distance from the edge cloud, the amount of edge cloud investment, the number of users, etc., the service may vary, but consumers can rest assured that the on-device XR capabilities will always be available.

## Slide 17: 5G Media Streaming and EVEX
Simplified version of TS 26.512 V17.1.0 figure 4.7.1-1

## Slide 18: 3GPP Specifications for Data Analysis and EVEX
SA2:
TS 23.288: Architecture enhancements for 5G System (5GS) to support network data analytics services
SA4:
TS 26.531: Data Collection and Reporting; General Description and Architecture
TS 26.532: Data Collection and Reporting; Protocols and Formats
TS 26.501: 5G Media Streaming (5GMS): General description and architecture
TS 26.512: 5G Media Streaming (5GMS): Protocols
CT3:
TS 29.517: 5G System; Application Function Event Exposure Service; Stage 3
TS 29.520: 5G System; Network Data Analytics Services; Stage 3
TS 29.522: 5G System: Network Exposure Function Northbound APIs; Stage 3
TS 29.591: 5G System; Network Exposure Function Southbound Services; Stage 3

## Slide 19: 5G defines two modes of broadcast communication
Addressing diverse ecosystem, deployment, and use case requirements
5G broadcast
Mixed-mode multicast
Single Frequency Network (SFN) for downlink broadcast only
Dynamic switching between broadcast and unicast, e.g., SC-PTM1
Focus of this presentation
Operator spectrum (IMT)
Integration with unicast network
Efficient delivery of multicast/broadcast traffic (vs unicast)
Reuse of cellular infrastructure (low power).
Broadcast spectrum (e.g. UHF)
No unicast. Downlink – only traffic.
Delivery of linear content (e.g. TV) or IP file delivery
Dedicated broadcast infrastructure (can be high power)

## Slide 20: General technology introduction
“5G broadcast” is a broadcasting standard defined by 3GPP (Release 16 - 2020)
  3GPP is the industry group responsible for defining global cellular tech standards (e.g. 4G / 5G)
  In the last few years 3GPP has expanded to new verticals (e.g. broadcast, automotive, satellite, etc.) hence it should not be regarded as a surprise that a broadcasting tech is coming out of 3GPP
Even though 5G Broadcast has been standardized by 3GPP, it is a broadcasting technology
  I.e. meant to be used by broadcasting operators, in broadcasting spectrum
  No need of supporting a unicast network. 5G Broadcast does not have anything to do with unicast
The main design target & “reason for being” of 5G broadcast is to enable operation of a broadcast network where the receivers are hardware-compatible with cellular modems
  “Hardware compatible” means lower barrier to adoption in mobile devices compared to other broadcasting technologies
    This is because several 5G Broadcast building blocks are already there in a 4G/5G modem, hence the additions are marginal.
    For other technologies, a separate piece of silicon / die area would be required
  To be clear, 5G Broadcast has nothing to do with “cellular operators trying to take over from broadcasters”
5G broadcast and 3GPP

## Slide 21
Significant interests towards 5G broadcast deployment worldwide
2020-22: 5G Media2Go Stuttgart/Heilbronn
2017-20: 5G Today in Bavaria
Germany
2020-22: VISTA Project with O2 Virgin Media
UK
2020: Distribution of free-to-air linear radio and TV using Rel-14 enTV with HPHT in Barcelona
2022 & 2023: MWC demos
Spain
2020-21: Delivery of TV and radio with Rel-14 broadcast trial deployment in Santiago de Tolú
Colombia
2020-23: TV 3.0 project calling for proposals
Brazil
2018-23: TV delivery with Rel-14/16 HPHT in Aosta and Turin
Italy
2020-23: Distribution of TV/Radio with 5G BC Rel-14/16 , with eMBB in Vienna
Austria
2020+: Growing interest in latest broadcast3 technologies
2023: Discussion on DTM strategy based on market feedback
Late 2021: Distribution of live TV using Rel-16 enTV near Seoul
South Korea
1 National Radio and Television Administration 2 Academy of Broadcast and Science commercia potential 3 Prasar Bharti working jointly with IIT Kanpur on Next Generation Broadcast Technology
Malaysia
2020+: Growing interest in 5G BC in addition to ATSC3.0
2023: FCC Approves A Low Power TV Station To Broadcast Over 5G Networks
2023: First 5G Broadcast in the US and first 24/7 5G Broadcast station in the world on WWOO, Boston, MA!
US
Philippines
2019-22: Direct to mobile Live TV/Radio in Manilla
South Africa
2019-20: Live testing of Rel-14 in Johannsburg
2022+: 5G Broadcast under investigation as latest broadcast technology
Russia
2022: Interest towards 5G BC during Mediterranean Games
France
2018-2022: Live testing of 5G BC in Paris
Belgium
2022-24: 5G BC imec.icon project with 2 HPHT sites
Finland
2019-22: TV delivery with Rel-14/16 HPHT in 3 sites
CZ
2020-23: Distribution of TV/Radio in Prague
2019-24: AIB project based on 5G Broadcast under the administration of NRTA1 and ABS2
2023: 5G Broadcast Chengdu pilot project formally kicked off on July 20th
GATIS' Global 5G Broadcast Summit
India
Denmark
Tour de France 22 powered by 5GB
Algeria
Greece
Croatia
2021-23: Live TV/Radio with 5G BC Rel-14/16 , with 3MHz in Athens
2022-24: Live 5G BC Rel-14/16
China
2023: Workshop on future of Broadcast and draft report will be available
Europe
2023: European broadcasters ink 5G Broadcast MoU

## Slide 22: Selected use cases
Enhanced broadcast use cases with 5G broadcast
One-way communication directly to handsets
More cost efficient than unicast (RAN and CDN)
Live sports, special events, general programming
Key for massive events (e.g. World Cup)
Linear TV and Radio
Combine linear video with interactivity.
Linear content from broadcaster, unicast using mobile network.
Comments, ratings, e-commerce, advertising
Interactive media
Emergency notifications to smartphones from broadcast infrastructure.
Possibility of sending text-only notifications and multimedia content
Emergency messages
Software / firmware upgrades.
Download and storage of popular content:
  TV shows
  “Viral” videos in social media.
General file download

## Slide 23: Coexistence of ATSC 3.0 & 5G Broadcast
5G Broadcast can be deployed by broadcasters in the exact same way as ATSC, and it greatly lowers the barrier to adoption in mobile devices since it is “only” an incremental feature to the 4G/5G modem
  Native broadcasting technologies like ATSC or DVB were never successfully incorporated in mobile devices at scale because their inclusion requires a separate piece of silicon (similar to, say, WiFi or GPS) and the ecosystem never took off
We could make use of the “reserved” frames of ATSC 3.0 to “superimpose” 5G Broadcast, thus achieving coexistence on the same channel
  An alternative would be for ATSC 3.0 and 5G Broadcast to coexist on two different frequencies, i.e. one MUX for each
The same broadcaster could thus deploy & operate both technologies at the same time
  ATSC 3.0 for fixed devices
  5G Broadcast for mobile devices
Documented in ATSC TG3-11
Rel-19 candidate work for 3GPP
ATSC 3.0 & 5G Broadcast can coexist: it does not have to be a either/or
Work Item in ATSC und 3GPP under preparation

## Slide 24: DVB-I via 5G Broadcast
Using MBMS/5G Broadcast Reference Points and APIs
Different options are considered
  Using file download services for carouselling metadata
  Using segment streaming for DVB-DASH
  Using transparent mode for DVB-I multicast distribution
Combinations with unicast, hybrid services also under development
See details in ETSI TR 103 972
Expected to be supported by reference tools
Joint DVB/5G-MAG task force

## Slide 25: Hybrid Unicast Broadcast
Content Provider may leverage 5G Unicast systems, 5G Broadcast systems, and 5G devices to build efficient and innovative applications
Supported by well defined network and client-side APIs
Examples:
  Hybrid Services
  Universal Coverage
  Broadcast on Demand
Integrated into 3GPP 5G specs, ETSI TS 103 720 and TR 103 972 (DVB over 5G)
Architectures, Collaboration Models and Use Cases
5G Broadcast Operator
Content Provider
5G MNO

## Slide 27: 5G defines two modes of broadcast communication
Addressing diverse ecosystem, deployment, and use case requirements
5G broadcast
5MBS: Mixed-mode multicast
Single Frequency Network (SFN) for downlink broadcast only
Dynamic switching between broadcast and unicast, e.g., SC-PTM1
Focus of this presentation
Operator spectrum (IMT)
Integration with unicast network
Efficient delivery of multicast/broadcast traffic (vs unicast)
Reuse of cellular infrastructure (low power).
Broadcast spectrum (e.g. UHF)
No unicast. Downlink – only traffic.
Delivery of linear content (e.g. TV) or IP file delivery
Dedicated broadcast infrastructure (can be high power)

## Slide 28: Multicast–Broadcast Services system architecture
Based on TS 23.247 V17.2.0 figure 5.1-1

## Slide 29: Multicast–Broadcast Services system architecture
Based on TS 23.247 V17.2.0 figure 5.1-2

## Slide 30: MBS User Service Architecture
User Service Announcement
  Aligned with MBMS User Service principles
  Simplified
  Modernized protocols
Object Distribution
  Single file delivery.
  Package Delivery
  Object Carouselling
  Real-Time Object Streaming DASH/HLS/CMAF
Packet Distribution
  Forward-only (tunnel)
  Proxy mode (UDP payload)
Associated Services
See TS 26.502 Figure 4.3.1-1

## Slide 31: Rel-18 5GMS feature overview
Extensive studies documented in TR26.804 result in the following updates
Consistent support for uplink streaming
End-to-end low latency live streaming with dynamic policies
5GMS over MBS and 5GMS hybrid unicast/MBS services.
Based on development in CTA WAVE in context of DASH/HLS interop specification in CTA-5005, it was identified that the same media service may be available in multiple formats, and 5GMS media is expected to offer the same service with different entry points in order for the device to select the service based on its capabilities, for example using a DASH player, or and HLS player, or using a progressive download system.
The 5G System offers different solutions for traffic identification and traffic detection. Traffic identification is essential so that the 5G System can detect application flows to which, for instance, an appropriate Policy and Charging Rule (PCC) is applied. 5GMS is extended to support the configuration of ToS values for the identification of traffic associated with a Dynamic Policy. and study use-cases with IPsec and the usage of the security parameter index for traffic identification.
The Quick UDP Internet Connection (QUIC) [43] and HTTP/3 protocols are among the most recent developments in the IETF, with the goal of combining flexibility, extensibility, and performance to web applications. The 5GMS specifications are updated to allow the use of HTTP/3 at relevant reference points in the 5GMS architecture.
Background data transfer (BDT)
Specification of the usage of Oauth 2.0 for 5GMS protocols based on the conclusions to address use-cases, when a UE hosts multiple 5GMS-Aware Applications from different 5GMS Application Providers.
Specifications for the 3GPP Service Handler and URL including the necessary functions on UE and device to support automatic launch of 5G System services in the context of 5G Media Streaming. It was identified that it is essential to provide a URL form for media services in order to automatically launch client and network functions without disrupting existing app workflows.
Specification of a RESTful API at reference point M3, for the configuration of 5GMS AS instances by 5GMS AF. M3 was undefined until now, but based on deployment experience it was identified that it is necessary to define this reference point more details.
Specification of data types for data reporting of ANBR-based Network Assistance invocations and specification of data types for exposure of events relating to invocation of AF-based and ANBR-based Network Assistance.
Enhancements based on feedback from 5G-MAG Reference tool developments. The support of 5G-MAG reference tools created essential inputs to the spec development and continuous exchange will result in additional updates.
this functionality is needed for media production services, but also for contributing user generated media to operator and third-party services. Different collaboration scenarios between the MNO and the service provider are addressed in an updated specification – bringing uplink streaming on par with downlink streaming.
is of crucial support to meet the TV industry needs in order to bring 5G on par with other distribution means. Live TV services are characterized by at least the following aspects: (1) scalability (in terms of concurrent users), (2) consistent quality, (3) high bandwidth requirements, (4) target latency constraints, and advanced TV Experiences. Primarily, updated DASH tools, QoE monitoring and QoS support for low-latency in 5G media streaming are specified in order to meet the requirements defined in TR 26.804.
This functionality is expected to allow scaling media services using multicast and point-to-multipoint distribution within the operators network.
Multiple Service Entry Points
Traffic Identification
QUIC and HTTP/3
enables mobile network operators to incentivize the offloading of traffic into off-peak hours with the aim of reducing network congestion during peak hours. Applications may register their interest in receiving content using BDT. The 5GMS specifications will be updated with the necessary parameter extensions to the M1, M5, and M6 reference points to provide access to BDT.
Oauth 2.0
3GPP Service URL Handling
Application Server Configuration
EVEX data types for ANBR-based Network Assistance
Support for 5G-MAG Reference Tools

## Slide 32: 5GMS via MBS
Abstract the distribution complexity for third party service provider
Different collaboration models
Unicast/Multicast combinations
Stage-3 still to be developed
See TS 26.501, Figure 4.9.1-1

## Slide 33: Launching a dedicated 5G System function on device
Unclear how this can happen consistently

## Slide 34: Service URL Handling
Add a 3GPP Service and URL Handler in the UE and the network as part of Media Session Handler and AF
Address provisioning, message exchange and call flows in order to support different use cases, namely the case for which the URL is resolved in the network, the URL is resolved in the UE, and the case for which the URL is resolved in a combination of network and UE.
Specify a concrete URL format for 3GPP services and reserve a URL prefix (e.g. services.3gpp.org) for 3GPP Services as part of 3GPP specifications, and ensure that this can be used in the context of 3GPP-based services, namely:
  Verify ownership of the domain through one of the Android website association methods.
  Create a suitable website redirection mechanism in case the application is not available on the device.
Specify 3GPP Service URL instantiations with parameters suitable for launching at least the Media Session Handler for 5G Media Streaming, MBMS Client (including Receive-Only Mode services) and MBS Client.
Provide the ability for a 5GMS-Aware application to create a Service URL to bootstrap 5G Media Delivery.
Address the provisioning of optional service parameters.

## Slide 35: Specific case: 5G Broadcast + CMAS Alert
Scenario

## Slide 36: 5G Media Delivery: Downlink and Uplink Streaming & RTC
Part of Rel-18 Work Items  Creation of a common specification TS 26.510 for Session Handling
Similarity of the 5GMS architecture and the Real-Time Communication (RTC) defined in TS 26.506
Feature | Downlink media streaming | Uplink media streaming | Real-time communication
Media Delivery Functions and Protocols |  |  | 
CMAF | Yes | yes | No
DASH/HLS | Yes | No | No
MP4 | Yes | No | No
RTP/AVP | Not until now | Not until now | No
webRTC | Not until now | Not until now | yes
HTTP/1.1 and TCP/IP | Yes | Yes | No
HTTP/2 | Yes | Yes | No
HTTP/3 and QUIC | Yes | Yes | No
UDP/IP | Yes | Yes | yes
Media Handling Functions |  |  | 
Service Access | Yes | Yes | Yes
Content hosting | Yes | No | ???
Content publishing | No | Yes | ???
Content preparation | Yes | No | ???
Network assistance | Yes | Yes | Yes
Dynamic policies | Yes | Yes | Yes
Remote control | No | Yes | ???
Consumption reporting | Yes | No | Yes
QoE metrics reporting | Yes | ??? | ???
Service URL Handling | Yes | Yes | Yes
Edge Computing | Yes | Yes | Yes
eMBMS delivery | Yes | No | ???
Data Collection | Yes | ??? | ???
MBS delivery | Yes | No | ???

## Slide 37: Tools in action …
5G-MAG @ IBC 2022
Nakolos (ORS/Bitstem)
BBC
Find information at developer.5g-mag.com

## Slide 38: Video Codecs in 3GPP
Streaming, Broadcast and Real-time Communication

## Slide 39: Summary of Codec Capabilities in 3GPP
TV Video Profiles TS 26.116, 5G Media Streaming TS 26.511, MTSI TS 26.114
Operation Point name | Video Codec | Profile | Tier | Level
H.264/AVC 720p HD | AVC | High | - | 3.1
H.265/HEVC 720p HD | HEVC | Main | Main | 3.1
H.264/AVC Full HD | AVC | High | - | 4.2
H.265/HEVC Full HD | HEVC | Main 10 | Main | 4.1
H.265/HEVC UHD | HEVC | Main 10 | Main | 5.1
H.265/HEVC Full HD HDR | HEVC | Main 10 | Main | 4.1
H.265/HEVC UHD HDR | HEVC | Main 10 | Main | 5.1
H.265/HEVC Full HD HDR HLG | HEVC | Main 10 | Main | 4.1
H.265/HEVC UHD HDR HLG | HEVC | Main 10 | Main | 5.1
H.265/HEVC 8K | HEVC | Main 10 | Main | 6.1
Alignment with mobile product roadmaps is driving 3GPP video specifications

## Slide 40: 3GPP 5G Video Characterization TR 26.955 approved at SA#96 (June 2022)
Feasibility Study in Rel-17

## Slide 41: Scenarios
Scenarios are defined
  to identify how video codecs are typically used in 5G type of services
  To define reference sequences (types and formats), decoding & encoding constraints
Defined Scenarios
  Scenario 1: Full HD Streaming
  Scenario 2: 4K-TV
  Scenario 3: Screen Content Scenario
  Scenario 4: Messaging and Social Sharing
  Scenario 5: Online Gaming
Note: 8K scenario discussed, but not added

## Slide 42: Anchor Generation for each Scenario
Reference Sequence
Anchor Configuration
Anchor Bitstream
Anchor Sequence
Metrics Computation
Reference Software
Encoder
Conforming
Decoder
Anchor Metrics
All sequences are available here https://dash-large-files.akamaized.net/WAVE/3GPP/5GVideo/ReferenceSequences/
All metrics, anchors and tests are available here: https://dash-large-files.akamaized.net/WAVE/3GPP/5GVideo/Bitstreams/
Scripts for running anchor and test generation, metrics generation as well as verification is provided here: https://github.com/haudiobe/5GVideo/

## Slide 43: Characterization
Characterization is the comparison of a codec under test with an anchor based on the framework introduced in this clause. Characterization in this report is based on Bjöntegard-Delta (BD)-rate.
A full characterization of a codec for a scenario against a 3GPP codec shall provide at least the following metrics
  The BD-rate gain for each defined anchor tuple and each required metric
  The average BD-rate gain across all anchors of the scenario for each required metric.

## Slide 44: Summary in 2022
H.265/HEVC
  No functional deficiencies or gaps, no lack any relevant features.
  performs sufficiently well for all the scenarios in this technical report.
  consider upgrading specifications to support profiles, levels, and possibly features available in HEVC. Features may include better support for screen content and computer-generated content, XR/AR type of services, as well as low and very low latency services.
New Codecs
  The framework and the initial results for new codecs demonstrate coding performance improvements over H.265/HEVC for some codecs of up to 50%, but not mature enough to support concrete recommendations on adding new codecs.
  The information in this TR, as well as any new developments in 3GPP with respect to codecs in latest specifications, could serve as a baseline for future work.
  However, no immediate need has been identified to initiate such follow-up work.
Scenario | AVC HEVC
S1 FullHD | 41.5
S3 Screen no RA | 52.4
S3 Screen RA | 44.2
S4 Sharing no RA | 46.7
S4 Sharing RA | 36.2
S5 Gaming no RA | 41.1
S5 Gaming RA | 31.0
Minimum | 31.0
Maximum | 52.4

## Slide 45: Ongoing and future work
HEVC Study Item in Rel-18
  MV-HEVC
  S-HEVC
  HEVC for still images
FGS Study Item
Expect in Rel-19
  work item in improvements to HEVC capabilities
  Study items on HEVC-based codecs to support 3D and XR such as multiview, depth, etc.
2022 Timeline Considerations have shifted due to renewed interest in HEVC

## Slide 46: XR and the Metaverse

## Slide 47: Technologies for the Metaverse: XR, AI, 5G
Boundless AR
5G network
Real time social interaction
Ultra low latency
  Eye tracking
  Spatial computing
Boundless VR
Contextual awareness and sensing
Notes: We'll now focus on how 5G is enabling cloud gaming, boundless VR, and boundless AR.
Each of these use cases have a split-processing architecture between the device and cloud, and they also require low-latency for a good user experience
Boundless XR, enables highly immersive experiences, wherever you are.
It combines the mobile XR experience, which has a simple ease of use with no setup with sleek design and leverages the mobile ecosystem, and fuses it with PC-tethered XR capability with extensive processing for high end graphics which is not limited by power and thermal constraints.
Boundless XR uses the concept of split-rendering over 5G, which brings the best of both worlds – photorealistic mobile XR in a sleek headset.
------------------------------------------------
https://www.gettyimages.com/detail/photo/engineer-using-augmented-reality-headset-to-see-royalty-free-image/926846200

## Slide 48: AR/VR/AI Work Flow
Simultaneous Complex Processing for Seamless AR/VR Experience
Eye tracking cameras
Sense the real world to track eye, position, orientation, and audio
1
See the world around you by collecting and monitoring visual images for depth info, object detection, face detection
2
Cameras with fisheye and telephoto lenses
Depth sensing camera (TOF, Structured Light, etc)
Optoelectronic night vision and thermal imaging sensors
Recognize and understand images for symbolic information
3
Sensors – accelerometer, gyroscope, ambient light, biometric, temperature, etc
Highly efficient and lower power CV processing
Collect virtual contents and data from cloud network
4
Multimode connectivity (4G, 5G, Wifi)
GPS for location information
Coding compression
Video transport
Overlay virtual objects/data with real or virtually created image scenes
5
Recommend personalized actions
6
Durable multimode display
Multiple audio microphones
Directional speakers

## Slide 49: A distributed compute architecture enables rich XR user experience
M2R2P = Edge processing + 5G round-trip time + Device processing
Game engine
Encoder
Application
Post processing (ATW, error concealment, …)
Decoder
Perception algorithms
Compressed rendered frames
6DoF HMD pose, controller, eye/hand tracking
Motion-to-render-to-photon latency
M2R2P
Notes: A distributed compute architecture enables rich XR user experience
So how does boundless XR work in reality? Boundless XR distributes the computation between edge cloud server and device to deliver truly immersive XR over 5G.
The XR headset provides power-efficient, latency-sensitive on-device rendering and tracking.
The Edge cloud server provides computationally intensive processing and graphics rendering.
5G provides the high bandwidth and low latency connectivity.

## Slide 50: Boundless XR over 5G
XR headset
Edge cloud server
Power-efficient, latency sensitive on-device rendering and tracking
Computationally intensive processing and graphics rendering
6-DoF head pose (500Hz, ~1Mbps)
Encoded data (90fps, 50-100Mbps)
Distribute computation between the edge cloud server and device
Leverage low-latency and high-capacity 5G
Notes: So how does boundless XR work in reality? Boundless XR distributes the computation between edge cloud server and device to deliver truly immersive XR over 5G.
The XR headset provides power-efficient, latency-sensitive on-device rendering and tracking.
The Edge cloud server provides computationally intensive processing and graphics rendering.
5G provides the high bandwidth and low latency connectivity.
Let’s look at an animation to explain the interaction between these components, and the processes involves in a boundless XR system [CLICK]
Additional Notes:
When the XR user moves his head, the on-device processing will determine the 6-DoF head pose and send it to the edge cloud through a low latency and high quality of service 5G link.
The edge cloud will use the head pose to partially render the next frame. The edge cloud capabilities will vary based on investment, but it should have racks of compute/CPU/GPUs to do photorealistic rendering. After quickly rendering the frame, the edge cloud will send the encoded data back to the XR headset.
The XR headset will decode the data, and based on the latest 6-DoF pose, which is being generated at a high frequency, the on-device processing will do any further rendering and adjustment to minimize motion-to-photon latency.
As you can imagine, making the XR experience truly immersive will require a system solution that guarantees low latency and high reliability. 5G is crucial for this. Depending on the distance from the edge cloud, the amount of edge cloud investment, the number of users, etc., the service may vary, but consumers can rest assured that the on-device XR capabilities will always be available.

## Slide 51
Achieved initial KPIs for at-scale 5G boundless VR deployments
Frame rate
2kx2k per eye at 90 frames per second
Throughput1
Reliable average downlink throughput of 50-100 Mbps
Reliable uplink throughput of ~1 Mbps, 500 Hz pose
Latency1
M2R2P latency < 70ms
5G RTT < 20ms
Immersive VR
Photorealistic visuals
6-DoF mobility
Robust and reliable
Notes: In our multi-user XR testbed in San Diego, we achieved initial KPIs for at-scale 5G boundless VR deployments.
Typical M2R2P latency numbers are < 70ms, and 5G RTT is < 20ms. Lower latency and higher throughput may be required depending on the use-cases.
Downlink average throughput is reliably kept at > 50Mbps.
By meeting these KPIs, we are able to deliver an immersive VR experience that reliably provides photorealistic visuals and 6 degrees-of-freedom mobility.

## Slide 52
KPIs for cloud-to-phone-to-glass deployments
Frame rate
2kx2k per eye at 90 frames per second
Throughput
Reliable average downlink throughput of 10-40 Mbps
Reliable uplink throughput of 3-20 Mbps
Latency
M2R2P latency of 50-100ms
5G+Wi-Fi RTT < 30ms1
Immersive AR
Photorealistic visuals
6-DoF mobility
Robust and reliable
Notes: In our XR testbed, we achieved the initial KPIs for at-scale 5G boundless AR deployments.
Typical M2R2P latency numbers are kept between 50-100ms, and 5G+Wi-Fi round-trip time is < 30ms. More immersive AR experiences for indoor applications require less than 20 ms round-trip time.
Downlink average throughput is reliably kept between 10 and 40 Mbps. Uplink is kept between 3 and 20 Mbps.
By meeting these KPIs, we are able to deliver an immersive AR experience that reliably provides photorealistic visuals and 6 degrees-of-freedom mobility.

## Slide 53: XR evolution – really?
Standalone VR and AR
Viewer VR & AR
cabled
Viewer VR & AR
wireless
1 – 4 years
Today
Wi-Fi
Standalone VR and AR
The “Next” Platform
Metaverse
6G research vector
Standalone AR/MR Glasses come with many challenges – see details
Notes: AR consumer: mostly viewers
AR enterprise: mix of viewers and standalone
VR consumer: mostly Standalone
VR enterprise: standalone
So when will we see 5G in Augmented Reality glasses of the future?
The ultimate destination is of course Standalone, e.g. all-in-one with 5G connectivity. With VR, we’ll see this next year. You heard it here first.
But with AR, there will be some form factor steps along the way, starting with AR glasses tethered to 5G Smartphones.
We will then see 2-piece designs, with a puck enabled with 5G wire-tethered to the glass.
This will evolve to removing the wireless, and using unlicensed mmWave in 60GHz (AD/AY) to remove the cables.
This is the exact same technology we’re demonstrating with Zerolight from PC to VR.

## Slide 54: Some Technology Trends and Announcements
Glasses-free 3D Displays
Lenticúlar Displays
Eyetracking
Announced at CES 2023
Not released and may never be
Simple Smart
Glasses
ptMR HMD
Primarily for gaming and enterprise
Adds AR/MR w/ camera see-through
Less is more
Meta’s smart glasses can take calls, play music, and livestream from your face
No visual display
https://www.leiainc.com/lume-pad-2
https://lookingglassfactory.com/

## Slide 55: Selected 3GPP SA4 Reports and Technical Specifications
Green completed, yellow ongoing
Specification | Title
TS 26.118 | Virtual Reality (VR) profiles for streaming applications
TS 26.119 | Media Capabilities for Augmented Reality
TS 26.250 | Codec for immersive voice and audio services - General overview
TS 26.264 | IMS-based AR Real-Time Communication
TS 26.565 | Split Rendering Media Service Enabler
TR 26.806 | Study on Tethering AR Glasses – Architectures, QoS and Media Aspects
TR 26.812 | QoE metrics for AR/MR services
TR 26.813 | Study of Avatars in Real-Time Communication Services
TR 26.918 | Virtual Reality (VR) media services over 3GPP
TR 26.926 | Traffic Models and Quality Evaluation Methods for Media and XR Services in 5G Systems
TR 26.928 | Extended Reality (XR) in 5G (completed in 2020)
TR 26.929 | QoE parameters and metrics relevant to the Virtual Reality (VR) user experience
TR 26.930 | Study on the enhancement for Immersive Real-Time communication for WebRTC
TR 26.998 | Support of 5G glass-type Augmented Reality / Mixed Reality (AR/MR) devices

## Slide 56: Rel-18 Media Capabilities for XR/AR
Defining baseline requirements for an AR lightweight and XR device
Hinge
SoC Media
Connectivity
Eye Tracking + Camera/Sensor Aggregator
Requirements include
OpenXR Core APIs
rendering capabilities
capturing capabilities
audio and video codecs
scene description
Wire formats for metadata
Profiles for split rendering and stand-alone rendering

## Slide 57: Standardizing Split XR in SA4 – Media Service Enabler
RTC Profile
RTP Profile
Signaling Profile
5G Integration
Edge Functionality
QoS Profile
QoE and Consumption
Data Collection
Provisioning
Guidelines: Post-processing, Pose correction,
XR Runtime
Split Rendering MSE
(TS 26.565)
Media Format Profiles
AR Profile
VR Profile
Gaming Profile
Scene Description Profile
Uplink Profile
5G RTC Enabler
26.113
Media Format Enabler
(TS 26.119)
5G Media Control Enabler
(26.506/
26.501)
Split Rendering API

## Slide 58: AR Call
Extend existing IMS and WebRTC-based telephony services
Multi-party calls and conferencing with AR
Users join with realistic avatars and contribute 2D/3D content
Create shared spaces where call participants can interact

## Slide 59: High Level Procedure
Scene of shared space
Scene of shared space
Add nodes to scene
Add nodes to scene
Send scene updates
Send scene updates
Send scene updates
Send scene updates
Pose and animation updates
Pose and animation updates
Update
Loop

## Slide 60: Avatar Representation
In shared spaces, avatars are an important component
Avatars are 3D representations of the user and allow the user to interact with the scene
Avatars may be purely synthetic or maybe an accurate representation of the user
The avatar needs to be real-time captured or retargeted to reflect the user’s actual motion/body pose/facial expression …
Avatar Representation Formats are proprietary, but may be subject of standardization – 3GPP collaborates

## Slide 61: Avatar Reconstruction Pipeline - Example
Avatar input format identified through a URN
Pipeline performs reconstruction into a mesh, e.g. by running an inference model on the input components
Interactivity metadata is mapped into the reconstructed Avatar mesh
Texture
Deformation maps
HEVC Decoder
HEVC Decoder
Vertex Buffer
Presentation Engine
Avatar Reconstruction
Parametrization Data
Static Metadata
Base Model
Texture Buffer
Skinning/Joint data Buffer
Interactivity Metadata Buffer
Avatar Reconstruction

## Slide 62: Beyond Rel-19

## Slide 63: WG Input to Rel-19 Workshop - 2
SA/SA2/RAN2 to let SA4 do stage-3 on media related topics. Early indication of potential impact to SA4 is nice-to-have.
SA4 is currently focused on Rel-18 Work and Rel-17 maintenance
SA4 hasn’t started Rel-19 planning. Several topics mentioned but no detailed discussions and conclusions. Example of potential larger work topics for SA4:
SA4#124 agreed to start Rel-19 discussions from December 2023:
  Build on leftovers from Rel-18, studies from Rel-18, as well as work topics related to RAN and SA2 work
  Identify substantial new work topics for Rel-19.
  Work with requirements and inputs from the industry: 5G-MAG, Metaverse Standards Forum, etc.
New Video Codecs
Avatars
XR Extensions
5GMS and MBS Extensions
AI/ML for Media

## Slide 64: Summary & Next Steps
Join the community of open standards and developments
5G is a platform for Broadcasters and Content Providers with features including 5G broadcast, Public Warning and many others
3GPP Standards are global and address billions of devices – from smart phones to many more verticals (automotive, IOT, etc.)
We need to integrate new media topics: Content Steering, CMCD/CMSD, Media over QUIC, etc.