## Slide 1: 5G Media Streaming Advances: towards a universal Media Distribution Platform
June 12, 2023
Media Web Symposium 2023
@qualcomm_tech
Dr. Thomas Stockhammer
Senior Director Technical Standards
Qualcomm Technologies

## Slide 2
Presenter
Dr. Thomas Stockhammer
Senior Director, Technical Standards
Qualcomm Europe, Inc., IEEE Fellow
Leading and driving among others
DVB: 5G TF, DVB-I
MPEG: MPEG-I, CMAF and DASH
3GPP: XR over 5G, 5G Video, 5GMS
DASH-IF: Interop WG, Test
ETSI & 5G-MAG: 5G Broadcast and 5GMS
CTA WAVE: CMAF Device PB, Test
Metaverse Standards Forum Lead
Today’s agenda
# Motivation
# 5G Media Streaming Idea
# Rel-17 Features
# In the cooking in Rel-18
# Beyond Rel-18
# Discussion

## Slide 3: Trends & News
Collected from Sandvine report, Bitmovin Developer report and Will Law from Akamai
Traffic
Mobile
Sports
Codecs
Monetization

## Slide 4: Rel-16 5G Media Streaming – The Idea
Approach:
  Framework aligned with today‘s OTTmedia distribution practices
  Supplementing MNO and third-party media services to easily access 5GS and 5GMS features
  Concrete instantiation for one or a small subset of recommended technologies (e.g. codecs, formats, etc.)

## Slide 5
Notes: 5G-MAG was instrumental to deliver an open-source platform for 5G Broadcast.
For target 2023, we in Qualcomm support the next steps in 5G-MAG Reference Tools to integrate 5G Broadcast with 5G Media Streaming.
As our first contribution to this exiting new project, we implemented basic 5G Media Streaming UE functions, the Media Session Handler and the Media Player, and connected to BBC‘s 5GMS network.
I hand over to my colleagues Weiyu and Shiling in China to explain more details..

## Slide 6
5G Content Provider UK
5G UE in China
5GMS-aware Application
Media Session Handler
Media Player
5GMS AS
5GMS AF
Select BBC
Access: http://5gms.bbc.uk/3gpp-m5/v2/service-access-information/d54a1fcc-d411-4e32-807b-2c60dbaeaf5f
JSON Response
{
"provisioningSessionId": "d54a1fcc-d411-4e32-807b-2c60dbaeaf5f",
"provisioningSessionType": "DOWNLINK",
"streamingAccess": {
"mediaPlayerEntry": "http://5gms.bbc.uk/m4d/provisioning-session-d54a1fcc-d411-4e32-807b-
2c60dbaeaf5f/Christmas-Greetings-to-5G-MAG.mpd"
}
}
Play BBC
GET X-MAS MPD
MPD Response
Notes: Hello, my name is Weiyu from Qualcomm China. I explain you the first handshake we did just a few days ago with the BBC 5GMS Network components you saw earlier.
We implemented initial functions of Media Session Handler and Media Player.
Here is our test app. Let us check the BBC Christmas Greetings.
[Click]
We send a 5GMS RESTful API call to the AF and get a 5G conforming JSON response.
The Media Session Handler instructs the media player to play the video and the Media Player gets the MPD from the AS.
[Click]

## Slide 7
5G Content Provider UK
5G UE in China
5GMS-aware Application
Media Session Handler
Media Player
5GMS AS
5GMS AF
MPD Response
<?xml version="1.0" ?>
<!-- MPD file BBC Christmas Greetings -->
<MPD xmlns="urn:mpeg:dash:schema:mpd:2011" minBufferTime="PT2S" type="static" mediaPresentationDuration="PT0H0M30S" maxSegmentDuration="PT0H0M2S" profiles="urn:mpeg:dash:profile:isoff-live:2011 ">
<Period duration="PT0H0M30.000S">
<AdaptationSet segmentAlignment="true" maxWidth="1920" maxHeight="1080" maxFrameRate="25" par="16:9" lang="und" startWithSAP="1" contentType="video" containerProfiles="'cmf2', 'cfhd'">
<SegmentTemplate media="1/$Time$.m4s" initialization="1/init.mp4" timescale="12800">
<SegmentTimeline>
<S t="0" d="25600" r="14"/>
</SegmentTimeline>
</SegmentTemplate>
<Representation id="1" mimeType="video/mp4" codecs="avc1.640028" width="1920" height="1080" frameRate="25" sar="1:1" bandwidth="5100000">
</Representation>
</AdaptationSet>
</Period>
</MPD>
GET X-MAS Segments
Segment Response
Monitor and Support
Notes: So let‘s unpack our Christmas present.
[Click]
We got a voucher for some Segments and we request those while 5GMS Control functions monitor the session.
[wait until the end of Richard‘s message]
Thank you Richard
[END]

## Slide 8: 5G Media Streaming Features for Rel-16
Only downlink features
Content Hosting
Network Assistance
Dynamic Policies
Consumption Reporting
Metrics Reporting

## Slide 9: Timelines for Rel-17 and Rel-18
Shifted by three months

## Slide 10: 3GPP Specifications for Edge Enablers
SA6:
TS 23.558: Architecture for enabling Edge Applications
SA2:
TS 23.501: Policy and charging control framework for the 5G System (5GS); Stage 2
TS 23.548: 5G System Enhancements for Edge Computing; Stage 2
SA4:
TS 26.501: 5G Media Streaming (5GMS): General description and architecture
TS 26.512: 5G Media Streaming (5GMS): Protocols
CT1:
TS 24.558: Enabling Edge Applications: Protocol specification
CT3:
TS 29.558: Enabling Edge Applications; Application Programming Interface (API) specification; Stage 3

## Slide 11: Rel-17 5GMS and Edge
Building on EDGEAPP and other 3GPP work on edge
Application Provider Provisioning
  Define application needs for edge resource and QoS requirement templates
Network Assistance
  5GMS AF works with the MSH (in UE) to translate templates into actual allocations for a media session
  UE discovers Edge Server that meets the requirements and can server the application
Core Application: XR Split Rendering
Enabling MM services with stringent requirements
FS_EMSA
5GMS_EDGE
5GMS_EDGE_3
3GPP Release 17
EDGE_ENH?
3GPP Release 18+

## Slide 12: Rel-17 EVEX – Event Exposure
UEs can log and report a variety of useful information (e.g. QoE metrics, usage measurements, dynamic QoS/Charging policy invocations) to a Data Collection AF, for subsequent offering via Event Exposure services to external entities for device, network and service performance monitoring and data analytics
5G Core
NR/
gNB
Data Collection
Application Function
Application
Service
Provider
Media/Service
Content
Network &
Data Analytics
Function
UE Data Measurement / Reporting
Event Exposure
Service
Data Collection & Reporting Configuration
Provisioning Info
Media/Service
Content
Notes: So how does all this work in reality?
The edge cloud will augment on-device processing for boundless photorealistic XR
Looking at the animation [CLICK]
When the XR user moves his head, the on-device processing will determine the 6-DoF head pose and send it to the edge cloud through a low latency and high quality of service 5G link.
The edge cloud will use the head pose to partially render the next frame. The edge cloud capabilities will vary based on investment, but it should have racks of compute/CPU/GPUs to do photorealistic rendering. After quickly rendering the frame, the edge cloud will send the encoded data back to the XR headset.
The XR headset will decode the data, and based on the latest 6-DoF pose, which is being generated at a high frequency, the on-device processing will do any further rendering and adjustment to minimize motion-to-photon latency.
As you can imagine, making the XR experience truly immersive will require a system solution that guarantees low latency and high reliability. 5G is crucial for this. Depending on the distance from the edge cloud, the amount of edge cloud investment, the number of users, etc., the service may vary, but consumers can rest assured that the on-device XR capabilities will always be available.

## Slide 13: 5G Media Streaming and EVEX
Simplified version of TS 26.512 V17.1.0 figure 4.7.1-1

## Slide 14: 3GPP Specifications for Data Analysis and EVEX
SA2:
TS 23.288: Architecture enhancements for 5G System (5GS) to support network data analytics services
SA4:
TS 26.531: Data Collection and Reporting; General Description and Architecture
TS 26.532: Data Collection and Reporting; Protocols and Formats
TS 26.501: 5G Media Streaming (5GMS): General description and architecture
TS 26.512: 5G Media Streaming (5GMS): Protocols
CT3:
TS 29.517: 5G System; Application Function Event Exposure Service; Stage 3
TS 29.520: 5G System; Network Data Analytics Services; Stage 3
TS 29.522: 5G System: Network Exposure Function Northbound APIs; Stage 3
TS 29.591: 5G System; Network Exposure Function Southbound Services; Stage 3

## Slide 15: 5GMS via 5G Broadcast and Hybrid Unicast Broadcast
Content Provider may leverage 5G Unicast systems, 5G Broadcast systems, and 5G devices to build efficient and innovative applications
Supported by well defined network and client-side APIs
Examples:
  Hybrid Services
  Universal Coverage
  Broadcast on Demand
Part of Rel-17 5G Media Streaming
Part of the ETSI TS 103 720 v1.2.1
Architectures, Collaboration Models and Use Cases
5G Broadcast Operator
Content Provider
5G MNO

## Slide 17: 5G defines two modes of broadcast communication
Addressing diverse ecosystem, deployment, and use case requirements
5G broadcast
5MBS: Mixed-mode multicast
Single Frequency Network (SFN) for downlink broadcast only
Dynamic switching between broadcast and unicast, e.g., SC-PTM1
Focus of this presentation
Operator spectrum (IMT)
Integration with unicast network
Efficient delivery of multicast/broadcast traffic (vs unicast)
Reuse of cellular infrastructure (low power).
Broadcast spectrum (e.g. UHF)
No unicast. Downlink – only traffic.
Delivery of linear content (e.g. TV) or IP file delivery
Dedicated broadcast infrastructure (can be high power)

## Slide 18: Timelines for Rel-17 and Rel-18
Shifted by three months

## Slide 19: Rel-18 5GMS feature overview
Extensive studies documented in TR26.804 result in the following updates
Consistent support for uplink streaming
End-to-end low latency live streaming with dynamic policies
5GMS over MBS and 5GMS hybrid unicast/MBS services.
Based on development in CTA WAVE in context of DASH/HLS interop specification in CTA-5005, it was identified that the same media service may be available in multiple formats, and 5GMS media is expected to offer the same service with different entry points in order for the device to select the service based on its capabilities, for example using a DASH player, or and HLS player, or using a progressive download system.
The 5G System offers different solutions for traffic identification and traffic detection. Traffic identification is essential so that the 5G System can detect application flows to which, for instance, an appropriate Policy and Charging Rule (PCC) is applied. 5GMS is extended to support the configuration of ToS values for the identification of traffic associated with a Dynamic Policy. and study use-cases with IPsec and the usage of the security parameter index for traffic identification.
The Quick UDP Internet Connection (QUIC) [43] and HTTP/3 protocols are among the most recent developments in the IETF, with the goal of combining flexibility, extensibility, and performance to web applications. The 5GMS specifications are updated to allow the use of HTTP/3 at relevant reference points in the 5GMS architecture.
Background data transfer (BDT)
Specification of the usage of Oauth 2.0 for 5GMS protocols based on the conclusions to address use-cases, when a UE hosts multiple 5GMS-Aware Applications from different 5GMS Application Providers.
Specifications for the 3GPP Service Handler and URL including the necessary functions on UE and device to support automatic launch of 5G System services in the context of 5G Media Streaming. It was identified that it is essential to provide a URL form for media services in order to automatically launch client and network functions without disrupting existing app workflows.
Specification of a RESTful API at reference point M3, for the configuration of 5GMS AS instances by 5GMS AF. M3 was undefined until now, but based on deployment experience it was identified that it is necessary to define this reference point more details.
Specification of data types for data reporting of ANBR-based Network Assistance invocations and specification of data types for exposure of events relating to invocation of AF-based and ANBR-based Network Assistance.
Enhancements based on feedback from 5G-MAG Reference tool developments. The support of 5G-MAG reference tools created essential inputs to the spec development and continuous exchange will result in additional updates.
this functionality is needed for media production services, but also for contributing user generated media to operator and third-party services. Different collaboration scenarios between the MNO and the service provider are addressed in an updated specification – bringing uplink streaming on par with downlink streaming.
is of crucial support to meet the TV industry needs in order to bring 5G on par with other distribution means. Live TV services are characterized by at least the following aspects: (1) scalability (in terms of concurrent users), (2) consistent quality, (3) high bandwidth requirements, (4) target latency constraints, and advanced TV Experiences. Primarily, updated DASH tools, QoE monitoring and QoS support for low-latency in 5G media streaming are specified in order to meet the requirements defined in TR 26.804.
This functionality is expected to allow scaling media services using multicast and point-to-multipoint distribution within the operators network.
Multiple Service Entry Points
Traffic Identification
QUIC and HTTP/3
enables mobile network operators to incentivize the offloading of traffic into off-peak hours with the aim of reducing network congestion during peak hours. Applications may register their interest in receiving content using BDT. The 5GMS specifications will be updated with the necessary parameter extensions to the M1, M5, and M6 reference points to provide access to BDT.
Oauth 2.0
3GPP Service URL Handling
Application Server Configuration
EVEX data types for ANBR-based Network Assistance
Support for 5G-MAG Reference Tools

## Slide 20: Multicast–Broadcast Services system architecture
Based on TS 23.247 V17.2.0 figure 5.1-1

## Slide 21: Multicast–Broadcast Services system architecture
Based on TS 23.247 V17.2.0 figure 5.1-2

## Slide 22: MBS User Service Architecture
User Service Announcement
  Aligned with MBMS User Service principles
  Simplified
  Modernized protocols
Object Distribution
  Single file delivery.
  Package Delivery
  Object Carouselling
  Real-Time Object Streaming DASH/HLS/CMAF
Packet Distribution
  Forward-only (tunnel)
  Proxy mode (UDP payload)
Associated Services
See TS 26.502 Figure 4.3.1-1

## Slide 23: 5GMS via MBS
Abstract the distribution complexity for third party service provider
Different collaboration models
Unicast/Multicast combinations
Stage-3 still to be developed
See TS 26.501, Figure 4.9.1-1

## Slide 24: Launching a dedicated 5G System function on device
Unclear how this can happen consistently

## Slide 25: Service URL Handling
Extend the baseline 5G Media Streaming architecture to add a 3GPP Service and URL Handler in the UE and the network according to figure 5.13.3-1.
Address provisioning, message exchange and call flows in order to support different use cases, namely the case for which the URL is resolved in the network, the URL is resolved in the UE, and the case for which the URL is resolved in a combination of network and UE as discussed in clause 5.13.3.
Specify a concrete URL format for 3GPP services and reserve a URL prefix (e.g. services.3gpp.org) for 3GPP Services as part of 3GPP specifications, and ensure that this can be used in the context of 3GPP-based services, namely:
  Verify ownership of the domain through one of the Android website association methods.
  Create a suitable website redirection mechanism in case the application is not available on the device.
Specify 3GPP Service URL instantiations with parameters suitable for launching at least the Media Session Handler for 5G Media Streaming, MBMS Client (including Receive-Only Mode services) and MBS Client.
Provide the ability for a 5GMS-Aware application to create a Service URL in order to bootstrap 5G Media Streaming.
Investigate and study the application of 3GPP services and URL handling beyond 5G Media Streaming.

## Slide 26: Specific case: MBMS-ROM Service + CMAS-based launch of service
Scenario

## Slide 27: Tools in action …
5G-MAG @ IBC 2022
Nakolos (ORS/Bitstem)
BBC
Find information at developer.5g-mag.com

## Slide 28: Rel-19 Timeline
TSG#101
Note: All starting dates are indicative
TSG#102
TSG#103
TSG#104
TSG#105
TSG#106
TSG#107
TSG#108
TSG#109
TSG#110
TSG#111
TSG#112
TSG#99
RAN4
content def.
RAN Content def.
2024
2025
Sep.
Mar.
Mar.
Mar.
Jun.
Jun.
Jun.
Sep.
Sep.
Sep.
Dec.
Dec.
Dec.
2026
RAN Rel-19 workshop
RAN4_Perf
Stage 3 (CT & SA)
RAN1
Stage 2 (SA2, SA6,…)
RAN Completion (RAN2/3/4core)
ASN.1 & Open APIs
St.2 Content approval
SA Rel-19
Workshop
TSG#100
June
2023
Now
100%
SA1 Stage 1 80%

## Slide 29: WG Input to Rel-19 Workshop - 2
SA/SA2/RAN2 to let SA4 do stage-3 on media related topics. Early indication of potential impact to SA4 is nice-to-have.
SA4 is currently focused on Rel-18 Work and Rel-17 maintenance
SA4 hasn’t started Rel-19 planning. Several topics mentioned but no detailed discussions and conclusions. Example of potential larger work topics for SA4:
SA4#124 agreed to start Rel-19 discussions from December 2023:
  Build on leftovers from Rel-18, studies from Rel-18, as well as work topics related to RAN and SA2 work
  Identify substantial new work topics for Rel-19.
  Work with requirements and inputs from the industry: 5G-MAG, Metaverse Standards Forum, etc.
New Video Codecs
Avatars
XR Extensions
5GMS and MBS Extensions
AI/ML for Media

## Slide 30: Summary & Next Steps
Join the community of open standards and developments
5G is a platform for Broadcasters and Content Providers with features including 5G broadcast, Public Warning and many others
3GPP Standards are global and address billions of devices – from smart phones to many more verticals (automotive, IOT, etc.)
We need to integrate new media topics: Content Steering, CMCD/CMSD, Media over QUIC, etc.